## Slide 1: Proposal on AI/ML for NR air interface in Rel-19

## Slide 2: General consideration for Rel-19
Rel-18 AI/ML study outcome
  In Rel-18, AI/ML for air-interface has been studied including the following 6 sub-use cases
    CSI feedback enhancement
      CSI compression based on two-sided model
      CSI predication based on UE-sided model
    Beam management
      Spatial domain beam prediction based on one-sided model
      Temporal domain beam prediction based on one-sided model
    Positioning accuracy enhancement
      Direct positioning based on one-sided model
      AI/ML assisted positioning based on one-sided model
  The conclusion from RAN1 is that,
    For use cases for BM and positioning, AI/ML model based operations are expected to provide potential gain compared to existing scheme in terms of performance and/or complexity/overhead.
    For CSI use cases, there is no consensus on recommendation of CSI compression and CSI prediction for normative work due to lack of sufficient performance gain and/or required complexity/overhead.
The work scope should be selected based on the following aspects
  Easier adaptation to vendors (e.g. keeping vendor-specific proprietary information)
  Expected performance gain and/or complexity/overhead
  Expected amount of specification impact

## Slide 3: General consideration for Rel-19
Direction related to AI/ML framework
  In Rel-18 AI/ML SI, AI/ML framework including functionality/model-based LCM has been studied.
  During the study, there were some controversial parts on their necessity/feasibility, i.e.
    Model/dataset transfer
    Model identification and model-based LCM
  On the other hand, there were some common parts on their necessity/feasibility, i.e.
    Signaling enhancement for data collection (e.g. L1 or L2 signaling)
    Enhancements for performance monitoring
    Inference-related feature enhancement (e.g. enhanced beam reporting for BM)
    Enhancements for dynamic reporting of applicable functionality/model
    Fallback mechanism
Proposal
  Support AI/ML WI in Rel-19 with selected use cases. For each use case, focus on the following enhancement areas.
    Signaling enhancement for data collection (e.g. L1 or L2 signaling)
    Enhancements for dynamic reporting of applicable functionality/model
    Inference-related feature enhancement
    Enhancements for performance monitoring
    Fallback mechanism

## Slide 4: CSI feedback enhancement
CSI compression
  In RAN1#115, following high-level summary and conclusion regarding CSI compression were agreed [1].
Proposal
  CSI compression may be further studied in Rel-19, and if studied, at least the followings are to be considered
    Methods to further improve the performance gain over legacy CSI feedback, and/or reduce the AI/ML computational complexity
    Further evaluation aspects that are not fully investigated in Rel-18 (e.g., CQI/RI calculation options, training collaborations options)
[1] RAN1#115 chairman’s note
Agreement
Capture the following summary in Section 8 of the 3GPP TR 38.843 on AI/ML based CSI compression sub-use case.
-------------------------------------------- Start of Text Proposal --------------------------------------------------------
The performance benefit and potential specification impact were studied for AI/ML based CSI compression sub use case.
Evaluation has been performed to assess AI/ML based CSI compression from various aspects, including performance gain over non-AI/ML benchmark, model input/output type, CSI feedback quantization methods, ground-truth CSI format, monitoring, generalization, training collaboration types, etc. Some aspects are studied but not fully investigated, including the options of CQI/RI calculation, the options of rank>1 solution.
Performance gain over baseline [and computation complexity in FLOPs] are summarized in clause 6.2.2.8 of TR 38.843.
Potential specification impact on NW side/UE side data collection, dataset delivery, quantization alignment between CSI generation part at the UE and CSI reconstruction part at the NW, CSI report configuration, CSI report format, pairing information/procedure and monitoring approach were investigated but not all aspects were identified.
The pros and cons are analysed for each training collaboration types, and each training collaboration type has its own benefits and limitations in different aspects. The study has investigated the feasibility of the studied training collaboration types and necessity of corresponding potential RAN1 specification impact. However, not all aspects have been concluded.
Both NW side and UE side performance monitoring were studied, some but not all aspects were concluded.
-------------------------------------------- End of Text Proposal --------------------------------------------------------
Agreement
Capture the following as a conclusion in section 8 of the TR
From RAN1 perspective, there is no consensus on the recommendation of CSI compression for normative work.
At least the following aspects are the reasons for the lack of RAN1 consensus on the recommendation of CSI compression for normative work.
  Trade-off between performance and complexity/overhead
  Issues related to inter-vendor training collaboration
Other aspects that require further study/conclusion are captured in the summary

## Slide 5: CSI feedback enhancement
CSI prediction
  In RAN1#115, following high-level summary and conclusion regarding CSI prediction were agreed [1].
Proposal
  CSI prediction based on UE-sided model may be further studied in Rel-19, and if studied, at least further performance analysis should be performed, e.g.
    Further performance analysis based on larger number of simulation results
      Performance comparison with non-AI based CSI prediction
      Spatial consistency needs to be taken into account
[1] RAN1#115 chairman’s note
Agreement
Capture the following text for CSI prediction summary agreed in RAN1 115, for section 8 of TR38.843.
-------------------------------------------- Start of Text Proposal --------------------------------------------------------
The performance and potential specification impact were studied for AI/ML based UE side CSI prediction sub use case.
Evaluation has been performed to assess AI/ML based CSI prediction from various aspects, including performance compared to baseline, model input/output type, generalization over UE speed, etc. Some aspects are studied but lack observations, including scalability over various configurations and generalization over other scenarios and approach of fine tuning. Performance monitoring accuracy is not evaluated.
Performance compared with baseline is summarized in clause 6.2.2.8 of TR 38.843.
Potential specification impact on data collection and performance monitoring are discussed in section 7.2.2 of TR 38.843.
  Limited specification aspects were considered.
-------------------------------------------- End of Text Proposal ----------------------------------------------
Agreement
Capture the following conclusion in section 8 of the TR 38.843
From RAN1 perspective, there is no consensus on the recommendation of CSI prediction for normative work.
The reason for the lack of RAN1 consensus on the recommendation of CSI prediction for normative work is due to
  Lack of results on the performance gain over non-AI/ML based approach and associated complexity
Other aspects that require further study/conclusion are captured in the summary.

## Slide 6: Beam management and Positioning accuracy enhancement
Motivation
  In RAN1#115, followings were agreed related to the recommendation for normative work of AI/ML based BM and positioning [1].
Proposal
  Adopt RAN1’s recommendation for AI/ML based beam management and positioning accuracy enhancement.
Agreement
Confirm the following working assumption (with modification in red) agreed in RAN1#114bis
Working Assumption
For AI-based beam management, from RAN1 perspective, at least the following are recommended for normative work
Both BM-Case1 and BM-Case2
  BM-Case1: Spatial-domain DL Tx beam prediction for Set A of beams based on measurement results of Set B of beams
  BM-Case2: Temporal DL Tx beam prediction for Set A of beams based on the historic measurement results of Set B of beams
DL Tx beam prediction for both UE-sided model and NW-sided model
Necessary signaling/mechanism(s) to facilitate data collection, model inference, and performance monitoring for both UE-sided model and NW-sided model
Signaling/mechanism(s) to facilitate necessary LCM operations via 3GPP signaling for UE-sided model
Agreement
It is recommended to specify necessary measurement, signaling and procedure to facilitate training, inference, monitoring and/or other LCM operations for both direct AI/ML positioning and AI/ML assisted positioning
specify necessary signaling of data collection; investigate the necessity of other information for supporting data collection, and if needed, specify during normative work
investigate on the necessity and signaling details of measurement enhancements, and if needed, specify during normative work
investigate on the necessity and signaling details of monitoring method(s), and if needed, specify during normative work
[1] RAN1#115 chairman’s note

## Slide 7: Proposed objective for Rel-19
Support the following use cases to facilitate AI/ML operation for air-interface
  DL Tx beam prediction for both BM-case 1 and 2.
  Direct AI/ML positioning and AI/ML assisted positioning.
Continue studying the following uses cases.
  CSI compression based on two-sided model
  CSI prediction based on UE-sided model
For the supported use cases, focus on the following enhancement areas.
  Signaling enhancement for data collection (e.g. L1 or L2 signaling)
  Enhancements for dynamic reporting of applicable functionality/model
  Inference-related feature enhancement
  Enhancements for performance monitoring
  Fallback mechanism