## Slide 1: Proposal on Duplex Evolution in Rel-19
3GPP TSG RAN Meeting #102
Edinburgh, Scotland, December 11-15, 2023
Agenda Item: 9.1.1.3
RP-233153

## Slide 2: Background
In RAN#101 meeting, there was a discussion about RAN Rel-19 package. In the summary of RAN Rel-19 package: RAN1/2/3-led [1], the potential objectives for evolution of duplex operation WI is included as below:
Potential objectives:
  For subband non-overlapping full duplex (SBFD) operation at gNB side within a TDD carrier
    [Semi-static/dynamic] indication of time location of SBFD subbands to UEs [in RRC_CONNECTED mode]
    Semi-static indication of frequency domain location of SBFD subbands to UEs [in RRC_CONNECTED mode]
    UE transmission and reception behavior and procedures in SBFD symbols and/or non-SBFD symbols
    Note: followings are assumed based on TR 38.858
      SBFD operation Option 4
      Coexistence between legacy UEs and SBFD aware UEs in the cell operating SBFD at gNB side
      SBFD scheme within a single configured DL and UL BWP pair with aligned center frequencies
      Up to one UL subband for SBFD operation in an SBFD symbol (excluding legacy UL symbol/slot) within a TDD carrier
    At least adjacent channel coexistence between two operators should be considered as a minimum.
  Specify enhancements for CLI handling:
    Support both the gNB-to-gNB co-channel CLI handling scheme(s) and UE-to-UE co-channel CLI handling scheme(s) (the detailed schemes are to be down-selected from those in TR38.858)
    The SBFD operation drives the CLI enhancements, which are expected to be applicable to the dynamic/flexible TDD operation but without dedicated optimization
  RF requirements for SBFD operation at gNB
Notes: 현재 PSI 정보를 기반으로는 discard 만 수행할 것이다. 하지만 이걸로 충분하지 않고 PSI 기반의 reliability 및 prioritization을 해야 한다.
한줄로 표현될 수 있도록 하자. 기고의 observation 같이.

## Slide 3: Background
Further discussions are needed for followings:
  Dynamic indication of time location of SBFD subbands
  Random access for SBFD aware UE in CONNECTED mode only or UE in RRC_IDLE/INACTIVE/CONNECTED mode
  Details of UE transmission and reception behavior and procedures in SBFD symbols and/or non-SBFD symbols
  Inter-gNB CLI handling schemes and inter-UE handling schemes
In this contribution, we provide our view about the scope.
Notes: 현재 PSI 정보를 기반으로는 discard 만 수행할 것이다. 하지만 이걸로 충분하지 않고 PSI 기반의 reliability 및 prioritization을 해야 한다.
한줄로 표현될 수 있도록 하자. 기고의 observation 같이.

## Slide 4: Dynamic indication of time location of SBFD subbands
Discussion
  For SBFD operation, bandwidth in SBFD symbol/slot is divided into DL subband and UL subband for simultaneous transmission and reception at gNB.
  Comparing between semi-static SBFD operation and static TDD, semi-static SBFD operation provides a benefit of UL performance enhancement, where the gain comes from assigning more UL resource. But, DL performance of semi-static SBFD operation is degraded due to the reduced DL resource.
  If switching SBFD symbol/slot into DL-only symbol/slot is allowed, the DL performance of SBFD can be compensated [4]. Furthermore, if switching SBFD symbol/slot into UL-only symbol/slot is allowed, further enhancement of UL performance can be achieved.
Proposal:
  Specify Indication of time and frequency domain locations of SBFD subbands to UEs
    Support semi-static indication of time location and frequency location of SBFD subbands
    Support dynamic indication of time location (e.g., slot(s) for SBFD can fall back to slot(s) for TDD DL only or flexible.)
Notes: 현재 PSI 정보를 기반으로는 discard 만 수행할 것이다. 하지만 이걸로 충분하지 않고 PSI 기반의 reliability 및 prioritization을 해야 한다.
한줄로 표현될 수 있도록 하자. 기고의 observation 같이.

## Slide 5: Random Access for SBFD aware UE
Discussion
  Improving coverage of PRACH and msg3 is desirable. SBFD aware UEs in RRC_IDLE/INACTIVE/CONNECTED mode can use consecutive UL slot in SBFD slot. Random access in SBFD symbols may potentially “reduce the random access latency, reduce the PRACH collision probability and/or improve the coverage of PRACH and msg3.” [2]
  In SI phase, these aspects were not fully evaluated in RAN1 and the specification impact was not studied. Therefore, further study for random access in SBFD symbol for SBFD aware UEs in RRC_IDLE/INACTIVE/CONNECTED mode seems necessary to support random access in SBFD symbol. Then, random access in SBFD symbol will be specified.
Proposal
  Study, and if justified, specify random access in SBFD symbol for SBFD aware UEs in RRC_IDLE/INACTIVE/CONNECTED mode
Notes: 현재 PSI 정보를 기반으로는 discard 만 수행할 것이다. 하지만 이걸로 충분하지 않고 PSI 기반의 reliability 및 prioritization을 해야 한다.
한줄로 표현될 수 있도록 하자. 기고의 observation 같이.

## Slide 6: Details of UE Tx and Rx behavior and procedures
Discussion
  Scope of UE transmission and reception behavior and procedures seems broad.
  Details need to be described.
Proposal:
  Specify transmission, reception and measurement behavior and procedure for SBFD operation, including
    Resource allocation/CSI reporting with non-continuous frequency domain grid, different BW size across SBFD and non-SBFD symbols
    Multiple configuration for supporting operation on SBFD symbols and non-SBFD symbols: Power control, Frequency Hopping, CSI reporting
    UE behavior according to Non-SBFD symbol and SBFD symbol: DG-PUSCH, TBoMS, CG-PUSCH, PDSCH
    MIMO configuration, Beam correspondence
Notes: 현재 PSI 정보를 기반으로는 discard 만 수행할 것이다. 하지만 이걸로 충분하지 않고 PSI 기반의 reliability 및 prioritization을 해야 한다.
한줄로 표현될 수 있도록 하자. 기고의 observation 같이.

## Slide 7: Co-channel CLI handling schemes
Discussion
  For dynamic/flexible TDD and co-channel co-existence case (i.e., the cells use legacy TDD while the others use SBFD operation), gNB-to-gNB co-channel CLI handling is required.
    Periodic NZP CSI-RS/SSB can be used for gNB-to-gNB co-channel CLI measurement and/or channel measurement.
    The knowledge among gNBs of semi-static SBFD time and frequency configuration can be used to determine whether CLI is existed in the resource.
    gNB can exchange beam related information among gNB(s) such as DL beam indication, preferred/non-preferred beam indication.
  For SBFD and dynamic/flexible TDD, UE-to-UE co-channel CLI handling is required.
    L1/L2 based CLI measurement and reporting provide benefits for inter-UE CLI handling.
      It can be optimized for short-term interference measurement and low latency.
      It can facilitate gNB adjusting UE scheduling for inter-UE CLI reduction.
    Inter-subband CLI measurement and reporting are necessary for SBFD operation.
Proposal
  Specify co-channel CLI handling schemes:
    Support inter-gNB co-channel CLI handling schemes (e.g., co-channel CLI and/or channel measurement, Coordinated scheduling for time/frequency resource between gNBs, Spatial domain coordination method, power control based solution). The detailed schemes are to be down-selected in WI
    Support UE-to-UE co-channel CLI measurement and reporting scheme (i.e., L1/L2 based CLI measurement and reporting including co-channel intra-/inter-subband CLI)
Notes: 현재 PSI 정보를 기반으로는 discard 만 수행할 것이다. 하지만 이걸로 충분하지 않고 PSI 기반의 reliability 및 prioritization을 해야 한다.
한줄로 표현될 수 있도록 하자. 기고의 observation 같이.

## Slide 8: Proposal
Objectives for Rel-19 Duplex Evolution WI
  Specify Indication of time and frequency domain locations of SBFD subbands to UEs
    Support semi-static indication of time location and frequency location of SBFD subbands
    Support dynamic indication of time location (e.g., slot(s) for SBFD can be converted to slot(s) for TDD DL only or flexible.)
  Study, and if justified, specify random access in SBFD symbol for SBFD aware UEs in RRC_IDLE/INACTIVE/CONNECTED mode
  Specify transmission, reception and measurement behavior and procedure for SBFD operation, including
    Resource allocation/CSI reporting with non-continuous frequency domain grid, different BW size across SBFD and non-SBFD symbols
    Multiple configuration for supporting operation on SBFD symbols and non-SBFD symbols: Power control, Frequency Hopping, CSI reporting
    UE behavior according to Non-SBFD symbol and SBFD symbol: DG-PUSCH, TBoMS, CG-PUSCH, PDSCH
    MIMO configuration, Beam correspondence
  Specify co-channel CLI handling schemes:
    Support inter-gNB co-channel CLI handling schemes (e.g., co-channel CLI and/or channel measurement, Coordinated scheduling for time/frequency resource between gNBs, Spatial domain coordination method, power control based solution). The detailed schemes are to be down-selected in WI
    Support UE-to-UE co-channel CLI measurement and reporting scheme (i.e., L1/L2 based CLI measurement and reporting including co-channel intra-/inter-subband CLI)
  RF requirements for SBFD operation at gNB
Notes: 현재 PSI 정보를 기반으로는 discard 만 수행할 것이다. 하지만 이걸로 충분하지 않고 PSI 기반의 reliability 및 prioritization을 해야 한다.
한줄로 표현될 수 있도록 하자. 기고의 observation 같이.

## Slide 9: Further Evolution beyond Duplex Evolution in Rel-18 SI
Discussion
  SBFD in Rel-18 SI follows conventional DL-UL resource separation in time-frequency domain
    Rel-18 SI excludes UE’s RF enhancements for full duplex operation
    Rel-18 SI considers limited enhancements for full duplex operation at gNB
  Further diverging service/traffic types require more flexible utilization of radio resources with reduced latency
    Full duplex (spectrum shared simultaneous DL-UL transmission/reception) operation within a carrier can be a strong candidate for further duplex enhancement
      Further enhancement at gNB implementation for full duplex operation (and at UE side as well) can be considered
  Therefore, spectrum shared full duplex (SSFD) operation can be studied in further releases as further evolution beyond duplex evolution studied in Rel-18
DL
UL
F
DL
&
UL
Guard
F
T
T
F
T
Half duplex operation
(Conventional)
SBFD operation
(Rel-18 SI)
SSFD operation
(Further evolution)
Notes: 현재 PSI 정보를 기반으로는 discard 만 수행할 것이다. 하지만 이걸로 충분하지 않고 PSI 기반의 reliability 및 prioritization을 해야 한다.
한줄로 표현될 수 있도록 하자. 기고의 observation 같이.

## Slide 10: References
  [1] RP-232745, “Summary for RAN Rel-19 Package: RAN1/2/3-led”, RAN Chair
  [2] TR38.858
Notes: 현재 PSI 정보를 기반으로는 discard 만 수행할 것이다. 하지만 이걸로 충분하지 않고 PSI 기반의 reliability 및 prioritization을 해야 한다.
한줄로 표현될 수 있도록 하자. 기고의 observation 같이.