## Slide 1
Views on 2Rx for XR
Apple Inc.
  3GPP TSG RAN Meeting #102
  Edinburgh, UK, December 11-15, 2023
  Source: Apple
  Agenda Item: 9.3.2.9
  RP-233168

## Slide 2
In RAN#101, 2Rx relaxation for XR was discussed and the following was endorsed:
  RAN#99 had outlined 2 steps towards progressing discussions on 2Rx XR devices, cf. RP-230740:
    “Step-1: Recognize that form factor limitations of a subset of XR devices can make it impossible for these devices to support 4 antenna ports.
      Exact characterization and form factor limitations of these devices are to be studied in RAN plenary. Contributions are invited to TSG-RAN#100 to address this.”
  Proposed resolution for Step-1 for the purpose of continuing discussions to Step-2:
    Handheld smartphone UEs are excluded from any 2Rx relaxation for XR wearables.
    The default for non-RedCap XR-wearable UEs is 4Rx (for frequency bands where 4Rx is mandated).
      A non-RedCap XR-wearable UE can be considered for 2Rx relaxation (for frequency bands where 4Rx is mandated) if and only if:
      Intended to be worn on the human head;
      When in use, is intended to be supported only by/behind the ears and by a nose-bridge resulting in a constrained form factor with limited volume available for Rx chains;
    No other relaxation is being considered apart from number of Rx antennas.
  ____________________________________________________________________________________________________________________________
  Step-2 is outlined as follows (cf. RP-230740):
    “Step-2: Recognize the importance of identifying these devices in the network, and potential network impact (e.g. performance, coverage, capacity) and UE impact
      Details of Step-2 will be further defined following the maturity of Step-1”
  Proposed scope for Step-2 for RAN#102:
    Address the impacts to RF and OTA requirements for non-RedCap 2Rx XR devices, and their potential network impact (performance, coverage, capacity, etc…) and the mitigation techniques.
    It is assumed that there is a need for the network to clearly identify non-RedCap XR devices with 2Rx restriction.
Background

## Slide 3
Analysis & evaluation on XR applications
XR applications are often associated with uplink traffic of substantial throughput and stringent latency/reliability requirements.
From Rel-17 XR study item evaluation, uplink rather than downlink is the bottleneck to achieve satisfied user experience (packet error rate less than 1% with the latency bound for each data flow).
  Definition of a satisfied (XR) UE:
    All the data streams of a UE are required to be received with more than 99% success rate to consider the UE as satisfied.
  As there is a latency budget for packets in each data stream, a packet can be dropped due to not enough scheduling opportunities or poor link quality.

## Slide 4
Coverage evaluation in XR
Coverage evaluation was conducted in Rel-17 XR study item (TR 38.838 “Study on XR (Extended Reality) Evaluations for NR”). Two evaluation methodologies were defined there, addressing different aspects in coverage:
  Evaluation with Methodology 1 reveals in a network loaded with XR devices at the network’s capacity, the coupling gain at the bottom 5 percentile, which reveals the coverage when intercell interference is the dominant factor.
  Methodology 2 is similar to the link level simulation conventionally used in 3GPP evaluations. Due to the particular XR traffic models, which are more elaborate than most traffic models used in previous releases, adaptation of the system level simulation was found useful in avoiding modifying LLS with the XR traffic models. Methodology 2 reveals the coupling loss of having a single XR device in the whole network, which reveals the coverages when thermal noise is the dominant factor.
Coverage Evaluation Methodology 2
For a given XR application (AR/VR/CG) for a given deployment scenario (DU/InH/UMa), the XR/CG in DL or UL coverage is determined as follows:
- Run SLS with #UEs per cell = 1 as shown in figure A.3-2. The UE is randomly dropped in the entire network (or in all the cells) that is associated with one of the three center cells (or gNBs), i.e., only one of the center gNBs is activated.
- Run SLS according to capacity evaluation methodology and determine whether the UE is satisfied or not.
- The coverage is defined to be the 5-percentile point in the CDF curve of coupling gain for all the satisfied UEs.
Figure A.3-2: Layout and UE distribution in Methodology 2 (1 UE / network)

## Slide 5
Evaluation results from TR 38.838
The evaluation results reveal:
  there is a difference in the coupling gain requirements for DL and UL, and UL is short by 15 dB (Methodology 1) or 24 dB (Methodology 2) for AR.
  Only for a case of VR, the gap is smaller, yet is still roughly 6 dB.
    Note: Only pose/control at low data throughput is generated in uplink and there is no video stream or audio/data streams in uplink.
Observations:
  To provide satisfactory XR service, both uplink and downlink need to work at the targeted throughput/latency/reliability, and the number of XR devices supported in a network is ultimately decided by the more stringent requirement between DL and UL.
  Uplink link budget is the bottleneck for network capacity as quantified by satisfied XR UEs. Often there is 15 dB to 24 dB difference in downlink link budget and uplink link budget requirements, in favor of the downlink. Therefore, 2Rx relaxation is not expected to impact the network coverage.
Link direction | Applications | PDB (ms) | #UE/cell | XR Coverage | 
 |  |  |  | Mean (dB) | Value (dB)
DL | VR/AR30 | 10 | 9 (Capacity) | -136.81 | -132.86
 |  |  | 10 (Capacity) |  | -140.76
 |  |  | 1 | -138.46 | -137.19
 |  |  |  |  | -140.9
 |  |  |  |  | -138
 |  |  |  |  | -137.73
 | VR/AR45 | 10 | 4 (Capacity) | -136.26 | -132.95
 |  |  | 6 (Capacity) |  | -139.56
 |  |  | 1 | -136.58 | -136.58
 | CG30 | 15 | 12 (Capacity) | -137.12 | -134.38
 |  |  | 11 (Capacity) |  | -139.86
 |  |  | 1 | -137.59 | -137.19
 |  |  |  |  | -138
UL | Pose | 10 | 1 | -130.5 | -136.01
 |  |  |  |  | -125
 | AR 1 stream | 30 | 1 | -119.99 | -121.61
 |  |  |  |  | -124.2
 |  |  |  |  | -123
 |  |  |  |  | -111.13
Evaluation with Methodology 1 for UMa
Link direction | Applications | PDB (ms) | XR Coverage | 
 |  |  | Mean (dB) | Value (dB)
DL | VR/AR30 | 10 | -145.32 | -145.33
 |  |  |  | -150.07
 |  |  |  | -144.65
 |  |  |  | -141.7
 |  |  |  | -144.84
 | VR/AR45 | 10 | -143.85 | -143.85
 | CG30 | 15 | -147.16 | -146.88
 |  |  |  | -148.2
 |  |  |  | -146.4
UL | Pose | 10 | -139.45 | -137.81
 |  |  |  | -139.8
 |  |  |  | -140.5
 | AR 1 stream | 30 | -120.01 | -122.5
 |  |  |  | -126.39
 |  |  |  | -111.13
 | AR 2 stream | 10,30 | -121.7 | -121.7
Evaluation with Methodology 2 for UMa

## Slide 6
Identification of 2Rx XR devices
Capture the following in the RAN4 specification:
  2Rx wearable UE: a UE intended to be worn on the human head. When in use, the UE is intended to be supported only by/behind the ears and by a nose-bridge resulting in a constrained form factor with limited volume available for Rx chains.
  Then, for the “2Rx wearable UE” defined as above, specify the 2Rx relaxation in the similar way as “Vehicular UE” and “RedCap UE” in TS38.101.
To provide further mechanisms for an operator to control what devices are allowed in its network, we are open to discuss the following solutions to identify the 2Rx XR devices in 3GPP
  2Rx XR device identification through a new UE capability signaling
  2Rx XR device identification through MIMO layer capability signaling
  2Rx XR device identification at initial access
  2Rx XR device identification through Subscriber Profile Identification (SPID)