## Slide 1
Discussion on MBS Related Enhancements
TCL New Technology
RP-233174

## Slide 2: Table of Contents
Support of MBS CP Extension & SFN operations
Support of Radio based Convergence of DTT and MBS
Support of Convergence of DTT/MBS & Satellite Access
Summary & Conclusion
RP-233174

## Slide 3: CP Extension Support
SFN Operation and CP extension are very necessary for NR MBS for guaranteeing enough coverage for media broadcast delivery as NR MBS is based on NR MFN cells operation only
In NR MBS the numerologies and cyclic prefix (CP) types is designed based on i.e., normal CP e.g., 15 kHz and 30 kHz as defined per TS 38.211. Such as numerologies limits the reachable coverage of SFN transmission especially for MBS broadcast, SFN operation CP extension beyond 15 and 30 kHz SCS is necessary to increase the theoretical coverage distance and improve the performance:
Study enhancements to support SFN operation and CP extension beyond 15 and 30 kHz to support wider broadcast coverage and improve the performance (RAN1).
Key objectives include:
RP-233174

## Slide 4: MBS & DTT Convergence
ETSI TS 103 720: “5G Broadcast System for linear TV and radio services; LTE-based 5G terrestrial broadcast system”.
DVB C100: Commercial Requirements for DVB-I over 5G
TG3-262r0 : ATSC 3.0 – 5G Harmonization
Benefits for Mobile network operators (MNO): Reducing load in cellular spectrum, improving spectral efficiency and enhancing the converge media content delivery
Benefits for broadcast network operators (BNO): Expanding the market by access of 5G mobile cellular users, improving performance via load balancing and spectrum sharing.
DTT technologies: ATSC , DVB, DTMB or ISDB including MBMS share almost the same system architecture : broadcasting servers, gateways and transmitters. The major difference between these technologies is that they use different transmission and radio configuration.
DVB already support interworking with 5G LTE broadcast via service configuration [ETSI TS 103 720] & [ESTI TS 124117].
DVB also support media-codec level convergence with 5G NR MBS system : Some codecs defined in DVB specifications support 5G Media Streaming segment formats defined based on Common Media Application Format (CMAF)[DVB-I DVB C100: ]
ATSC is currently discussing interworking of ATSC 3.0 with MBS via an Interworking Function (A3IWF) and studio-to- Transmitter Link as xMB interface to ATSC transmitter TG3-262r0
DTMB: CBN & ABS and Huawei are developing interworking of 5G LTE broadcast with NR
RP-233174

## Slide 5: MBS & DTT Convergence, Radio-Based
Figure 2: Option 1: Time Domain based MBS and DTT operations. Option 2: BWP/CFR based MBS and DTT operations
RP-233174
Key objectives include:
Due to regulatory constraints and lack of spectrum, there is an interest in to deploy both DTT and 5G MBS multiplexed in the same of different carriers. However, due to the fact that the frame structures of these two technologies are not compatible. To support efficient DTT and 5G MBS multiplexing it will be beneficial to study:
Definition of additional periodicity patterns for cell acquisition sub-frames to allow TDM operation between NR MBS, unicast and non-3GPP DTT (e.g., ATSC 3.0 and DVB-T2) frame structures (RAN1).
Definition of BWP/CFR for MBS, unicast and DTT to allow the reception 5G MBS, unicast and DTT by the same UE (RAN1, RAN2).

## Slide 6: Support of MBS & DTT Services via NTN
Key objectives include:
On-board Network Function (gNB, UPF) issues including
  Frequent MBS/DTT session update, IP multicast session update and GTP-U tunnel end-points configuration due to feeder link which due to on-board satellite change (RAN3).
  Signaling messages impacts due to the MBS/DTT mobility involving a large number of UEs per MBS/DTT sessions (RAN3)..
N2/N3
Ground station
NGSO satellites
Feeder Link
UEs
UPF AMF
CN
gNB
gNB
Feeder Link
CN
UPF
AMF
UEs
gNB
gNB
N2/N3
N2/N3
RP-233174
Figure 3: Example of mobility involving on-board gNBs Network Functions .

## Slide 7: Support of MBS & DTT Services via NTN
Other Key NTN related objectives :
Architectural enhancements for 5G multicast-broadcast services via NTN
Location dependent MBS service: Enabling distribution of different media content data to different MBS service areas, satellite beams coverage larger than the coverage of the targeted area of the broadcast service (RAN3)..
User group dependent MBS services: to enable User group dependent MBS/DTT services delivery to user group over a large geographic area and different regulatory regions (RAN3)..
Joint TN access and NTN MBS and DTT reception simultaneously (SA2,RAN2, RAN3).
RWS-230367- 5G-MAG views on Media related topics for Rel-19
RWS-230048 Consideration on RAN1/2/3 led NTN topics for Release 19
RP-233174

## Slide 8: Summary & Conclusion
In this report we propose to investigate study the following RAN enhancements related topics MBS and DTT and NTN convergence including:
Support of MBS CP Extension & SFN operations
Support of Radio based Convergence of DTT and MBS
Support of Convergence of DTT/MBS & Satellite Access