## Slide 1
0
Views on candidate RF topics for Rel-19
3GPP TSG RAN #102 RP-233430
Edinburgh , GB, December 11-15, 2023
Agenda Item: 9.1.4.2
Source: CMCC
Document for: Discussion

## Slide 2
Extension of UL Tx switching scenarios
Specify UE requirements to enable Tx switching between cases, where 2 contiguous aggregated carriers on band A and 2 contiguous aggregated carriers on band B, including both 1Tx-2Tx switching and 2Tx-2Tx switching.
Potential Objectives
In Rel-17, UL Tx Switching between one carrier in band A and two contiguous carriers in band B was specified.
In our network, both 2.6GHz (n41) and 4.9GHz (n79) has two contiguous UL carriers. In order to further improve the uplink throughput, UL 2Tx-2Tx switching between band A (2.6GHz) and band B (4.9GHz), each with two contiguous uplink carriers, should be supported.
Time mask requirements need to be specified for UL Tx switching between two contiguous carriers in band A and two contiguous carriers in band B.
According to TS38.214 section 6.1.6.2 Uplink switching for carrier aggregation, it is specified that UE is not expected to transmit for certain duration on any of the uplink carriers, there is no differentiation on the number of uplink carriers on each band. No RAN1 impact is observed.
Motivations: UL Tx switching

## Slide 3
Enhancement for Handheld UE
Specify RF requirements for PC1.5 of following band combinations
  PC1.5 2Tx: intra-band CA, PC2 TDD/FDD band 1Tx + PC2 TDD band 1Tx (UL MIMO and TxD) if not included in Rel-18
  PC1.5 3Tx:
    TDD + TDD band, including PC2 + PC2, PC1.5 + PC2/PC3
    TDD + FDD band, including PC2+ PC2(2Tx)
HPUE enhancement
Prioritize handheld UE enhancement compared to FWA
  6Rx single band for handheld UE
    Example bands are n41, n77, n78 and n79 (other bands to be introduced in the release independent way later from Rel-18)
    Applicable frequency upper bound to support 6Rx.
  3Tx inter-band UL CA for handheld UE
Enhancement for Handheld UE

## Slide 4
THANK YOU！