## Slide 1
3GPP TSG RAN#102 RP-233500
Edinburgh, Scotland, December 11-15, 2023
Agenda Item: | 9.1.2.5
Source: | CEPRI, China Southern Power Grid, SGITG, Spreadtrum
Title: | Motivation on smart grid differential protection backup for Rel.19
Document for: | Discussion and decision
China Electric Power Research Institute
2023-12
http://www.sgcc.com.cn/

## Slide 2
Introduction on State Grid
State Grid Corporation of China (SGCC)
The world's largest utility, and supplies power to 1.1 billion population with service area covering 88% of Chinese territory.
Ranking 3rd on Fortune Global 500 with a total revenue of 530 billion USD.
Operates backbone energy networks in 9 countries and regions.
Transformation(converting) capacity is 5.23 TVA(TW).
Length of transmission lines is 1.142 million km.
SGCC Sustainable Development with Green and Low-carbon
Chart: Length of transmission lines
| 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020
系列 1 | 0.8436 | 0.888 | 0.932 | 0.981 | 1.038 | 1.09 | 1.142
Northeast
East
North
Central
Southwest
Northwest
South
UHV AC in operation
UHV DC in operation
UHV AC under constriction
UHV DC under constriction

## Slide 3
Justification on differential protection backup
  Differential protection
    Differential protection is used to protect the power line from being burnt down and any secondary damages a fireball blaze on the power line can cause.
    The mechanism of line current differential protection follows the Kirchhoff's current law, which is that the sum of currents at a junction of a circuit equals to zero.
5G back up for differential protection
    Traditional differential protection is usually in an 1+1(even 1+N) backup mode via optical fiber. Optical fiber always brings very high cost and faces great construction difficulty in some areas, this lead to a very low penetration rate.
    5G NR backup mode for differential protection can potentially resolve the issues of optical fiber, and also resolve the concern from grid customers on wireless transmission robustness and is aligned with the differential protection devices which are traditionally equipped by 1+1 or 1+N backup modes.
Relay_a
(main)
Relay_a’
(back up)
Relay_b
(main)
Relay_b’
(back up)
Back up optical fiber
Main optical fiber
Traditional back up for differential protection
UE 1
UE1’ (back up)
Relay_a’(back up)
5G gNB
UE 2
UE2’ (back up)
Relay_b’ (back up)
Line current information sampling
Relay_a (main)
Relay_b (main)
5G back up for differential protection
I_a
I_b
Power line
CT
CT
Uu
Uu
XCBR
XCBR
I_a’
I_b’
Relay_a
Relay_b
Line Current Differential Protection by two protection relays
Note: In addition to SGCC, China Southern Power Grid also shows strong requirement on differential protection backup.

## Slide 4
Proposal
  Proposal
    Study and specify 5G Air Interface back up schemes for differential protection in R19.

## Slide 5
THANKS