## Slide 1: Rel19 WI proposals on AI/ML for Air Interface
3GPP TSG RAN Meeting #102 December 11-15, 2023
Agenda Item: 9.1.1.1
RP-233501
Sourced by: CEWiT, IIT-K, Tejas Networks

## Slide 2: CSI Enhancement Rel18
Observation for CSI compression,
In Rel18 SI, AI based compression of spatial-frequency CSI has been considered and precoding vector is taken as the input to the AI/ML model.
Benchmark : Rel16 Type-II codebook
Different types of training collaborations(type-1,type-2 and type-3) are assumed for model training of two-sided models.
Generalization of AI/ML models for various antenna configuration, deployment scenarios, carrier frequency were studied.
Performance monitoring using (a) proxy CSI model at UE side (b) legacy codebook at NW
Observation for CSI prediction,
In Rel18 SI, time-domain based UE side CSI prediction is considered.
Benchmark : Historic CSI / Kalman Filter
Generalization of AI/ML models over various observation window lengths, prediction window size, CSI periodicity and UE speeds were discussed.
Model monitoring using intermediate KPI at UE side and NW side were considered

## Slide 3: Proposal for Rel19
Proposal for CSI compression
  Support for normative WI in Rel19
  CQI calculation for higher ranks.
  CSI omission/priority rules when using AI/ML based feedback
  Capability report to pair the compatible CSI-generation model and CSI-reconstruction model
  For Type-3 training, consider the possible spec impact of signaling for quantization awareness, data collection, model monitoring and model retraining.
Proposal for CSI prediction,
  Proceed with normative work in Rel19 for UE-side CSI prediction
  Consider signaling impact on data collection
  AI/ML model selection based on model IDs for different UE speeds.
  Signaling procedures to facilitate LCM operations

## Slide 4: AI/ML for Positioning
Observation based on Rel18 study
Direct AI/ML positioning can achieve multifold enhancement gain to horizontal positioning accuracy than conventional positioning methods under both mild and heavy NLOS settings.
Good generalization ability with mixing data training or finetune.
Label based and Label free model monitoring are feasible.
Proposal for Rel19
Direct AI/ML Positioning and AI/ML assisted positioning at NW and UE side in R19 WI.
Data collection for training and monitoring assistance signalling (including report/request) and procedure to support LCM operations.
Data collection for training and monitoring measurement labeling types and quality , labelling assistance and RS configurations, timing information, scenario ID

## Slide 5: AI/ML for Beam Management
Proposals for Rel19
For AI-based beam management, from RAN1 perspective, at least the following are recommended for normative work
Both BM-Case1 and BM-Case2
  BM-Case1: Spatial-domain DL Tx beam prediction for Set A of beams based on measurement results of Set B of beams
  BM-Case2: Temporal DL Tx beam prediction for Set A of beams based on the historic measurement results of Set B of beams
DL Tx beam prediction for both UE-sided model and NW-sided model
Necessary signaling/mechanism(s) to facilitate data collection, model inference, and performance monitoring for both UE-sided model and NW-sided model
Signaling/mechanism(s) to facilitate necessary LCM operations via 3GPP signaling for UE-sided model