## Slide 1: LTM Enhancements for Inter-CU Handover
3GPP TSG RAN Meeting #102 December 11-15, 2023
Agenda Item: 9.1.2.1
RP-233508
Sourced by: CEWiT, IIT-K, Tejas Networks

## Slide 2
Potential objectives:
  Specify support for inter-CU Layer 2 Mobility (LTM)
    Prioritize the case when CU is acting as MN when DC is not configured
    Whether to additionally support e.g. when CU is acting SN? (focus on practical deployments)
      In this case, whether it is supported for EN-DC and/or NR-DC only?
  Measurements related enhancements for purpose of supporting LTM:
    Specify event triggered L1 measurement reporting for triggering LTM  depending on the detailed discussion in RAN#102, resolve how to avoid overlapping with similar objective in MIMO WI
    Specify support for CSI-RS measurements for LTM procedures and enable CSI-RS based beam management and/or other physical layer operations on candidate cells before LTM
  Support of conditional mobility (including set of candidate cells, UE evaluated mobility conditions, ability for UE to perform subsequent mobility procedures without need for RRC configuration) along with short mobility interruption time (similar to that achievable with LTM).
    Next Step question to consider the most appropriate approach to achieve this aim. For example, by specifying conditional triggering of LTM, or specifying support of Early TA or RACHless (as defined for LTM) to be used as part of layer 3 CHO, or possibly other approaches. If this questions cannot be concluded during the Rel-19 scoping discussion then it may be possible to start with a RAN2 study phase.
  Anything else (e.g., RAN4 related)?
References: RP-232745

## Slide 3: LTM for Inter-CU Mobility
Relevant Issues
  Facilitate Security Key updates as a part of LTM
    Reuse existing Xn interface messages
  Candidate List Preparation for candidate CUs
    Candidate-DU lists are to be sent from each candidate CUs.
    Support over Xn interface
  MAC reset.
    Similar to L3 HO – full reset