## Slide 1
3GPP TSG RAN Meeting #102
Edinburgh, Scotland, December 11-15, 2023
Agenda ltem: 9.1.1.4
Source: BJTU (Beijing Jiaotong University)
Title: Multiple access and backscatter consideration for R19 ambient IoT
Document for: Discussion and decision
Authors： Gongpu Wang, Rongtao Xu, Ming Liu, Junliang Lin, Ziqi Cui
RP-233518

## Slide 2
NR
LTE
RedCaP
LTE Cat.4
eMTC
LTE Cat.1
NB-IoT
Ambient IoT (Backscatter)
1 Gbps
100 ~10 Mbps
1 Mbps
100 kbps
<100 kbps
Rate
Power Consumption
<1 mW
1 mW ~ 1uW
Lower rate / energy / hardware cost
Lower complexity, massive connection
Visions on A-IoT
Notes: 计算机相连；手机相连；万物互联。

## Slide 3
Low Power
Low Cost
Easy Deployment
Massive Connection
Wide-ranging Applications: logistics, agriculture, transport, monitoring, etc.
Applications and Use Cases

## Slide 4: Views on Physical Layer Issue
Physical layer
  Multiple access
    Device A/B: proper multiple access scheme that balances efficiency and complexity, e.g. CDMA/enhanced-TDMA, etc.
    Device C: efficiency-oriented multiple access, i.e., other OMA/NOMA, etc.
  Frame structure
    Device A/B: (1) normal/extended preamble + payload + CRC
    (2) normal preamble + payload1 + midamble + payload2 + postamble + CRC
    Device C: normal preamble + payload + CRC
    Preamble/midamble/postamble pattern: position/power constraint/spectrum efficiency, etc.
  Waveform
    Device A/B: ASK/FSK/PSK
    Device C: QAM, OFDM, OTFS etc.

## Slide 5: Views on Transceiver and Interference Issues
Transceiver architecture
  Transmitter
    Device A/B: only backscattering
    Device C: compatible of both passive backscattering and active transmitting
  Receiver
    Device A/B: LP WUS, energy harvesting, power management, negative resistance amplification
    Device C: NB-IoT / WUS with low-noise amplifier, power management
  Interference
    Self-interference
      Carrier distortion, i.e., signal impaired by phase noise, IQ imbalance, etc
    Leakage from In-band NR signal / low-SNR case
      No prior information on NR signal, spread spectrum: DSSS/FHSS/CSS

## Slide 6: Current Research Progress on A-IoT
Constellation plot
Distorted and impaired backscatter signal
Wavy signal and striped constellation are intrinsically related

## Slide 7: Current Research Progress on A-IoT
Traditional signal processing
DC
Blocker
Matched
Filter
Frame
Sync.
Symbol
Sync.
Channel
EQ.
Detection
DC
Blocker
Matched
Filter
Frame
Sync.
Symbol
Sync.
Channel
EQ.
DSIC
Time-varying self-interference suppression
Adaptive decision boundary
Dynamic Self-interference Cancellation
Data-aided Decision Boundary
Our Solution
DDB

## Slide 8: Current Research Progress on A-IoT
bit ‘0’
PLL
fractional
mode
bit ‘1’
PLL
fractional
mode
bit ‘1’
PLL
integral mode
bit ‘0’
PLL
integral mode
Proposed DSIC lowers RMS by more than 50%

## Slide 9: Current Research Progress on A-IoT
Fractional mode
(only DDB)
Integral mode
(only DDB)
Fractional mode
(only DSIC+DDB)
Integral mode
(only DSIC+DDB)
Proposed DDB effectively reduces the BER
when the training length > 10
BER improvement of DDB

## Slide 10: Proposal
Support R19 study/work item for Ambient–IoT, considering:
  multiple access： new CDMA
  frame structure: training/pilot design (both transmitter and tag)
  transceiver design: SIC at receiver and SVM-based detector