## Slide 1: Views on NR NTN evolution in Rel-19
China Telecom
December 2023
3GPP TSG RAN Meeting #102
Edinburgh, UK, December 11-15, 2023
Agenda: 9.1.2.3
RP-233594

## Slide 2: Potential Objectives in RP-232745
For Rel-19, the spec work for NTN should focus on the essential issues to promote the deployment of NR NTN in the future.
In the summary for RAN Rel-19 Package in RP232745, the potential objectives for NR NTN were captured as below:

## Slide 3: Coverage enhancement
DL coverage enhancement
  Motivation: The DL coverage of NTN cells is impact by the link bughet of NTN wireless channel, power sharing among multiple satellite beams and the movement of satellites. With satellite altitude increasing, the provision of DL coverage faces more challenges. The DL coverage of GEO needs to place emphasis in the evolution of Rel-19 NTN.
  Potential Objective
    Identify the bottleneck of NTN DL physical channels. The performance of PDSCH (for VoIP, low data rate, Msg2, Msg4), PDCCH, SSB should been evaluated especially for GEO scenario. The enhancement methods focus on the bottleneck channels.
UL coverage/capacity enhancement
    Via HPUE
    Via Multiplexing
Proposal 2: For NR-NTN in Rel-19, the UL coverage/capacity enhancement should be specified.
Proposal 1: For NR-NTN in Rel-19, the DL coverage should be evaluated, especially for GEO scenario. The enhancement methods focus on the bottleneck channels.

## Slide 4: Mobility enhancement
Motivation
  In Rel-18 there are some leftover work for mobility, such as soft switch of PCI unchanged enhancement.
  The co-existence of TN and NTN cells introduces complexity of cell reselection and handover of UEs.
  The signaling overhead needs to optimize when the target cell is same for a group of UEs.
Potential Objective
  Soft switch of PCI unchanged enhancement of SSB collisions
  TN-NTN cell reselection and handover to reduce the power saving and service continuity.
  The categorize of UEs into groups and the procedure of group handovers.
Proposal 3: For NR-NTN in Rel-19, the TN-NTN cell reselection and handover could be considered.

## Slide 5: Support of Regenerative Architecture
Motivation
  Regenerative payloads can reduce control plane latency (RAN level), improve service and feeder link spectrum efficiency, and make deployment more flexible compared to existing transparent architectures.
  Currently, satellite can support full gNB onboard scenario at the hardware/software level, e.g. GEO support carrying high-performance payloads and achieved high-throughput satellite communication using SDR, multi beam and other technologies.
Potential Objective
  Both GEO and LEO are supported.
  With/without ISL are considered. ISL could be regarded as a transport link without any specification work.
  Specify the support of gNB on board in TS 38.300, and evaluate enhancements related to the NGAP to address feeder link switchover issue, if needed.
Proposal 4: Support regenerative payload and prioritize full gNB on board.
Proposal 5: Evaluate enhancements related to the NGAP to address feeder link switchover issue.

## Slide 6: Conclusion
In this contribution, we have following proposals:
Proposal 1: For NR-NTN in Rel-19, the DL coverage should be evaluated, especially for GEO scenario. The enhancement methods focus on the bottleneck channels.
Proposal 2: For NR-NTN in Rel-19, the UL coverage/capacity enhancement should be specified.
Proposal 3: For NR-NTN in Rel-19, the TN-NTN cell reselection and handover could be considered.
Proposal 4: Support regenerative payload and prioritize full gNB on board.
Proposal 5: Evaluate enhancements related to the NGAP to address feeder link switchover issue.

## Slide 7: Thanks!