## Slide 1
3GPP TSG RAN Meeting #102 RP-233605
Edinburgh, Scotland, December 11-15, 2023
Source: Huawei, HiSilicon
Title: Remaining issues on 2Rx relaxation for XR wearable devices
Document for: Discussion and decision
Agenda Item: 9.3.2.9

## Slide 2
Background of “2Rx relaxation for XR wearable devices”
Discussion history in RAN plenary: Raised in RAN#96, endorsed way forwards at RAN#99/100/101
Issue firstly raised
Issue re-submitted, but no discussion
Had some discussions, but no conclusion
Endorsed a way forward in RP-230740
202206 (RAN#96)
202209 (RAN#97)
202212 (RAN#98）
202303 (RAN#99)
Endorsed a way forward in RP-231483
202306 (RAN#100)
RAN#101 discussions (Endorsed following way forward and next steps in RP-232657)
RAN#99 had outlined 2 steps towards progressing discussions on 2Rx XR devices, cf. RP-230740:
“Step-1: Recognize that form factor limitations of a subset of XR devices can make it impossible for these devices to support 4 antenna ports.
Exact characterization and form factor limitations of these devices are to be studied in RAN plenary. Contributions are invited to TSG-RAN#100 to address this.”
Proposed resolution for Step-1 for the purpose of continuing discussions to Step-2:
Handheld smartphone UEs are excluded from any 2Rx relaxation for XR wearables.
The default for non-RedCap XR-wearable UEs is 4Rx (for frequency bands where 4Rx is mandated).
A non-RedCap XR-wearable UE can be considered for 2Rx relaxation (for frequency bands where 4Rx is mandated) if and only if:
  Intended to be worn on the human head;
  When in use, is intended to be supported only by/behind the ears and by a nose-bridge resulting in a constrained form factor with limited volume available for Rx chains;
No other relaxation is being considered apart from number of Rx antennas.
202309 (RAN#101)
Endorsed way forward and next steps in RP-232657
Step-2 is outlined as follows (cf. RP-230740):
“Step-2: Recognize the importance of identifying these devices in the network, and potential network impact (e.g. performance, coverage, capacity) and UE impact
Details of Step-2 will be further defined following the maturity of Step-1”
Proposed scope for Step-2 for RAN#102:
Address the impacts to RF and OTA requirements for non-RedCap 2Rx XR devices, and their potential network impact (performance, coverage, capacity, etc…) and the mitigation techniques.
It is assumed that there is a need for the network to clearly identify non-RedCap XR devices with 2Rx restriction.

## Slide 3
Discussion – Time plan to address XR 4Rx vs 2Rx issue
The remaining issues for XR 2Rx can be addressed and decided at RAN#102
XR is one important industry to expand the value for 5G-Advanced and the issue is better to be solved within Rel-18
RAN#101 already concluded the characterization of XR devices to which a 2Rx relaxation could apply, thus Step 1 has been finalized
RAN#102 can address and decide the remaining issues in step 2
The major remaining issues to be addressed at RAN#102 include the below
The definition of XR devices applicable for 2Rx relaxation needs to be captured in the specification
The appropriate requirements need to be defined in RAN4
The identification of XR devices with 2Rx relaxation need to be defined in RAN2/RAN4
The access control of XR devices with 2Rx relaxation
Proposal 1：RAN#102 to discuss and decide the way forward on XR device with 2Rx relaxation
The definition of XR devices applicable for 2Rx relaxation needs to be captured in the specification
The appropriate requirements need to be defined in RAN4
The identification of XR devices with 2Rx relaxation need to be defined in RAN2/RAN4
The access control of XR devices with 2Rx relaxation
[1] https://omdia.tech.informa.com/pr/2023/02-feb/omdia-near-eye-display-shipments-for-xr-applications-will-grow-by-67-in-2023-thanks-to-the-new-model

## Slide 4
Discussion – Remaining issues on 2Rx relaxation for XR wearable devices
Capture the definition of XR devices applicable for 2Rx relaxation
It is useful to capture the definition agreed in RAN#101 for common understanding and future testing/certification work
The potential specification to capture this definition can be discussed, e.g. 38.300, 38.306, 38.101 etc.
38.101 is preferred, as 38.101 is the place which usually defines different UE form factors with different RF requirements, e.g. for FWA devices, 2Rx vehicles.
Proposal 2: It is suggested to use 38.101 to capture the definition of XR devices applicable for 2Rx relaxation.
Potential Requirements definition in RAN4
RAN4 has defined 2Rx RF requirements in Table 7.3.2-1a/b in TS 38.101-1 for RF requirements, and XR devices applicable for 2Rx relaxation can reuse the requirements defined in this table as an exception (similar definition as FWA devices)
OTA requirements are band specific and rely on large scale measurement data from commercial available UEs. RAN4 has not finished defining OTA requirement for legacy handheld UE yet even after 2 releases and it seems not practical to define OTA requirements now.
There is performance difference between 4Rx and 2Rx in network capacity, and it’s not appropriate to define unified OTA requirements for 4Rx and 2Rx devices accordingly
Proposal 3: It is suggested to re-use 2Rx RF requirements defined in Table 7.3.2-1a/b in TS 38.101-1 for XR devices applicable for 2Rx relaxation, and OTA requirements are not essential to be defined at this stage.

## Slide 5
Discussion – Remaining issues on 2Rx relaxation for XR wearable devices
Potential mechanism for device identification
Option 1: similar mechanism as REDCAP, e.g. MSG1/MSG3 early identification
Option 2: similar mechanism as 2Rx for vehicles, e.g. a new SPID (Subscriber Profile ID for RAT/Frequency Priority) value for 2Rx XR devices
Option 2 is preferred since SPID can give operators control on this relaxation, and has less specification workload.
Proposal 4: It is suggested to adopt a new value for SPID to identify XR devices applicable for 2Rx relaxation.
Potential mechanism for access control
In REDCAP
  There is one bit indicator to show whether the network supports REDCAP
  There are two access barring indicators in SIB1 to indicate respectively whether REDCAP 2Rx/1Rx UEs are allowed to camp on this cell
For XR devices with 2Rx relaxation, one bit indicator is sufficient as there is only 2Rx relaxation (the design can be simplified)
  Set to “1” indicates the network supports such services and the UE is allowed to camp on this cell
  Set to “0” indicates the network does not support such services and the UE is not allowed to camp on this cell
Proposal 5: It is suggested to introduce one bit indicator in NR SIB to indicate whether the XR devices with 2Rx relaxation are allowed to camp on this cell.

## Slide 6
Summary
Proposal 1：RAN#102 to discuss and decide the way forward on XR device with 2Rx relaxation
The definition of XR devices applicable for 2Rx relaxation needs to be captured in the specification
The appropriate requirements need to be defined in RAN4
The identification of XR devices with 2Rx relaxation need to be defined in RAN2/RAN4
The access control of XR devices with 2Rx relaxation
Proposal 2: It is suggested to use 38.101 to capture the definition of XR devices applicable for 2Rx relaxation.
Proposal 3: It is suggested to re-use 2Rx RF requirements defined in Table 7.3.2-1a/b in TS 38.101-1 for XR devices applicable for 2Rx relaxation, and OTA requirements are not essential to be defined at this stage.
Proposal 4: It is suggested to adopt a new value for SPID to identify XR devices applicable for 2Rx relaxation.
Proposal 5: It is suggested to introduce one bit indicator in NR SIB to indicate whether the XR devices with 2Rx relaxation are allowed to camp on this cell.