## Slide 1
Views on evolution of NR duplex operation in Rel-19
3GPP TSG RAN Meeting #102
Edinburgh, Scotland, December 11-15, 2023
Agenda item: 9.1.1.3
RP-233610

## Slide 2
01
Background
02
Outcome of Rel-18 study item
03
Prototypes of SBFD
04
Draft Rel-19 WI Objective

## Slide 3: Background: Motivation for SBFD
e7d195523061f1c074694c8bbf98be7b1e4b015d796375963FD28840057458461C7CA0DAD340D15583DEDFC2E3241C4F392EF3A8B4D067B40CF4F149DD7E51F346B0CAB1BCCF6DB2480C67273C6C9E4C1DEDEDC3DC32419F7EF6E3A45653EEB37EB607A1606D9B642BAD9E7DB48978CCC6C17D46B37F2A89DF2B4C05B1F2618D36B27D7DDA3B9D69
SBFD addresses the challenge of supporting both high UL throughout traffic and high reliability traffic in the same cell.
Performance assurance is one of main challenges for vertical
BW >200Mbps
Latency 5-10ms
HD Machine Vision
Ultra-HD 3D Machine Vision
BW >50Mbps
Latency 20ms
Remote Control
Ultra-dense remote control
BW >50Mbps
Connectivity 1~2
Latency 20ms@99.99%
BW >200Mbps
Connectivity >10
Latency 10-15ms@99.999%
High uplink requirement for HD video and XR
High fidelity, strong interaction
>100Mbps，<20ms
High fidelity, less interaction
>100Mbps， >150ms
Online game
XR
BW 5Mbps
Latency 100ms
Video 1080P
Video 4K
BW 25Mbps
Latency 100ms
Throughput
< 10ms@99.999%
Machine vision quality inspection
Panoramic monitoring of production line
AGV coordination
Cloud PLC
Remote control of crown block
Unmanned driving
Panoramic monitoring
Machine vision inspection of steel strip surface
Intelligent manufacturing
Scenarios
Outdoor
Outdoor & Indoor
Main services
> 300Mbps
Latency
< 20ms@99.999%
> 300Mbps
Control command
Smart Steel Industry
Diverse requirement for sensing, remote control and smart industry

## Slide 4: Background: Study item in 3GPP
The objective of this study is to identify and evaluate the potential enhancements to support duplex evolution for NR TDD in unpaired spectrum.
In this study, the followings are assumed:
  Duplex enhancement at the gNB side
  Half duplex operation at the UE side
  No restriction on frequency ranges
The detailed objectives are as follows:
  Identify applicable and relevant deployment scenarios (RAN1).
  Develop evaluation methodology for duplex enhancement (RAN1).
  Study the subband non-overlapping full duplex and potential enhancements on dynamic/flexible TDD (RAN1, RAN4).
    Identify possible schemes and evaluate their feasibility and performances (RAN1).
    Study inter-gNB and inter-UE CLI handling and identify solutions to manage them (RAN1).
      Consider intra-subband CLI and inter-subband CLI in case of the subband non-overlapping full duplex.
    Study the performance of the identified schemes as well as the impact on legacy operation assuming their co-existence in co-channel and adjacent channels (RAN1).
    Study the feasibility of and impact on RF requirements considering adjacent-channel co-existence with the legacy operation (RAN4).
    Study the feasibility of and impact on RF requirements considering the self-interference, the inter-subband CLI, and the inter-operator CLI at gNB and the inter-subband CLI and inter-operator CLI at UE (RAN4).
    Note: RAN4 should be involved early to provide necessary information to RAN1 as needed and to study the feasibility aspects due to high impact in antenna/RF and algorithm design, which include antenna isolation, TX IM suppression in the RX part, filtering and digital interference suppression.
    Summarize the regulatory aspects that have to be considered for deploying the identified duplex enhancements in TDD unpaired spectrum (RAN4).
Note: For potential enhancements on dynamic/flexible TDD, utilize the outcome of discussion in Rel-15 and Rel-16 while avoiding the repetition of the same discussion.

## Slide 5: Outcome of Rel-18 study item
Simulation results
For coverage, link level simulation was conducted by companies
  RAN1 observed 5.09 – 5.41dB gain (median value) for FR1 for SBFD
  RAN1 observed 5.72 – 6.92 dB gain (median value) for FR2-1 for SBFD
For UPT, system level simulation was conducted by companies
  For deployment case 1: single operator & single-layer network
    RAN1 observed UPT gain for indoor scenarios for most cases
    RAN1 observed UPT gain for urban macro and dense urban macro for most cases if gNB-self interference, co-site inter-sector CLI and gNB-gNB CLI are suppressed to a acceptable level
  For deployment case3-2: single operator & two-layer network
    RAN1 observed UPT gain for most cases
  For deployment case 4: two operators (SBFD and TDD operator) & two-layer network
    RAN1 observed UPT loss for both SBFD operator and TDD operator for most cases especially for 0% grid-shift and RAN1 observed mean/5% UL UPT gain of SBFD operator in most cases.

## Slide 6: Outcome of Rel-18 study item
SBFD framework
SBFD operation at gNB for UEs was studied under the following assumptions,
  SBFD operation within a TDD carrier,
  SBFD scheme within a single configured DL and UL BWP pair with aligned center frequencies, and
  Up to one UL subband for SBFD operation in an SBFD symbol (excluding legacy UL symbol) within a TDD carrier.
RAN1 concluded SBFD operation Alt 4 is feasible for RRC_CONNECTED state from the RAN1 specification perspective, where SBFD operation Alt 4 assumes
  Both time and frequency locations of subbands for SBFD operation are known to SBFD aware UEs.
  UE behaviors for non-SBFD aware UEs follow existing specifications.
  From RAN1 perspective, new UE behaviors can be introduced for SBFD aware UEs based on the time and frequency locations of subbands for SBFD operation.
Non-SBFD aware UEs, including legacy UEs, and SBFD aware UEs can coexist in cells with SBFD operation at gNB side from RAN1 specification point of view.
To support SBFD operation Alt 4 for RRC_CONNECTED state, RAN1 identified the following potential specification impact for SBFD-aware UE:
  Indication of time and frequency domain locations of SBFD subbands to UEs
  UE transmission, reception and measurement behavior and procedures in SBFD symbols and/or non-SBFD symbols

## Slide 7: Outcome of Rel-18 study item
CLI handling
For semi-static SBFD, the gNB-to-gNB co-channel CLI handling schemes and UE-to-UE co-channel CLI handling schemes were studied, including performance and specification impact, which are included in Section 7.4.2, Section 7.4.3 and Section 7.4.4. The summary of observations for co-channel CLI handling schemes are included in Section 7.4 of TR38.858.
  For dynamic/flexible TDD, the gNB-to-gNB co-channel CLI handling schemes and UE-to-UE co-channel CLI handling schemes, which can be specific for dynamic/flexible TDD and/or common for both SBFD and dynamic/flexible TDD, were studied, including analysis, performance and specification impact, which are included in Section 8.3 and Section 8.4. The summary of observations for gNB-to-gNB CLI handling schemes are included in Section 8.3 TR38.858.

## Slide 8: Prototypes of SBFD
Two SBFD BS prototypes are researched and verified by ZTE and CMCC collaboratively in CMCC’s 5G-A Innovation Lab.
  The 1st SBFD prototype is researched to verify the feasibility and evaluate the actual performance of SBFD operation with test UE (TUE).
  The 2nd SBFD prototype is researched to verify the compatibility with legacy commercial UEs and also test the performance. The commercial 5G UEs used in our tests are ZTE Axon 20 and Axon 30 with 2T4R.
Prototype | Figures | Performance
The 1st SBFD prototype with TUE (4T4R) |  | Peak UL data rate: 1.4Gbps E2E latency: less than 4ms
The 2nd SBFD prototype with commercial UE (2T4R) |  | Peak UL data rate: 700Mbps E2E latency: around 4ms

## Slide 9: Prototypes of SBFD
Another filed test of the SBFD prototype with commercial UE in outdoor environment is also carried out in ZTE Xi'an Research Institute.
Prototype | Figures | Performance
Field test SBFD prototype with commercial UE (2T4R) |  | Peak UL data rate: 672 Mbps E2E latency: around 5.3ms

## Slide 10: Prototypes of SBFD
The subband configuration and other the detailed setting about this SBFD prototype
  The first slot and last slot are DL only slot and UL only slot with 100MHz transmission bandwidth, respectively. The DL subband is set as 10MHz and the UL subband is set as 90MHz.
  More detailed configuration of SBFD prototypes and results can be found in our RAN1 tdoc R1-2304595

## Slide 11: Draft Rel-19 WI Objective
RAN1 has finished the duplex evolution study item in August meeting. Based on RAN1’s outcome, it is observed that SBFD provides UL UPT, latency and coverage gain in most cases if the gNB-self interference, co-site inter-sector CLI and gNB-gNB CLI are suppressed under a acceptable level. Meanwhile, the DL performance loss is unobvious or smaller than the gain for UL.
Targeted SBFD BS class and deployment scenarios should be decided after the completion of RAN4 SBFD work.
The justification during the SI phase show that it is beneficial to start the normative work for subband full duplex in Rel-19.
The estimated TU for RAN1 for subband full duplex in Rel-19 is 2 TUs per meeting.
  This is under the assumption that only basic SBFD operations together with ~ 2 CLI handling schemes for gNB side and ~ 2 CLI handling schemes for UE side will be included in the WI

## Slide 12: Draft Rel-19 WI Objective
  Proposal 1: Start normative work for subband full duplex at gNB side in Rel-19 with 2 TUs in RAN1.
  Proposal 2: Draft objectives for Rel-19 subband full duplex
  SBFD framework (RAN1, RAN2)
    Support semi-static subband-based SBFD configuration/operation within one TDD carrier, same subband frequency resources across different SBFD symbols, both time/frequency locations of subbands are known to SBFD aware UEs
    Unaligned boundaries between resource block group(s)/reporting subband(s) and SBFD subbands (e.g., PRG)
    Resource configuration/allocation across DL subbands (e.g., CSI-RS, CLI-RS)
    DL/UL transmissions across SBFD symbols and non-SBFD symbols in different slots
    DL/UL collision handling, including SBFD operation under SSB symbols
    Potential RACH enhancement for SBFD operation
    CLI schemes for SBFD & dynamic TDD (RAN1, RAN3)
    gNB-gNB CLI handling
      SSB/CSI-RS based measurement, finer granularity of measurement/report, including the time misalignment issue between gNBs due to the non-zero N_TA_offset
      Spatial domain coordination: beam nulling, report of high/low interfering Tx beam
    UE-UE CLI handling
      L1 based measurement/report, finer granularity of measurement/report,
    Information exchange between gNBs, including at least SBFD pattern and measurement results (RAN3)
    RF requirement definition for SBFD BS (RAN4)

## Slide 13
Thank You