## Slide 1
Views on Rel-19 Mobility Enhancement
3GPP TSG RAN Meeting #102
Edinburgh, Scotland, December 11-15, 2023
Agenda item: 9.1.2.1
TDoc number: RP-233617

## Slide 2: Background -- NR mobility enhancements in Rel-18
  Both LTM and subsequent CPAC have been supported in Rel-18 with similar framework
    Configuration of candidate cells will be provided to UE as RRC container, and similar method for signaling overhead reduction (reference + delta signaling) is expected to be used in both approaches.
    One of the pre-configured container will be applied once mobility/SCG change is required, back and forth cell/cell group switch among pre-configured RRC containers is allowed.
  Limitation or drawbacks of Rel-18 mobility
    For LTM:
      Limited scenario: Inter-CU is not supported.
      Restricted demodulation perf. and user-perceived-throughput (UPT) experience: CSI-RS based measurement (e.g., CSI meas./acq., and T/F-fine-sync by using TRS) is not supported.
      Imbalance between report latency and overhead: event-based measurement reporting is not supported.
      Pingpong risk: L1 measurement filtering is not supported.
    Only NR-DC with selective activation of SCG (i.e. subsequent CPAC) is supported.

## Slide 3: Rel-19 Mobility - Enhancements on LTM
  Inter-CU LTM
    Motivation: To extend the benefits of LTM to additional scenarios, e.g. inter-CU, NR-DC
    Potential WID objectives
      Support CU as MN in NR SA / NR CA / NR-DC, and CU as SN (for FR2) in NR-DC
      Candidate cell configurtaion and maintenance for inter-CU candidates (also including inter-CU + intra-CU candidates), including Xn/F1 interface signaling design
      Support of subsequent inter-CU LTM without need for RRC reconfiguration
      Security update and L2 handling
      Early data forwarding
  Conditional LTM
    Motivation: To combine latency benefits of LTM with reliability benefits of CHO by introducing conditional triggering for LTM
    Potential WID objectives
      Signalling for configuration of conditional candidate cells, execution conditions, early DL/UL synchronization, etc. (leveraging as much as possible from Rel-18 LTM)
      Support of subsequent conditional LTM without need for RRC reconfiguration

## Slide 4: Rel-19 Mobility - Measurements related enhancements
  Event triggered L1 measurement report
    Motivation: To achieve good balance between report latency and report overhead and power saving compared to CSI-based report.
    Potential WID objectives
      Specify event triggered L1 measurement report, where it does not overlap with objectives of Rel-19 MIMO WI, e.g.,
        Rel-19 Mob enh.: RS config., triggering-event, condition to trigger/stop, report container (UCI on PUCCH/PUSCH v.s. MAC CE on PUSCH), etc.
        Rel-19 MIMO WI: Report format (e.g., UCI on PUCCH/PUSCH)
  CSI-RS based “other physical layer operation” on candidate cells for LTM
    Motivation: To achieve link adaptation and fine F/T-sync and guarantee demodulation performance before cell switch command.
    Potential WID objectives
      Specify support for CSI-RS measurements for LTM procedures and enable CSI-RS based beam management and CSI acquisition and TRS Tracking (if not supported or completed in Rel-18 LTM) on candidate cells before LTM

## Slide 5: Proposed objectives
Proposed objectives:
  Specify support for inter-CU LTM [RAN2, RAN3]
    Support CU as MN in NR SA / NR CA / NR-DC, and CU as SN (for FR2) in NR-DC
    Candidate cell configurtaion and maintenance for inter-CU candidates (also including inter-CU + intra-CU candidates), including Xn/F1 interface signaling design
    Support of subsequent inter-CU LTM without need for RRC reconfiguration
    Security update and L2 handling
    Early data forwarding
  Measurements related enhancements for purpose of supporting LTM [RAN1, RAN2]
    Specify event triggered L1 measurement reporting for triggering LTM
    Specify support for CSI-RS measurements for LTM procedures and enable CSI-RS based beam management and CSI acquisition and TRS Tracking (if not supported or completed in Rel-18 LTM) on candidate cells before LTM
  Specify support for conditional LTM [RAN2, RAN3]
    Signalling for configuration of conditional candidate cells, execution conditions, early DL/UL synchronization, etc. (leveraging as much as possible from Rel-18 LTM)
    Support of subsequent conditional LTM without need for RRC reconfiguration

## Slide 6: Thank You！