## Slide 1
Huawei, HiSilicon, CAICT
AI/ML for Air Interface in Rel-19
3GPP TSG RAN#102 RP-233659
Edinburgh, December 11-15, 2023
Agenda Item: 9.1.1.1

## Slide 2
Contents
Performance evaluations of use cases in Rel-18 SI
Key outcome of study in RAN1/2/4
Extension for temporal-spatial-frequency (TSF) CSI compression
Views on the potential scope for Rel-19 AI/ML for air interface
Discussion on project management for Rel-19 AI/ML for air interface

## Slide 3
Performance evaluations of use cases in Rel-18 SI
CSI
Beam Management
Positioning
BM-case 1: Spatial-domain BM
  Results for the case that set B is a 1/4 subset of set A:
    DL Tx beam prediction accuracy
    about 70-80% prediction accuracy achieved by AI for Top-1 case
    RSRP difference
    below or about 1dB achieved by AI for Top-1 case
  Lower gain observed when Set B is a 1/8 subset of Set A
BM-case 2: Temporal-domain BM
  Results for the case that set B is a 1/4 subset of set A:
    about 56.4-93.4% prediction accuracy achieved by AI for Top-1 case with 80 ms predication time
Observation: It is beneficial to enable AI/ML for beam management in the considered evaluation scenarios
Direct positioning
  Results for the case of InF-DH heavy NLOS
  <1m@90% horizontal positioning accuracy as compared to >15m for existing positioning method
Assisted positioning
  Results for the case of InF-DH moderate and heavy NLOS
  <0.4m@90% horizontal positioning accuracy as compared to >9m for baseline in moderate NLOS scenario
  <1m@90% horizontal positioning accuracy as compared to >15m for baseline in heavy NLOS scenario
  Observation: It is beneficial to enable AI/ML for positioning in the considered evaluation scenarios
CSI compression (spatial-frequency domain compression)
  Baseline: R16 Type 2 codebook
  Results (1-on-1 joint training, mean UPT):
  0.2%~2%/-0.3%~6%/-4%~6% gains for Max rank 1/2/4, respectively, under RU≤39%;
  0.1%~4%/-0.5%~10%/-1.8%~12.22% gains for Max rank 1/2/4, respectively, under RU40%-69%;
  0.23%~9%/-0.2%~15%/-1%~17% gains for Max rank 1/2/4, respectively, under RU≥70%;
CSI prediction
  Baseline: non-AI prediction method
  Results (mean UPT):
  3 sources observe gains of 0.7% ~ 7.0% over baseline
  2 other sources show loss of about -0.1%~-17%
  Observation: The performance gain for the current evaluated sub-use cases is not that promising

## Slide 4
Key outcome of study in RAN1
Summaries/recommendations
There is no consensus on the recommendation of CSI compression for normative work, with reasons including at least the following:
  Trade-off between performance and complexity/overhead
  Issues related to inter-vendor training collaboration
There is no consensus on the recommendation of CSI predication for normative work, with reasons including at least the following:
  Lack of results on the performance gain over non-AI/ML based approach and associated complexity
For AI-based beam management, from RAN1 perspective, at least the following are recommended for normative work:
  Both BM-Case1 and BM-Case2
  DL Tx beam prediction for both UE-sided model and NW-sided model
  Necessary signalling/mechanism(s) to facilitate data collection, model inference, and performance monitoring for both UE-sided model and NW-sided model
  Signalling/mechanism(s) to facilitate necessary LCM operations via 3GPP signalling for UE-sided model
It is recommended to specify necessary measurement, signalling and procedure to facilitate training, inference, monitoring and/or other LCM operations for both direct AI/ML positioning and AI/ML assisted positioning, specifically:
  specify necessary signalling of data collection; investigate the necessity of other information for supporting data collection, and if needed, specify during normative work
  investigate on the necessity and signalling details of measurement enhancements, and if needed, specify during normative work
  investigate on the necessity and signalling details of monitoring method(s), and if needed, specify during normative work
Aspects have been studied for the general framework of AI/ML over air interface for one-sided models and two-sided models. However, no recommendation is achieved on which aspects for normative work, with reasons including at least the following:
  No conclusion on functionality based LCM vs. Model-ID based LCM
  No conclusion on model transfer/delivery, e.g. case y and case Z1~Z5

## Slide 5
Key outcome of study in RAN2
Summaries
Rel-18 SI is considered complete from RAN2 point of view.
  Data collection
  Data collection mechanisms are studied, e.g., logged MDT, immediate MDT, L3/L1 measurement, UAI, early measurement, LPP signallings
  Model transfer/delivery
  RAN2 analyzed different model transfer/delivery solutions, e.g. current status and gaps, potential RAN spec impacts
  The necessity/feasibility of model transfer/delivery is dependent on further RAN1 discussions/conclusions
  Mapping of functions to entities
  RAN2 analyzed the mapping between functions and entities per AIML use cases on UE, gNB and LMF side
  RAN2 identified the mapping between functions and OAM/CN, but did not study them as both are out of RAN2 scope
LCM related procedures
  Mechanisms on model/functionality control, model identification, UE capability reporting, additional condition, etc., are discussed, with some candidate solutions are identified
  For model identification and additional condition, the necessity/feasibility of is dependent on further RAN1 discussions/conclusions, and the candidate solutions are not fully investigated at RAN2

## Slide 6
Key outcome of study in RAN4
Summaries
  Test framework for two-sided model
  4 options of test decoder are considered, the clarification and pros/cons analysis of which are partially studied.
  Note: The testability of two-sided model relies on the feasibility of the testing option(s) which need further study.
  Test goal/metrics
  2 options of test goal are identified for selection depending on the test. Regardless of going with which test goal,
  potential test metrics related to performance requirement are considered for each use case.
  potential LCM procedure related to core requirement are also identified.
  Note: The testability/feasibility of specific test metric and LCM procedure may need further investigation
  Verification of generalization
  Generalization related test is considered, where a static TE configuration is taken as baseline.
Dataset generation
  3 options are identified for defining testing dataset for further study.

## Slide 7
Extension for temporal-spatial-frequency (TSF) CSI compression
For further exploring benefits of AI/ML on CSI compression, AI/ML model can learn time domain correlation of channels on top of spatial-frequency domain compression.
Past/historical information from previous slots are stored and used to compress/recover the CSI of the current slot
Performance of TSF-CSI
Further study on TSF CSI compression
  Performance evaluation
    Higher UE speed, generalization over UE speed, different training type, etc.
  Potential specification impact
    Robust mechanism when UCI missing, e.g., reset, re-transmission missing UCI, etc.
Initial results
  TSF-CSI compression can provide 14% addition gain on top of SF CSI compression, total 29% gain over R16
Chart: 
| R16 | SF | TSF | Ideal
FB, Rank ？ | 0.63 | 0.725 | 0.815 | 1
~29%
15%
Rank2 throughput gain, RU=80%, 80 bits
AI/ML model diagram of TSF-CSI compression
Motivation of TSF-CSI

## Slide 8
Views on the potential scope for Rel-19 AI/ML for air interface
Potential scope for normative work
Specify beam management using one sided model, including BM-case 1 (i.e. spatial-domain DL beam predication) and BM-case 2 (i.e. temporal DL beam predication) [RAN1, RAN2, RAN3]
DL Tx beam prediction for both UE-sided model and NW-sided model
  Necessary signaling and mechanism(s) to facilitate data collection, model inference and performance monitoring
Specify AI/ML based positioning using one sided model [RAN1, RAN2, RAN3]
Study and if necessary specify measurement, signaling and procedure to enable AI/ML for positioning accuracy enhancements
Specify necessary signaling and mechanism(s) to facilitate functionality-based LCM operations for UE-sided model [RAN2, RAN1]
Specify the corresponding core requirements [RAN4]
Potential scope for further study
Continue study CSI compression using two sided model [RAN1, RAN2, RAN3], including at least
  Training types for two sided model, including model transfer/delivery and dataset delivery
  Model ID based LCM, including model identification procedure
  Data collection from UE to NW, including high resolution ground-truth CSI
  Extension for temporal-spatial-frequency CSI compression
  Continue study the testability aspects [RAN4]

## Slide 9
Discussion on project management for Rel-19 AI/ML for air interface
Two potential options for project management for Rel-19 AI/ML for air interface
Option 1: One Rel-19 RAN1-led WI, including a study phase for items for further study
Normative work for beam management and positioning using one sided model
A study phase for CSI and RAN4 testability
    CSI using two sided model
    RAN4 testability aspects
    Study outcome captured in the same TR as Rel-18
Option 2: One R19 RAN1-led WI + one additional Rel-19 RAN1-led SI
RAN1-led WI: Normative work for beam management and positioning using one sided model
RAN1-led SI: Continue the study of CSI using two sided model, and RAN4 testability aspects
The RAN1-led WI and RAN1-led SI share the TUs allocated to AI/ML for air interface in each WG, e.g. share the 4 TUs in RAN1