## Slide 1
3GPP TSG-RAN Meeting #102 RP-233749
Edinburgh, Scotland, 11th – 15th December 2023
Agenda Item: 9.1.1.3
Source: Ericsson
Title: Duplex Evolution
Document for: Discussion, Decision

## Slide 2
RAN Chair’s Summary for RAN-P Rel-19 package

## Slide 3: Background
Sub-Band Full Duplex (SBFD) has been studied during a Rel-18 Study Item (SI).
  For both FR1 and FR2,
  Low power indoor to high power wide area cases considered,
  Various deployment scenarios studied.
Our analysis shows:
  Feasibility of SBFD is highly questionable for realistic outdoor, wide-area FR1 scenarios,
  potential uplink coverage improvements observed only when the system load is low in all co-existing networks in the same frequency band
After RAN #101 plenary, a potential set of objectives for Duplex Evolution in Rel-19 was proposed by the RAN Chair [1].

## Slide 4: Potential WI Objectives: RRC_IDLE/INACTIVE modes
The following potential objective was included regarding potential SBFD operation in RRC_IDLE/INACTIVE modes
  [Semi-static/dynamic] indication of time location of SBFD subbands to UEs [in RRC_CONNECTED mode]
The SI in RAN1 focused primarily on operation and performance of SBFD in RRC_CONNECTED mode
  Potential issues and performance for SBFD operation in RRC_IDLE mode including interference to PRACH have not been sufficiently studied, and motivation has not been clearly identified.
  No conclusions/recommendations for operation in RRC_IDLE/INACTIVE mode were drawn in the TR.
Hence,
Proposal 1: WI on SBFD should only consider CONNECTED mode. SBFD operation in IDLE/INACTIVE mode is out of scope.

## Slide 5: Potential WI Objectives: Dynamic SBFD
The following potential objective was included regarding dynamic time location of SBFD subbands, referred to as “dynamic SBFD”
  [Semi-static/dynamic] indication of time location of SBFD subbands to UEs [in RRC_CONNECTED mode]
During the SI, dynamic SBFD was studied,
  In dynamic SBFD, the transmission direction for semi-statically configured sub-bands is overridden to support DL transmission in an UL sub-band and/or UL transmission in a DL sub-band.
  Our analysis show that dynamic TDD supported by current specifications performs equally or better than dynamic SBFD
  No conclusions/recommendations were drawn in the TR.
Hence,
Proposal 2: WI on SBFD should only consider semi-static SBFD. Dynamic SBFD is out of scope.

## Slide 6: Potential WI Objectives: CLI handling schemes
The following potential objective was included regarding CLI handling schemes
  Specify enhancements for CLI handling:
    Support both the gNB-to-gNB co-channel CLI handling scheme(s) and UE-to-UE co-channel CLI handling scheme(s) (the detailed schemes are to be down-selected from those in TR38.858)
    The SBFD operation drives the CLI enhancements, which are expected to be applicable to the dynamic/flexible TDD operation but without dedicated optimization
gNB-gNB CLI:
  A major source of interference for SBFD is gNB-gNB CLI from both co-sited nodes and other-sites, particularly in WA macro networks
    TR addresses only co-channel (intra-operator) CLI handling, while adjacent channel (inter-operator) CLI is also a major source of interference for both SBFD and dynamic TDD.
  Addressing inter-operator CLI is not feasible; thus mitigating only cochannel (intra-operator) gNB-gNB CLI is not sufficient
  Benefit of CLI mitigation for small cell or indoor networks is questionable
UE-UE CLI:
  UE-UE CLI is much less of an issue compared to gNB-gNB CLI
    Rare that two UEs are simultaneously in close proximity, scheduled in opposite directions, and near cell edge
TR 38.858 contains high level description of multiple CLI handling schemes proposed by different companies
  Each one evaluated by only 1 or 2 sources, with inconsistent evaluation assumptions
Proposal 3:
In order to have a manageable WID, discussion is needed to narrow the scope of potentially supported CLI mitigation scheme(s) only to those that were evaluated among the discussed CLI handling schemes in the TR 38.858.
Proposal 4:
Propose to add the following note to the WID:
NOTE: CLI schemes should not assume changes to latency or data rate capabilities for existing interfaces, e.g., Xn, F1.

## Slide 7: RAN4 objectives
RAN4 will need to develop RF requirements for the gNB, following on from the SI
  For some requirements, such as blocking in SBFD slots, some further co-existence work may be required (due to the blocking signal coming from other operators gNB, not other operators UE)
Depending on RAN1 decisions, changes to physical channels across SBFD/non-SBFD slots or CSI reporting may necessitate updates to performance requirements
Depending on RAN1 decisions, UE-UE CLI measurements may necessitate measurement requirements or performance requirements
The assumption on at least adjacent channel co-existence between two operators being considered should be included and updated according to the discussion in RP-232895
Proposal 5: RAN4 scope should include:
gNB RF requirements
RRM requirements if necessary
Performance requirements if necessary

## Slide 8: Proposed TUs for the WI
Working Group | Proposed TUs
RAN1 | 2.0
RAN2 | 0.5
RAN3 | 0.5
RAN4 RF | 1.0
RAN4 RD | 0.5
Proposal 6: For the Duplex Evolution WI, adopt the above proposed TUs for different working groups.

## Slide 9: Proposed WID objectives
Potential objectives:
  For subband non-overlapping full duplex (SBFD) operation at gNB side within a TDD carrier
    [Semi-static/dynamic] indication of time location of SBFD subbands to UEs [in RRC_CONNECTED mode]
    Semi-static indication of frequency domain location of SBFD subbands to UEs [in RRC_CONNECTED mode]
    UE transmission and reception behavior and procedures in SBFD symbols and/or non-SBFD symbols
    Note: followings are assumed based on TR 38.858
      SBFD operation Option 4
      Coexistence between legacy UEs and SBFD aware UEs in the cell operating SBFD at gNB side
      SBFD scheme within a single configured DL and UL BWP pair with aligned center frequencies
      Up to one UL subband for SBFD operation in an SBFD symbol (excluding legacy UL symbol/slot) within a TDD carrier
    At least adjacent channel coexistence between two operators should be considered as a minimum.
  Specify enhancements for CLI handling:
    Support both the gNB-to-gNB co-channel CLI handling scheme(s) and UE-to-UE co-channel CLI handling scheme(s) (the detailed schemes are to be down-selected from those schemes evaluated by simulations in TR38.858)
      NOTE: CLI schemes should not assume changes to latency or data rate capabilities for existing interfaces, e.g., Xn, F1.
    The SBFD operation drives the CLI enhancements, which are expected to be applicable to the dynamic/flexible TDD operation but without dedicated optimization
  At least adjacent channel co-existence between two operators should be considered as a minimum [RAN4, RAN1]
  RF requirements for SBFD operation at gNB
  RRM requirements for SBFD operation at gNB
  Performance requirements, if necessary, for SBFD operation at gNB
Proposal 7: Adopt the above proposed WI objectives for Duplex Evolution. New proposed objective text highlighted in green. Proposal in blue to be updated as needed.

## Slide 10: References
RP-232745 Summary for RAN Rel-19 Package: RAN1/2/3-led; for RAN #102 Plenary, Edinburgh, December 2023