## Slide 1: General views on RAN4 Rel-19
NTT DOCOMO, INC.
3GPP TSG RAN #102
Edinburgh, Scotland, December 11-15, 2023
Agenda Item: 9.1.4.1
Document for: Discussion
RP-233750

## Slide 2: Overview
As of Rel-18, 5G/5G-Advanced has been specifying many features to improve performance and enhance usecases
From RAN4 perspective, following further enhancements from Rel-18 should be treated in Rel-19 to improve the NW versatility
  NW performance improvement perspective
    FR1 3Tx/6Rx requirements for handheld UE
    FR2 MPR requirements improvement for intra band CA
    FR2 Intra+Inter UL CA with different frequency bands for PC1/2/3/5
    Performance requirements of MMSE-IRC receiver for NR BS
    FR2 RRM delay reduction enhancements
    HO with PSCell requirements for new scenarios
  NW availability improvement perspective
    100 km coverage support for HAPS TDD
    BS RF requirements for femtocell/home gNB for FR2

## Slide 3: Summary for each topic
FR1 3Tx/6Rx requirements for handheld UE
FR2 MPR requirements improvement for intra band CA
FR2 Intra+Inter UL CA with different frequency bands for PC1/2/3/5
Performance requirements of MMSE-IRC receiver for NR BS
Topic | Motivation | Priority
1 | Further enhancement on fundamental UE form factor (Handheld UE) is important. Especially for 3Tx, due to the limitation of 2Tx until Rel-18, UE supporting UL MIMO in single carrier needs to do non-UL MIMO in UL CA. | Middle
2 | MPR for intra-band CA is large and hence it is difficult to keep intra-band CA in practice (e.g., switching to single cell operation around cell edge), and also difficult to use joint scheduler for multi-cell scheduling. | High
3 | New spectrum assignment of 26/40GHz is expected to be done by the end of March 2026 in Japan. FR2 Intra+inter band UL CA is possbile configuration for future deployments. | High
4 | Considering the expansion of HPUE, BS MMSE-IRC receiver is more important than LTE era. In addition, the standardized performance requirements are necessary to introduce multi-vendor architecture smoothly. | High
5 | FR2 RRM delay is relatively long, thus delay reduction can make deployment and operation easier. It results in FR2 area expansion in the real NW. | High
6 | In order to fully utilize HO with PSCell in commercial network, the dropped scenarios should be specified and the workload may not be high. | Low
7 | HAPS operation in TDD band is attractive from operator point of view, and expansion of frequency ranges for HAPS will be discussed in WRC-23. The necessary requirements should be discussed in advance. | High*
8 | NR FR2 femto has not yet been specified and output power regulation in Japan is based on FR1 femtocell/home BS without technical considerations. The appropriate Tx power needs to be discussed from performance, implementation and feasibility point of view. | High*
FR2 RRM delay reduction enhancements
HO with PSCell requirements for new scenarios
100 km coverage support for HAPS TDD
BS RF requirements for femtocell/home gNB for FR2
*It can be discussed without a new WI (i.e., addressed in TEI)

## Slide 4: UE RF enhancements
FR1: 3Tx/6Rx for Handheld UE
  Until Rel-18
    For 3Tx, WI was approved to study 1Tx+2Tx for handheld UE in Rel-18, but no normative work for handheld UE in Rel-18.
      UE supporting UL MIMO in single carrier needs to do non-UL MIMO operation in UL CA.
    For 6Rx, it had been one of candidates for Rel-18 scope discussion, but it was dropped.
  Our view on Rel-19
    Specify 1Tx+2Tx CA/DC for handheld UE (1Tx FDD+2Tx TDD with 1CC per band)
    Specify 6RX requirements for handheld UE (n77/n78/n79)
FR1: Power domain enhancement (Ref: RAN1 led, but RAN4 related)
  Until Rel-18
    UE Tx power availability is important to determine proper UL scheduling
    Especially, with high-power UE and multi-carrier UL being deployed, it is expected that UEs adjust its maximum transmit power in a dynamic manner to e.g., compliant with SAR
      Although deltaPPowerclass reporting can be supported in Rel-18, P-MPR reporting for FR1 is not supported until Rel-18
      Even if deltaPPowerclass is supported, it is likely to be as instantaneous information. No information for future power availability is to be supported
  Our view on Rel-19
    Specify enhancements by which NW-side awareness on UE power availability is improved, e.g.,
      Specify P-MPR reporting for FR1 in Rel-19
        Additional restriction of the reported value can also be studied (e.g., when the reported P-MPR is expired)
      Study, and if needed specify, ΔPPowerClass and P-MPR reporting with additional information, e.g.,
        Timing when the reported ΔPPowerClass and P-MPR are expired

## Slide 5: UE RF enhancements
FR2: Improving MPR for intra band CA
  Until Rel-18
    MPR for intra-band CA is large and hence it is difficult to keep intra-band CA in practice (e.g., switching to single cell operation around cell edge).
    FR2 CA MPR is defined based on not only UL CBW but also DL CBW (i.e., cumulative aggregated channel bandwidth), and thus 1UL/xDL CA operation needs large MPR.
    Due to such switching between intra-band CA and single cell operation, it is difficult to use joint scheduler for multi-cell scheduling instead of per-cell scheduler in practice
  Our view on Rel-19
    Consider whether MPR for FR2 intra band CA can be improved.
      Study whether MPR for FR2 intra band CA can be defined based on only UL CBW (i.e., independent from DL CBW)
FR2: Intra+Inter UL CA with different frequency bands with IBM for PC1/2/3/5.
  Until Rel-18
    Inter band UL CA with different frequency bands and 1CC in each band for PC1/2/3/5 was introduced(e.g., n257A+n259A).
  Our view on Rel-19
    Specify intra+inter band UL CA with different frequency bands with IBM
    Power class: PC1/2/3/5, Example band combination: n257I+n259M
UL
DL
UL CBW
DL aggregated CBW
Cumulative aggregated CBW(CABW)
→ MPR is defined based on CABW

## Slide 6: RRM/Demod enhancements
In Rel-18, many candidates were proposed and discussed but many items were dropped because of limited TU
Following dropped items are considerable from operator point of view, thus should be revisited
  Demod
    Performance requirements of MMSE-IRC receiver for NR BS
      Considering the expansion of HPUE, BS MMSE-IRC receiver is more important than LTE era
      In addition, the standardized performance requirements are necessary to introduce multi-vendor architecture smoothly
  RRM
    FR2 RRM delay reduction enhancements
      In Rel-18, some of the delay reduction mechanisms has been specifying in separate WIs but a lot of candidates were dropped since time limitation
      FR2 RRM delay reduction should be focused on as one specific WI to improve FR2 utilization in real NW
    HO with PSCell requirements for new scenarios
      Considering real NW deployment, from NR-SA to NR-DC can be the candidate scenario
      In order to fully utilize HO with PSCell in commercial network, the dropped scenarios should be specified

## Slide 7: 100 km coverage support for HAPS TDD
Views on Rel-18
  HAPS is expected as a means of expanding coverage
  According to the current TS 38.104, NR operating band n1 can be applied for HAPS operation as below
    5.2 Operating bands (TS 38.104 V18.1.0)
      NR is designed to operate in the operating bands defined in table 5.2-1 and 5.2-2.
      NR operating band n1, which is defined in Table 5.2-1, can be applied for HAPS operation.
  From operator’s point of view, it is important to increase choice for HAPS bands not only FDD but also TDD e.g., Band 34/n34 based on the need taking the outcome of WRC-23 below into account
Related ITU-R discussions
  Only 2GHz is allowed in the current RR
  Expansion of frequency ranges for HAPS will be discussed in agenda item 1.4 in WRC-23
HAPS
GW
UE
UE-HAPS-GW-gNB:
100km
gNB
20km

## Slide 8: 100 km coverage support for HAPS TDD
RAN4 spec impact especially for TDD band
  Although the RAN1 spec (TS 38.211) already specified PRACH format 1 which can cover propagation distance of UE-HAPS-GW-gNB (about 100 km), the current RAN4 BS spec (TS 38.104) does not define it for FR1. Also, 3ms UL duration for PRACH format 1 needs to be covered by additional TDD patten
  Since the existing TDD patterns specified in A.1.2 of 38.101-4 cannot support 100 km coverage due to lack of guard symbols, additional TDD pattern with more guard symbols will be necessary
  This topic can be specified in TEI without a new WI.
PRACH format 1 for FR1
Additional TDD pattern

## Slide 9: BS RF requirements for femtocell/home gNB for FR2
Views on Rel-18
  Femtocell/home BS is expected as a means of extending coverage indoors at lower cost and power than small-cell base station e.g., Local area BS
  While NR FR1 Home BS was specified as a category of Local Area BS in RAN#98 [ref.RP-223298], NR FR2 femtocell/home has not yet been specified and output power regulation in Japan is based on FR1 home(LA) BS without technical considerations
  In order to accelerate high-speed/capacity operation, FR2 femtocell BS should be specified
RP-223298: CR for 38.104: define home class as one kind of LA BS

## Slide 10: BS RF requirements for femtocell/home gNB for FR2
RAN4 spec impact
  To specify related BS RF requirements, especially the appropriate Tx power needs to be discussed from performance, implementation and feasibility point of view
    When RF requirements(including Tx power) don' t impact the specifications(TS38.104, TS38.141-2), FR2 femtocell can be specified in TEI without a new WI similarly to FR1 femto.