## Slide 1: Satellite operator priorities for NR NTN Evolution in Release 19
Viasat, Inmarsat, Omnispace, Ligado, Skylo
11-15th Dec 2023, 3GPP TSG RAN#102, Edinburgh
RP-233782

## Slide 2: Introduction and General Views
NTN is a reality now, with networks being deployed as we speak.
Initial focus of deployments and products has been NB-IoT NTN in FR1, but systems will evolve in time
NB-IoT NTN devices are being released to the market, even before the Release 17 and 18 work has been fully finalized
  NB-IoT NTN was slightly rushed to market with a shorter Work Item phase in R17, this achieved the proposed goal of meeting market demand, but meant some aspects were missed.
We must focus on:
  Features that ensure better system efficiency based on learnings from field
  Features that facilitate deployment and ROI
Release 19 is likely the last chance to improve what’s missing before too many products are already on the market.

## Slide 3: RAN123 NR NTN Operator Priorities
NR NTN
UL Capacity/Throughput enhancements [RAN1]
DL Coverage Enhancements [RAN1]
Multicast and Broadcast Data Transmission Support [RAN2, RAN3]
Robust DL Notification Alert [RAN1, RAN2]

## Slide 4: Focus on Capacity Improvements - Rationale
Network and System capacity will be the most important and fundamental factor for NTN systems after link reliability
Network Capacity directly affects economics and user experience
Coverage improvements typically lead to capacity loss – It’s a trade-off
Most new and emerging non-3GPP satellite communication systems already support modes of operation geared at maximizing system capacity over large, uniform coverage areas, by:
  including code-domain multiplexing (e.g. CDM/OCC/CDMA) on top of other existing methods
  allowing multiple concurrent transmissions to/from numerous Users in overlapping or partially overlapping time-frequency resources, in many cases in a partially- or fully-untimed manner
  minimizing the required signalling for users to access the network and initiate a data transmission
3GPP NTN Solutions must be able to support equal or better capacity economics, in order to outmatch other competing non-3GPP solutions at scale

## Slide 5: Uplink Capacity Enhancements for NR NTN
Objectives:
Specify DFT-s-OFDM PUSCH enhancements via Orthogonal Cover Codes (OCC), including initial access [RAN1]:
  Targeting 6 to 12 times capacity improvement compared to legacy, taking into account realistic impairments (e.g. Doppler, time variation, phase distortion) and minimizing impact on emissions [RAN1]
  Specify necessary signalling, if needed [RAN2]
  Update RF requirements accordingly if needed [RAN4].
  Note: The orthogonal cover codes are across OFDM symbols and/or within an OFDM symbol.
Specify improved mechanisms for sporadic access (i.e. contention based PUSCH) to a pool of shared resources [RAN1/2]
  FFS PUCCH enhancements, if needed [RAN1]
Intent/Assumptions:
The intent is not to replace MU-MIMO capability but to improve system capacity.

## Slide 6: DL Coverage Enhancements & Robust DL Notification Alert for NR NTN
We identify three gap areas, in terms of DL coverage:
  Beam Hopping, Power Sharing and Frequency Reuse - Improved supportability of “beam hopping” (i.e. time-domain scheduling of satellite beam illumination based on signalled schedule or dynamic demand)
    Flexible and Dynamic scheduling of satellite beams in both space (beam tier/footprint) and time domain according to Signalled and On-Demand schedule.
    Relaxation of Cell transmission periodicity (or receiving) frequently over time, also accommodating payload dynamic re-configuration constraints. These can also be beneficial for IoT NTN (e.g. Cell DTX).
    Dynamic beam combining and simul-casting of specific transmissions across beams for one or multiple Cells.
    MU-MIMO of UE groups in different beams, to allow for efficient FRF=1 (same frequency), whilst minimizing interference.
  Coverage gaps between different L1 channels – Coverage performance and margins are different for different L1 channels (e.g. PDSCH, PDCCH, etc). A number of companies have reported that there are major gaps in coverage in certain channels.
  Paging/Notification of User in deep coverage – Introduce a mechanism for the network to notify either all users in a given cell, or a specific subset of users (>=1) in deep coverage that DL data is available (e.g. for emergency broadcast, paging requiring user action)

## Slide 7: DL Coverage Enhancements - Beam Hopping
Due to system limitations, it may not be always possible to illuminate all beams of a given satellite coverage area, e.g.:
  Total Payload Power Budget – i.e. how much max power the payload can draw and use at any given instant of time (t)
  Beamformer Capacity – how many beams can the beamformer physically form at any given instant of time (t)
  Channelizer Capacity – esp. for transparent payloads, how many channels can be mapped to beam footprint at any given instant of time
Demand is not equal or constant across the coverage area – varies over time and geography
Beam hopping consists of illuminating different beams at different time instants in a Time-Domain pattern (also called “time-coloring”)
With Beam Hopping, Satellite Cells can be:
  Dynamically “loaded” depending on localized demand – beam dwell time and frequency depends on demand in each Virtual Cell
  Illuminated in a pre-signalled sequence that the system can broadcast in advance
5G NR already supports this mode to some extent, however:
  Despite 5G NR discrete signalling, there are some constraints to expected periodicity and persistence, which would prevent more relaxed beam hopping schedules (.e.g turning off cells temporarily)
  The Cell-per-satellite-beam case is left to implementation
    gNB scheduler(s) need to be coordinated
    No signalling to UEs
Beam illumination over Time (ms)
Demand-based beam/cell hopping
High demand cell
Low demand cell

## Slide 8: Multicast and Broadcast Support for NR NTN
Rationale:
Satellite is by nature a broadcast medium, that can quickly reach very large coverage areas even when terrestrial networks are down.
Radio resource density per km^2 of NTN systems is much, much smaller than TN
Delivery of same data to a very large UE population in the same area via Unicast is not scalable (resource requirement scales with the number of UE, which for NTN with large coverage areas per-cell is simply not viable!)
With Multicast/Broadast, service delivery becomes more and more efficient with more and more UE are targeted!
Use Cases include (but not limited):
Emergency broadcast messaging (e.g. EW4All)
Public safety communications (e.g. such as first responders, emergency services, disaster response teams) and Other Group Communications: media and news network teams exchanging information during a news coverage event, private citizens within a closed communications group.
  Services will include group messaging, group data and file sharing, group PTT voice, real-time voice (group call), one-to-many video streaming, group video call, etc
Firmware and configuration delivery (for IIoT, Automotive, UAV/UAM, etc)
Content Delivery (Automotive, UAM, Aero, Maritime
Source: https://www.un.org/en/climatechange/early-warnings-for-all
Multicast/Broadcast is a key aspect of satellite networks, and a very low hanging fruit which can significantly improve the addressable market and quality of services provided via NTN

## Slide 9: Multicast and Broadcast Support for NR NTN
Assumptions:
No impact to physical layer channels
Some liaison with SA might be required
Objectives:
Focus should be on supporting group communication and basic content delivery
Focus on identifying minimum gaps to support Broadcast messaging and data delivery [RAN2, RAN3]
Address potential mismatch between the targeted broadcast service area and the NTN radio cell coverage given that NTN radio cells may be larger than TN radio cells [RAN2, RAN3]
Specify minimum enhancements to support multicast in connected mode over GSO and NGSO (e.g. latency, mobility) [RAN2]

## Slide 10: RAN4 NR NTN Operator Priorities
Non-spectrum:
NR less than 5 MHz – At least enabling support for 3 MHz channel BW and 12 PRB transmission, as already specified by NR_FR1_lessthan_5MHz_BW also for NTN bands. This is critical to enable NR NTN deployments within the context of existing non-3GPP services, as well as to support EIRP limited satellites and maximize frequency reuse efficiency.
HPUE for NR NTN – For all FR1 NTN bands, with support for PC2 (+26 dBm), PC1.5 (+29 dBm) and PC1 (31 dBm), reusing existing TN assumptions for FDD HPUE
4RX for NR NTN – To improve receive performance and align NR NTN UE with TN specification and requirements.
Better Support of Fragmented Spectrum - To accommodate situations where the existing legacy services may interrupt a 5G NR channel allocation, requiring 5G NR NTN services to be scheduled around
Spectrum:
Extended L-band for NR NTN (FR1) – Support of Extended L-band for NR NTN as [n254]

## Slide 11: NR NTN less than 5 MHz
Initial NR NTN deployments will have to coexist with existing non-3GPP satellite services
Furthermore, satellites will still have limited power and will be largely EIRP-limited
Reduction of the minimum BW required can facilitate with:
  Early NR NTN deployment around existing services
  Support of EIRP-limited satellite assets
  Easier frequency resource management and reuse
As a minimum, reuse existing TN assumption of support down to 12 PRB with no further impact to PSS/SSS and PBCH puncturing.
  Potentially up to 5 dB PBCH link budget loss has been identified due to puncturing
  Clarify link budget loss for NTN and consider techniques to recover PBCH performance loss
  Allow deployment of 12 PRB SSB within a larger system/channel BW where other services may exist, resulting in fragmented spectrum
  Consider if further reduction could be achieved at least for certain physical layer channels (i.e. no impact to PSS/SSS)

## Slide 12: HPUE support for NR NTN
Background:
Current NTN systems in are both coverage and capacity challenged in UL due to the tight link budget, especially when taking realistic antenna gain assumptions (e.g. -5.5 dBi gain)
Current solutions to improve coverage are mostly based on repetitions, which severely affect system capacity.
This issue was raised during RAN#97 and later RAN#99 and was postponed to Rel-19.
Satellite UE transmission regulation allow transmission powers up to 15 dBW for hand-held type terminals (e.g. satellite phones) and far higher for non-handheld. 3GPP should better align with what is allowed within the current satellite regulatory framework.
The lack of this capability will be severely limiting for a number of use cases in upcoming NR NTN deployments
Objectives:
Taking reference NTN bands n255, n256 the n254 and upcoming Extended L-band [n253] into consideration:
For NR NTN UEs: Specify support for PC2 (+26 dBm) for smartphone form factor; PC1.5 (+29 dBm) and PC1 (+31 dBm) at least for non-smartphone form factor.
Consider aspects related to duty cycle to control Specific Absorption Rate (SAR) for smartphone applications.
Consider the introduction of New VSAT power classes for FR1 as well (similar to current legacy satcom systems)

## Slide 13: Thank You!