## Slide 1: Satellite operator priorities for IoT NTN Evolution in Release 19
Viasat, Inmarsat, Omnispace, Ligado, Skylo
11-15th Dec 2023, 3GPP TSG RAN#102, Edinburgh
RP-233783

## Slide 2: Introduction and General Views
NTN is a reality now, with networks being deployed as we speak.
Initial focus of deployments and products has been NB-IoT NTN in FR1, but systems will evolve in time
NB-IoT NTN devices are being released to the market, even before the Release 17 and 18 work has been fully finalized
  NB-IoT NTN was slightly rushed to market with a shorter Work Item phase in R17, this achieved the proposed goal of meeting market demand, but meant some aspects were missed.
We must focus on:
  Features that ensure better system efficiency based on learnings from field
  Features that facilitate deployment and ROI
Release 19 is likely the last chance to improve what’s missing before too many products are already on the market.

## Slide 3: RAN123 IoT NTN Operator Priorities
IoT NTN (focus on NB-IoT NTN)
Network Capacity Enhancements [RAN1, RAN2]
Network-Controlled/Steered Anchor-to-Anchor Carrier Switching [RAN2]
Efficient Multicast and Broadcast Data Transmission Support [RAN2]
Avoid sending UE capability update during TAU update upon TN to NTN mobility [RAN2]
5GC Support for IoT NTN [RAN3, RAN2]

## Slide 4: Focus on Capacity Improvements - Rationale
Network and System capacity will be the most important and fundamental factor for NTN systems after link reliability
Network Capacity directly affects economics and user experience
Coverage improvements typically lead to capacity loss – It’s a trade-off
Most new and emerging non-3GPP satellite communication systems already support modes of operation geared at maximizing system capacity over large, uniform coverage areas, by:
  including code-domain multiplexing (e.g. CDM/OCC/CDMA) on top of other existing methods
  allowing multiple concurrent transmissions to/from numerous Users in overlapping or partially overlapping time-frequency resources, in many cases in a partially- or fully-untimed manner
  minimizing the required signalling for users to access the network and initiate a data transmission
3GPP NTN Solutions must be able to support equal or better capacity economics, in order to outmatch other competing non-3GPP solutions at scale

## Slide 5: Network Capacity Enhancements for IoT NTN (NB-IoT)
NB-IoT NTN is already being deployed live at this very moment.
Current NB-IoT NTN system capacity is severely limited
The main limiting factors are:
  The heavy signalling and dependencies between UL and DL, especially on DL signalling
  The limit in number of simultaneous UE UL transmissions per TTI
  Lack of ability to handle concurrent MO UL transmissions (i.e. UL shared resource pooling) without explicit signalling and scheduling request, even when UE stil have a valid TA
Today we are also gated by DL capacity, due to the larger signalling overhead in the downlink (up to ~53%), and the tight coupling between UL and DL signalling. This impacts predominantly UL-heavy traffic, such as Mobile Originated (MO) transmissions, which are the primary target of massive IoT and initial emergency messaging use cases supported by IoT NTN. In order to unlock the additional UL capacity, there is a need to reduce dependency on DL as much as possible.

## Slide 6: Network Capacity Enhancements for IoT NTN (NB-IoT)
UL transmission in shared resources:
Some techniques, such as Preconfigured Uplink Resource (PUR) with Shared Resource and the adoption of a Random Access procedure similar to 2-step RACH, already supported in 5G NR Small Data Transmission (SDT), could be used to achieve this and thus significantly increase the UL system capacity by reducing the reliance on DL signalling. However:
NB-IoT does not currently support 2-step RACH or similar procedures;
Dedicated PUR schemes rely on persistent periodic resources that have to be reserved for specific UE, thus significantly reducing the network capacity available to other users.
Current Contention Free Shared (CFS) PUR schemes currently only allow a limited number of pre-configured UL sequences (up to 2 for 12 tones, or less), thus significantly limiting the potential gains.
In addition, for single tone transmissions, NB-IoT does not allow the possibility of multiplexing multiple UEs in the same tone at all, which significantly reduces capacity in power-limited scenarios.
In the past 3GPP had studied the specification of Contention-Based schemes for PUR with Shared resources (CBS PUR), with the specification of additional signatures, based on CDM orthogonal cover codes, additional DMRS configurations, etc, which had shown the potential for significant gains in UL capacity.
  The Network should be capable of configuring a pool of UL resources that the UE can access in a contention-based way.
  Current legacy PUR procedures are incomplete and insufficient, EDT requires heavy signalling and is not applicable to the initial access.

## Slide 7: Network Capacity Enhancements for IoT NTN (NB-IoT)
Objectives:
Specify enhancements to enable multiplexing of multiple UEs (e.g. at least up to 4) in a single 3.75kHz or 15 kHz subcarrier via orthogonal cover codes for NPUSCH and NPRACH [RAN1]
  Multi-tone support should also be included (to allow scheduling flexibility and different transmission strategies depending on UE type)
  NOTE 1: The enhancements in this objective can be combined with the enhancements in the following objectives.
  NOTE 2: Impact of frequency offset shall be taken into account
Specify enhancements to existing PUR/EDT procedure to minimize the amount of necessary downlink/uplink signalling to complete a PUR/EDT transaction [RAN1, RAN2], e.g.
  UL transmission time/frequency resource pool to be configurable across one or more anchor/non-anchor carriers.
  RRC early data complete delivery
  Msg3 contention-based operation without PRACH and Random Access Response
  Consider primarily for Mobile Originated (MO) data transmissions
  NOTE 3: PUR/EDT enhancement may be used also independently from the use of OCC
Consider mechanisms to reduce the signalling required for UE initial access in a similar manner to existing 2-step RACH mechanisms supported for NR

## Slide 8: Network-Controlled/Steered Anchor-to-Anchor Carrier Switching for NB-IoT
Rationale/Background:
Satellite and satellite beam coverage areas are very large, with different beam sizes or tiers and will very likely include multiple NB-IoT NTN cells deployed as different carreirs in the same footprint
There are very common situations in which the network may need to move one or more UE between NB-IoT NTN carriers for load-balancing or frequency management purposes
There are also very common situations in which the network may want to instruct one or more UE to move between beams for mobility, coverage, frequency or load-balancing purposes
NB-IoT currently does not support CONNECTED_MODE mobility or any kind of Network-controlled mobility or load-balancing
A combination of multiple NB-IoT NTN Anchor and Non-anchor carriers may be deployed within any given satellite beam coverage area
NTN operators may have a constraint of being able to deploy only Anchor carriers in adjacent beams or within the same beam
Moreover, it is likely expected that additional Non-Anchor carriers associated with a given Anchor carrier are only deployed within the same beam, and that adjacent beams will mostly be associated with different Anchor carriers

## Slide 9: Network-Controlled/Steered Anchor-to-Anchor Carrier Switching for NB-IoT
Objectives:
Identify and specify NB-IoT enhancements to support an efficient mechanism for Network-controlled or steered anchor to anchor carrier switching for UE [RAN2]
  Including in Connected Mode
  Note : No impact on connected measurements
Identify and specify NB-IoT enhancements (e.g. SIB signalling) to allow the Network to support UE in carrier switching [RAN2]
  Include Anchor to anchor, anchor to non-anchor and non-anchor to anchor carrier switching
  Note: How carriers are mapped to same or different satellite beams is left to an Operator’s deployment considerations

## Slide 10: Multicast and Broadcast Support for IoT NTN
Rationale:
Satellite is by nature a broadcast medium, that can quickly reach very large coverage areas even when terrestrial networks are down.
Radio resource density per km^2 of NTN systems is much, much smaller than TN
Delivery of same data to a very large UE population in the same area via Unicast is not scalable (resource requirement scales with the number of UE, which for NTN with large coverage areas per-cell is simply not viable!)
With Multicast/Broadast, service delivery becomes more and more efficient with more and more UE are targeted!
Use Cases include (but not limited):
Firmware and configuration delivery (for IIoT, Automotive, etc)
Emergency broadcast messaging (e.g. EW4All)
Public safety communications (e.g. such as first responders, emergency services, disaster response teams) and Other Group Communications: media and news network teams exchanging information during a news coverage event, private citizens within a closed communications group.
  Services will include group messaging, group data and file sharing, group PTT voice, etc.
Source: https://www.un.org/en/climatechange/early-warnings-for-all

## Slide 11: Multicast and Broadcast Support for IoT NTN
Assumptions:
No impact to physical layer channels
Some liaison with SA might be required
Objectives
Identify and specify enhancement to current SC-PTM implementation with reduced signalling overhead and more flexible resource allocation, to improve efficiency and delivery times. [RAN2]
  Reduction of requirements for periodic service announcements (and corresponding UE monitoring requirement), i.e. only when data is actually available via on-demand paging
  Network-directed service delivery (removal of mandatory UE-driven joining requirement)
  e.g. semi-persistent scheduling, more flexible packet size and TBS
  Emergency broadcast message with priority – entire cell or sub-set of the UE in a cell
We think making Multicast/Broadcast work well on IoT NTN is a key aspect and a very low hanging fruit which can significantly improve the addressable market and quality of services provided via NTN

## Slide 12: RAN4 NTN Operator Priorities
IoT NTN
HPUE for IoT NTN - For all FR1 IoT NTN bands including especially for NB-IoT NTN, with support for PC2 (+26 dBm), PC1.5 (+29 dBm) and PC1 (31 dBm).
  Duty-cycle and SAR related aspects may need to be considered.
In-Band NB-IoT and eMTC – Currently, deployment of NB-IoT and eMTC within or in guard-band of 5G NR carriers is already supported for terrestrial networks, helping greatly improve spectrum usage efficiency. This is a key missing feature and low hanging fruit for NTN.

## Slide 13: HPUE support for IoT NTN
Background:
Current NTN systems in are both coverage and capacity challenged in UL due to the tight link budget, especially when taking realistic antenna gain assumptions (e.g. -5.5 dBi gain)
Current solutions to improve coverage are mostly based on repetitions, which severely affect system capacity.
This issue was raised during RAN#97 and later RAN#99 and was postponed to Rel-19.
Satellite UE transmission regulation allow transmission powers up to 15 dBW for hand-held type terminals (e.g. satellite phones) and far higher for non-handheld. 3GPP should better align with what is allowed within the current satellite regulatory framework.
The lack of this capability is currently severely limiting ongoing NTN deployments and use cases, which are starting with NB-IoT.
Objectives:
Taking reference NTN bands 255, 256, 254 and 253 into consideration:
For eMTC IoT NTN UEs (Cat M1): Specify support of UE Power class 2 (+26 dBm) for smartphone form factor; Power class 1.5 (+29 dBm) UE Power class 1 (+31 dBm) at least for non-smartphone form factor;
For NB-IoT NTN UEs (Cat NB1, NB2): Specify support for a new UE Power Class with MOP of +26 dBm; Power Class with MOP of +29 dBm) and Power Class with MOP of +31 dBm;
Consider aspects related to duty cycle to control Specific Absorption Rate (SAR) for smartphone applications (NB-IoT might be used for smartphones)
UE TX PA architecture may need to be analysed for NB-IoT
Consider the introduction of New optional VSAT power classes for FR1 as well (similar to current legacy satcom systems)

## Slide 14: Thank You!