## Slide 1: Proposals on RRM and UE demodulation enhancements for RAN4 led Rel-19 items
3GPP TSG RAN Meeting #102 RP-233785
Edinburgh, Scotland, December 11-15, 2023
Agenda Item: 9.1.4.3
Source: Ericsson
Title: NR RRM enhancements in Rel-19
Document for: Discussion

## Slide 2: Contents
RRM enhancement:
  FR2 measurement delay reduction
  UE power saving enhancements:
    eDRX for non-ReCap UEs and
    RLM/BFD relaxation for RedCap UEs
Demodulation enhancement
  Spatial channel model for MIMO requirement
  CSI Resource Indicator (CRI) requirements

## Slide 3: FR2 measurement delay reduction
Justification
FR2 measurement delay for layer-1 measurements (e.g. RLM/BFD/CBD, L1-RSRP etc) and layer-3 measurements (e.g. cell search, RSRP/RSRQ/SINR period) is much longer than in FR1 due to UE RX beam sweeping.
Rel-18 work on FR2 delay reduction is limited to SCell activation.
FR2 measurement delay increases execution of:
  RLM and link recovery procedures which rely on Layer-3 measurements
  mobility procedures which rely on Layer-3 measurements
Longer measurement delay causes more scheduling restriction resulting in throughput loss.
Wide range of UEs are expected to support simultaneous reception of reference signals (e.g. SSB, CSI-RS) from multiple beams and cells by means of utilizing multi-Rx chain/multi-panel implementation.
Objectives
  FR2 measurement delay reduction for layer-1 and layer-3 measurements [RAN4]
    Identify cases where FR2 delay can be reduced at least for the following layer-3 measurements (intra/inter-frequency/inter-RAT NR/CA/DC) applicable in all the relevant RRC states: RRC Idle, RRC inactive and RRC connected states:
      RRC idle/inactive: cell re-selection, including idle mode CA/DC measurements etc.
      RRC connected: RLM, beam management/link recovery procedure, cell search, RSRP/RSRQ/SINR, SSB index acquisition, CGI reading etc.
    Specify reduced measured delay requirements for the identified cases
  Specify if needed, signaling enhancement for the UE to meet the reduced FR2 delay requirements [RAN4, RAN2]
  Specify RRM performance requirements including test cases for the above core requirements [RAN4].
BS1
Cell change
BS2
Figure 1: Mobility procedures rely on layer-3 measurements

## Slide 4: UE power saving enhancements: eDRX for non-RedCap UEs
Justification
eDRX and relaxed RLM/BFD measurements enable substantial UE power saving without impacting network performance when used in certain scenarios.
In LTE eDRX requirements are specified for all types of UEs and in all RRC states.
eDRX requirements are specified for Redcap UE in both RRC idle and RRC inactive states.
eDRX requirements are specified for non-RedCap UEs only in RRC idle state; but they are missing in other relevant scenarios e.g. under RRC inactive state, small data transmission (SDT) etc.
Objectives
Specify eDRX requirements for non-RedCap UEs in Rel-19 for all the missing cases based on Rel-17 and Rel-18 eDRX procedures e.g. under RRC inactive state, SDT etc.
Specify RRM performance requirements including test cases for the above core requirements [RAN4].
eDRX cycle
Time
DRX cycle

PTW



Figure 2: Paging time window (PTW) of eDRX contains multiple DRX cycles

## Slide 5: UE power saving enhancements: RLM/BFD relaxation for RedCap UEs
Justification
RLM/BFD measurements for NR UEs can be relaxed under certain conditions e.g. low mobility, high SNR
  However, relaxed RLM/BFD requirements are not specified for Redcap
Objectives
Relaxed RLM/BFD requirements [RAN4]
  Identify cases where SSB/CSI-RS based RLM/BFD measurements can be relaxed for Redcap UE.
  Specify relaxed RLM/BFD requirements for Redcap UE for SSB/CSI-RS based RLM/BFD for the identified cases.
Specify RRM performance requirements including test cases for the above core requirements [RAN4].
SSB periodicity
Time
Example of SSBs used for relaxing RLM/BFD


Figure 3: UE sparsely uses configured SSBs for relaxed RLM/BFD measurements to conserve its power

## Slide 6: BS/UE demodulation proposals
The time available for demodulation topics should be checked carefully considering the time needed for RAN1-3 led items and RAN4 items.
Provisionally, around 1-2 objectives might be accommodated

## Slide 7: BS/UE demodulation proposals
Study and specification of spatial channel models (a.k.a. Clustered Delay Line, CDL) for MIMO requirements is the most promising proposal for demodulation
  Good MIMO requirements are essential for ensuring good return on investments in AAS/MIMO deployments
  CDL was not introduced into Rel-15 due to lack of alignment between companies and lack of time
  However, with TDL based requirements, some MIMO requirements, in particular multi-layer are not properly tested.
  In order to enable higher levels of MIMO performance, and especially to be ready for 6G, invest time now in aligning and making CDL work.
  Focus on a one or two requirements in Rel-19, e.g., UE PDSCH demodulation and/or PMI reporting requirements.

## Slide 8: BS/UE demodulation proposals
Specify UE CSI-RS Resource Indicator (CRI) reporting requirements with multiple CSI-RS resources configured
  CRI reporting was specified in Rel-15 NR, based on Rel-14 LTE CRI reporting.
  This reporting quantity is essential, but this requirement is missing in current CSI reporting requirement specifications and will enable improved CSI reporting performance.
  Rel-14 LTE CRI reporting requirement is a starting point.
  Targeting both FR1 and FR2.