## Slide 1: On 2RX XR UE item and related WFs
SOURCE:
TELECOM ITALIA, […..]
3GPP TSG RAN Meeting #102 RP-233797
Edinburgh, UK, December 11-15, 2023

## Slide 2: Status on “2Rx relaxation for XR wearable devices” after last plenary
Handheld smartphone UEs are excluded from any 2Rx relaxation for XR wearables.
  The default for non-RedCap XR-wearable UEs is 4Rx (for frequency bands where 4Rx is mandated).
  A non-RedCap XR-wearable UE can be considered for 2Rx relaxation (for frequency bands where 4Rx is mandated) if and only if:
    Intended to be worn on the human head;
    When in use, is intended to be supported only by/behind the ears and by a nose-bridge resulting in a constrained form factor with limited volume available for Rx chains;
  No other relaxation is being considered apart from number of Rx chains.
Recognize the importance of identifying these devices in the network, and potential network impact (e.g. performance, coverage, capacity) and UE impact
  Address the impacts to RF and OTA requirements for non-RedCap 2Rx XR devices, and their potential network impact (performance, coverage, capacity, etc…) and the mitigation techniques.
  It is assumed that there is a need for the network to clearly identify non-RedCap XR devices with 2Rx restriction.

## Slide 3: Important considerations by operators community
Common and increasing concern on relaxation of TX/RX requirements for NR devices (even on NTN side) that strongly harms network performance and QoS user perception
This particular XR Device reduction is a clear failure to properly design devices to ensure compliance with well-established and standardized RF performance criteria
  Unfortunate precedent that 3gpp allows this loophole, this MUST BE A single and unique exception to be NOT repeated anymore, since it is going to harm 3gpp standardization principles & philosophy, that made success of mobile comms since 2G onwards
As other categories of “bad performing” UEs, a way to early identify, segregate it and even to bar it inside our Nets have to be clearly specified by 3gpp
TRS-RX sensisitivity for this particular UE MUST BE SPECIFIED by ran4, or simply step back and use 4rx reqs or use simply tethering with normal smartphones/modems
  this last point is categorical

## Slide 4: Proposed WFs by operators community
The definition of XR devices applicable for 2Rx relaxation needs to be captured in the specification, in order to confine this particular case and to not propagate the exception
As other categories of “bad performing” UEs, a way to early identify, segregate it and even to bar it inside our Nets have to be clearly specified by 3gpp in ran2, ran4 and eventually CN/SA side
OTA, mainly TRS-RX sensisitivity for this particular UE MUST BE SPECIFIED by ran4, even if also TRP can be affected (e.g. TAS can be affected)
  this last point is categorical
  Otherwise, adoption of existing 4Tx/rx values by default or tethering usage ONLY

## Slide 5: Detailed WFs by operators community
The definition of XR devices applicable for 2Rx relaxation needs to be captured in the specification, in order to confine this particular case and to not propagate the exception
As other categories of “bad performing” UEs, a way to early identify, segregate it and even to bar it inside our Nets have to be clearly specified by 3gpp in ran2, ran4 and eventually CN/SA side
  early identification of these XR 2Rx Devices via ad-hoc Information Element in RRC signalling, using the same solution adopted for Cat.1bis 1Rx and RedCap (e.g for 5G SA)  RAN2 engagement
  Segregation and potential barring e.g. via dedicated UE category type, involving also SA/CT solutions
OTA, mainly TRS-RX sensisitivity for this particular UE MUST BE SPECIFIED by ran4,
  this last point is categorical
  Potential suggestion is conducted 4rx REFESENS

## Slide 6: Summary of proposed WFs
Proposal1 The definition of XR devices applicable for 2Rx relaxation needs to be captured in the specification, in order to confine this particular case and to not propagate the exception
Proposal2 Early identification of these XR 2Rx Devices via ad-hoc Information Element in RRC signalling, using the same solution adopted for Cat.1bis 1Rx and RedCap (e.g for 5G SA)  RAN2 engagement
  Segregation and potential barring via dedicated UE category type, involving also SA/CT solutions
Proposal3 OTA, mainly TRS-RX sensisitivity for this particular UE MUST BE SPECIFIED by ran4,
  this last point is categorical
  Potential suggestion is conducted 4rx REFESENS

## Slide 7: THANKS