## Slide 1: Considerations for R19 work on Ambient IoT
Philips International B.V.

## Slide 2: 5G support for ambient IoT
Ambient IoT = Ultra low power IoT  NB-IoT and LTE-M still too high energy consumption and peak power requirements.
Very useful for body-worn sensors, asset/patient tracking and inventory management, given the limited space for a good battery and (logistical) difficulties for recharging.  We need devices powered by energy harvesting, being either battery-less or with limited energy storage capability. This also reduces waste.

## Slide 3: Scope for release 19
Study phase to address indoor Ambient IoT use cases identified by SA1 in forthcoming TS (draft version in S1-233257)
  Inventory taking (=rUC1)
  Sensor data collection (=rUC2)
  Asset tracking (=rUC3)
  Actuator control (=rUC4)
Prepare foundations for related functional service requirements including:
  Communication between AIoT device and network (rUC1, rUC2, rUC3, rUC4)
  Periodic reporting (rUC2)
  Positioning/location services (rUC1, rUC3)
  AIoT device management (rUC1, rUC2, rUC3, rUC4)
Support Device Type A/B, as defined in TR 38.848
  Device Type C to follow in a later release
  Aim for communication bursts with about 2 Kbit/s throughput.
To address communication range of A/B Devices, we consider that topologies 2 and 3 will be valuable for these applications, as well as topology 1