## Slide 1: Proposal for a Rel-19 Irregular Channel BW Work Item
3GPP TSG-RAN Meeting #102 RP-233875
Edinburgh, Scotland, December 11-15, 2023

## Slide 2: Background
NR was supposed to be better in every way than LTE, but in reality, LTE allowed for higher spectral utilization for irregular channel bandwidths
Operators requested a solution for the channel bandwidths to the right, but so far there is none.
In addition to these FDD channel BWs, in the US there are many irregular licensed channel bandwidths in n41
Operator Requests from the SI

## Slide 3: Irregular channel bandwidth Study Item
Formally, the Study Item was titled “Study on Efficient utilization of licensed spectrum that is not aligned with existing NR channel bandwidths”
The SI included bandwidths that are not multiples of 5 MHz
The SI began in Rel-17 and concluded in Rel-18, but there has been no follow-on Work Item so far
The 100 kHz raster issue for UE Specific channel bandwidths surfaced during the Study Item, and its resolution clears the way to finalize some of the techniques covered in the Study Item Technical Report

## Slide 4: Techniques from the Study Item
Larger Channel BW than licensed BW
Overlapping channel bandwidths
  Overlapping UE CBWs from Network Perspective
  Combined UE CBW (one cell)
  Overlapping CA (two cells)
Of these, Larger Channel BW than licensed BW, and Overlapping UE CBWs from the Network Perspective have the least impact on the specs and UEs, and should be followed up on.

## Slide 5: Overlapping UE CBWs from Network Perspective
Regulatory requirement: No issue
UE performance degradation relative to minimum requirements: No issue
gNB complexity: gNB has to support the irregular channel BW (can also be implemented through RF combining of 2 channels)
UE complexity: No changes needed, supported by legacy UEs
UE throughput: UE throughput based on existing channel BWs (5MHz for holdings <10MHz, 10MHz for holdings <15MHz, etc.)
Spectral utilization: UE throughput based on existing channel BWs (5MHz for holdings <10MHz, 10MHz for holdings <15MHz, etc.)
Cell Spectral utilization: Entire spectrum holding can be used even only with legacy UEs
Network capacity: Entire spectrum can be used by multiplexing different UEs in the frequency domain
Legacy UE support: Legacy UEs supported
RAN1/2/4 Specification impact: RAN4 – BS requirements for new channel BW
From TR 38.844

## Slide 6: Larger CBW (one cell)
Regulatory requirement: Potential issue on the BS side, gNB filters will be needed depending on BS implementation.
UE performance degradation relative to minimum requirements: UE ACS and in-band blocking degradation. Possible impact on Rx sensitivity vs regular CBW, if single carrier Tx-Rx separation is not maintained.
gNB complexity: No changes needed if the BS can meet regulatory requirements with the RF front end of the wider channel BW. Otherwise, gNB has to support the irregular channel BW
UE complexity: No changes needed, supported by legacy UE
UE throughput: UE throughput based on how many RBs can be used
Spectral utilization: Depends on the usable number of RBs, single SSB needed
Cell Spectral utilization: Entire spectrum holding, but with wider guard bands than in the other methods, can be used even only with legacy UEs
Network capacity: Entire spectrum can be used by any UE
Legacy UE support: Legacy UEs supported
RAN1/2/4 Specification impact: RAN4 – BS requirements for new channel BW, possibly restrictions of the suitable scenarios. New asymmetric bandwidth combinations for UE are needed. However, these combinations would be “regular” BW combinations, so existing process.
From TR 38.844

## Slide 7: Proposal
Create a Release-19 Irregular Channel Bandwidth Work Item
  “Irregular Channel Bandwidth” refers to the licensed channel bandwidth, not necessarily the UE channel bandwidth.
Include overlapping channels from the network perspective
  Asses the impact on spectral efficiency of having SSBs in two slots for 6 and 7 MHz channels
Include Larger Channel BW than Licensed BW
Include solutions for both FDD and TDD bands