## Slide 1: Proposal for a Rel-19 FR1 High Order Modulation Work Item
3GPP TSG-RAN Meeting #102 RP-233876
Edinburgh, Scotland, December 11-15, 2023

## Slide 2: Proposals
Add 4 Layer DL 1024 QAM for FWA in FR1
  Although RAN1 specs cover 4L DL 1024 QAM, currently only 2 Layer DL requirements exist for 1024 QAM in the RAN4 specs
    BS EVM requirments needed
    UE Performance requirements needed
Add 8 Layer DL 256 QAM in FR1
  Codebook defined in RAN1 specs
  UE performance requirements needed
Add 4 Layer UL 256 QAM in FR1
  Codebook defined in RAN1 specs
  UE requirements including 4Tx MPR needed