## Slide 1
RAN WG3 Chair: Yin Gao
RAN WG3 Vice-Chairs: Angelo Centonza, Gen Cao
RAN3 Secretary: Seonggu Shim
Status Report for RAN WG3
3GPP TSG RAN #104, Shanghai, China
Jun 17th – 20th, 2024
RP-240867

## Slide 2: Executive Summary
Total 1234 Tdocs at submission deadline (excluding LSin received from other groups) in Q2
  9% LSs and related documents
  32% Maintenance: Rel-18 & earlier
  2% Rapporteur Corrections: Rel-18
  56% Documents to Rel-19 WIs
Updated endorsed guidelines for f2f meeting with 1-way remote access: R3-243003
TR30.531 Work Plan and Working Procedures - RAN WG3 was updated and approved in R3-243004
R19 WIs/SIs discussion starts in RAN3.
RAN3 #123bis | Apr 15th – 19th, 2024 Changsha, China
RAN3#124 | May 20th – 24th, 2024 Fukuoka, Japan
RAN #104 | Jun 17th – 20th, 2024 Shanghai, China

## Slide 3: Tdoc submitted to RAN3
In R19, the total number of contributions around 660 (less than R18) for each RAN3 meeting seems reasonable.
Notes: w

## Slide 4: Tdocs for each Topic

## Slide 5: Tdocs for each Topic

## Slide 6: Overview of RAN3-led Rel-19 NR SI/WIs
UID | Name (acronym) | Acronym | Target completion | Old % (the same as in WI/SI SR) | WID | New % | Change or comments
1021092 | Data collection for SON (Self-Organising Networks)/MDT (Minimization of Drive Tests) in NR standalone and MR-DC (Multi-Radio Dual Connectivity) Phase 4 WI | NR_ENDC_SON_MDT_Ph4-Core | 25/09/2025 | 0% | WID: RP-234038 | 15% | 
1020083 | Study on enhancements for Artificial Intelligence (AI)/Machine Learning (ML) for NG-RAN SI | FS_NR_AIML_NGRAN_enh | 25/09/2024 | 0% | WID: RP-240323 | 80% | 
1020082 | Study on additional topological enhancements for NR SI | FS_NR_WAB_5GFemto | 25/09/2024 | 0% | WID: RP-240319 | 70% | 
WI: Black SI: Blue
Completed WI/SI: Red

## Slide 7: RAN3 CRs to RAN
List of RAN3 CRs to RAN in RP-240868, which includes:
  135 CRs were agreed in Q2 for TEI corrections.
    3 Rel-16: 3 Cat.F CRs
    10 Rel-17: 8 Cat.F CRs, 2 Cat.A CRs
    122 Rel-18: 89 Cat.F CRs, 8 Cat.A CRs, 6 Cat.B CRs, 19 Cat.D CRs
      2 pre-R18 Non-Backwards-Compatible (NBC) CRs
        Rel-16: R3-243035(Cat.F), Rel-17 mirror CR: R3-243036(Cat.A)
        (Here is how 3GPP works with NBC changes)
    8 Cat.B TEI18 CRs with TEI identifier
      [2Rx_XR_Device] R3-243031, R3-243038, R3-243044, impact on RAN2 (R2-2405926, R2-2405647) and RAN4 (R4-2407298)
      [SDT_ReleaseEnh] R3-243043, impact on RAN2 (R3-243042 as draft CR for stage 2 TS38.300 -> R2-2406049, R2-2405648)
      [ECIDQualTimeStamp] R3-243077, R3-243078, impact on RAN2 (R3-243079 as draft CR for stage 2 TS38.305->R2-2406052)
  21 endorsed draftCRs to RAN2 specs.

## Slide 8: Experience for GTW Usage in f2f meeting
RAN3 has 1 main meeting room and 2 breakout rooms in RAN3#123bis, while has 1 main meeting room and 1 breakout room in RAN3#124. Considering the current work load, 1 main meeting room and 1 breakout room seems sufficient for RAN3.
In general, the number of remote participants for main session is quite limited, less than 8. The audio device test for remote access was performed before daily session starts.
MCC and IT support during the meeting are sufficient.

## Slide 9: R19 SON/MDT WI
Progress in the last quarter
MRO Enhancements
  MRO for LTM:
    Work on scenarios of near failure LTM.
    Work on scenarios for the differentiation of too early LTM, too late LTM and LTM to wrong cell.
    RAN3 to prioritize MCG LTM over SCG LTM.
    RAN3 to discuss enhancements related to the information of RACH-less access and RACH-based access from UE related to MRO for LTM.
  MRO for CHO with Candidate SCG(s):
    MRO for CHO with candidate SCG failure and near failure cases.
    RAN3 focuses on NR-DC for MRO for CHO with candidate SCG in R19.
    R19 SON/MDT solution discussion is based on R18 work.
    RAN3 will start with the failure scenarios with UEs configured with CHO with candidate SCGs.
  MRO for S-CPAC:
    Work on the scenarios of failure in S-CPAC. The optimization of non-failure scenarios (e.g., near failure and ping-pong) is not excluded.
    CPAC failure scenarios and detection mechanism captured in stage2 used as baseline.

## Slide 10: R19 SON/MDT WI
Progress in the last quarter
SON/MDT for NTN and Slicing
  Intra-NTN Mobility:
    Logged MDT enhancement based on scenarios to be worked first, work on immediate MDT if time allows.
    MRO mechanisms for intra-NTN should be addressed based on failure scenarios first, work on near failure scenarios later.
    Take the connection failure scenarios in §15.5.2.2.2 of TS 38.300 as starting point with necessary update, if needed, in MRO for intra-NTN mobility.
    MRO for intra-NTN mobility shall consider the following trigger conditions:
      -Measurement-based trigger condition;
      -A time-based trigger condition;
      -A location-based trigger condition;
      -A time-based and Measurement-based combined trigger condition;
      -A location-based and Measurement-based combined trigger condition;
    Do not consider MRO for feeder link switch.
    MRO for intra-NTN mobility shall consider both conditional and non-conditional intra-NTN handover.
  Network Slicing:
    Both the logged MDT and immediate MDT enhancements based on scenarios to be worked.
    Work on the Slice aware MRO scenarios.
    RAN3 to support immediate MDT measurements collection on specific area per slice(s).
    RAN3 to work on logged MDT enhancement for slice-based cell reselection.

## Slide 11: R19 SON/MDT WI
Progress in the last quarter
R18 leftovers
  RACH optimization for SDT:
    Work on scenario of RACH optimization for SDT first.
    There is no need for UE to report SDT configurations, e.g., RSRP threshold, data volume threshold, T319a, and other configurations.
  MRO for MR-DC SCG failure:
    Keep the following R18 agreement in R19: Support MRO for SCG failure in EN-DC, NGEN-DC and NE-DC scenarios.
    RAN3 focuses on NR-DC for MRO for CHO with candidate SCG in R19.
  MHI/UHI Enhancement for SCG Deactivation/Activation:
    Wait for RAN2’s progress.
Impacts and dependencies on other WGs
LS to RAN2 on the feasibility to support MRO for SCG failure in R19 in R3-242195.
Other important info
N/A

## Slide 12: R19 AI RAN SI
Progress in the last quarter
Network Slicing:
  In Rel-19, predicted information from CN to NG-RAN is not considered.
  Agree to improve the granularity of UE performance feedback in Rel-19 for slicing.
  Measured/predicted slice-level radio resource status, and measured/predicted slice available capacity can be transferred between NG-RAN nodes to assist AI/ML network slicing.
Coverage and Capacity Optimization:
  Initial progress about solution for CCO in the case of split architecture and non-split architecture.
  For non-split architecture, future CCO state can be derived via legacy mechanism or AI/ML techniques which is up to implementation.
  For split architecture, the standardization of AI/ML based future CCO state inference in the gNB-DU is not supported in R19, how to derive future CCO state is up to implementation in the gNB-DU, e.g., legacy or AI/ML.

## Slide 13: R19 AI RAN SI
Progress in the last quarter
R18 Leftover:
  Energy Saving Enhancements:
    Measured Energy Cost can be transferred from DU to CU.
    Only discuss on finer granularity of energy cost in Aug meeting and make the conclusion.
  Split architecture:
    Transferring Measured UE performance from CU-UP to CU-CP.
  NR-DC mobility optimization:
    Enhance the Dual Connectivity procedure (e.g., MN-initiated SN addition, MN-initiated SN change) to trigger the collection of measured UE performance.
  Continuous Management-based MDT Data Collection
    TP was agreed in R3-243952.
Impacts and dependencies on other WGs
N/A
Other important info
Multiple-hop UE trajectory is not supported in R19.

## Slide 14: R19 Topology Enh SI
Progress in the last quarter
The study focuses on the use of WAB-MT´s PDU session via NR Uu as backhaul of WAB gNB. Other options for the backhaul (including non-3GPP radio technology) are not precluded but not a part of the study.
In case MT authorization is based on slice, signaling enhancements to the AS layer for the support of WAB-MT authorization are not needed.
The NG connection(s) of a WAB-gNB whose authorization status changes from “authorized” to “not authorized” can be removed. Any Stage 3 decisions are to be taken during normative work.
Establishment of Xn Connections of the WAB-gNB with BH-RAN nodes, as well as with surrounding RAN nodes, is supported and can follow legacy procedures.
TPs for TR 38.799 on Architecture/Integration/Authorization/ Mobility/miscellaneous issues have been agreed.
Architecture for NR Femto:
  4 options for NG interface and 2 options for Xn interface are captured in TR;
  Option1 for NG interface and optionA for Xn interace have no architecture change in 3GPP
  Evaluation of architecture for NG interface has finished.
Reusing CAG configurations and mobility functionalities specified for PNI-NPN also for NR Femto nodes deployments.
No impacts on the UE are in scope of the study for NR femto.
Impacts and dependencies on other WGs
For WAB: Reply LS to SA2 on FS_VMR_Ph2 solution impacts to RAN was agreed in R3-243961.
For NR femto: Security aspects are under SA3′s responsibility. LS from SA2 ans SA3 were received in RAN3#124 to check the progress of NR femto architecture, the reply LS plans to be sent based on conclusion next meeting.
Other important info
LS on CSG-CAG mobility was discussed in RAN3#124. However corresponding Reply LS is postponed due to companies can not reach consensus on the RAN impact analysis.

## Slide 15: R19 Mobility Enh WI
Progress in the last quarter
Prioritize to support inter-CU LTM over Xn interface, and RAN3 specify the inter-CU LTM solutions for standalone scenario first.
Reuse existing Xn Handover Request and Handover Request ACK for Inter-CU LTM initial preparation.
Confirm the case that inter-CU LTM is not configured in both MCG and SCG at the same time.
Early data forwarding can be supported for inter-CU LTM.
Cell Switch Notification from source DU to target DU (in different gNB from source) for LTM execution.
Source gNB-CU initiates the handover preparation procedure for inter-gNB-CU LTM.
Introduce a new procedure on Xn to transfer the TA information.
A new XnAP class 2 procedure, namely LTM Cell Switch Notification is introduced on Xn to forward the target Cell ID and target TCI state ID(s) from the source gNB-CU to the target gNB-CU.
Reuse Handover Success procedure over Xn for Rel-19 Inter-CU LTM, to tell the source CU that the UE has accessed to the target Cell.
The Handover Cancel message is reused by the source gNB to release the reserved resource for LTM candidate cells in the candidate gNBs.
Early data forwarding can be triggered before the Source gNB triggers a MAC CE Command to the UE to change cells, timing is left to implementation.
Early sync configuration (TCI state and RACH configuration) can be obtained during the LTM preparation phase through the handover request and handover request acknowledge messages.
A candidate gNB can initiate cancellation of configured LTM candidate cell(s) of its own.
Other important info
N/A

## Slide 16: R19 NR NTN WI
Progress in the last quarter
Support MBS broadcast service:
  RAN3 starts work on MBS broadcast service.
  WA: The mapped cell ID can be used to define MBS broadcast service in NTN.
Support of Regenerative payload:
  There is no consensus to discuss new NTN architecture now; wait for an LS from SA2 on this particular issue.
  Technical discussion based on current architecture can be discussed.
Impacts and dependencies on other WGs
Reply LS to SA2 on Support of Regenerative-based Satellite Access in R3-243954.
Reply LS to SA2 and SA3 on Security of IP transport over satellite transport links in R3-243955.
Other important info
N/A

## Slide 17: R19 Ambient IoT SI
Progress in the last quarter
RAN3 considers both Topologies at the same time looking whether commonalities are applicable.
For Topology 1, RAN3 starts with AIoT RAN node being aggregated.
AIoT Paging can be used to reach one or more devices for identified AIoT services (e.g., inventory, command).
Inventory over CN-RAN interface can be used for a single device, or a group of devices, or all devices.
Command over CN-RAN interface can be used for a single device. FFS for command on a group of devices, or all devices.
AIoT device location information may be used for the following purposes:
  (a) improving the AIoT operation itself, e.g. by sending a Command to one or more readers (e.g., the last reader(s)) associated to the device rather than sending it blindly.
  (b) providing location information to the consumer of the AIoT service.
  Locating an Ambient IoT device at “reader ID granularity” is useful for both purposes.
Impacts and dependencies on other WGs
Further details regarding AIoT functions hosted in the AIoT CN and the respective functional split to be decided by RAN2, RAN3 and SA2.
Other important info
RAN3 continues to discuss logical System Architecture for AIoT and corresponding impact over RAN-CN interface.

## Slide 18
Progress in the last quarter
Support on-demand SIB1 for UEs:
  Scenario1: UE obtains the UL WUS configuration from Cell A, and transmits UL WUS to NES Cell.
    -UL WUS configuration from NES Cell to Cell A via Xn, e.g., before entering on-demand SIB1 mode in the NES Cell or when the UL WUS configuration is changed
  Focus on case2 (as defined in RAN1) in RAN3 first.
Impacts and dependencies on other WGs
RAN3’s work highly depends on the progress of RAN1 and RAN2.
Other important info
N/A
R19 Network ES WI

## Slide 19: R19 XR WI
Progress in the last quarter
Add the behavior text on handling the PDU Set QoS Parameters IE in S-NG-RAN node Addition Preparation procedure and M-NG-RAN node initiated S-NG-RAN node Modification Preparation procedure.
Enhance the S-NG-RAN node Addition Preparation procedure and M-NG-RAN node initiated S-NG-RAN node Modification Preparation procedure, to transfer the ECN Marking or Congestion Information Reporting Request IE to S-NG-RAN node, and support the S-NG-RAN node to report ECN Marking or Congestion Information Reporting Status to M-NG-RAN node.
The PDCP host node to inform the corresponding node about whether the UL PSI based SDU discarding is (re)configured/released for MN-terminated SCG bearer and SN-terminated MCG bearer over XnAP.
For XR in NR-DC, non-homogenous deployment is possible similar like other features in DC.
If the SN receives the burst arrival time, the SN may use it by considering the SFN offset of the MN.
Impacts and dependencies on other WGs
LS R3-243957 is sent to RAN2 to ask RAN2 to clarify the UE behavior for handling uplink PSI based PDU discarding when MN and/or SN node sends the PSI-Based SDU Discard Activation/Deactivation MAC CE.
Reply LS in R3-243958 is sent to SA2.
Other important info
N/A

## Slide 20: TEI Corrections
Progress in the last quarter
Positioning:
  For pre-configured SRS activation, RRC container based solution is used to transfer the pre-configured SRS from the last serving gNB to the receiving gNB. New indicator should be introduced in XnAP Retrieve UE Context Request. gNB should notify LMF the pre-configured SRS is activated for the UE in the NRPPa Positioning Information Update.
  Other stage2 and stage3 correction.
AI RAN:
  AI/ML Model Training follows the definition of “ML model training” as specified in clause 3.1 of TS 28.105.
  AI/ML Model Inference: follows the definition of “AI/ML inference” as specified in clause 3.1 of TS 28.105.
  LS on terminology definitions for AI-ML in NG-RAN to SA5, RAN2 in R3-243969.
  UE level performance is derived as the average value of per DRB level measurements of the UE.
Restoration procedures for Split PDU Sessions from CT4:
  Support restoration procedures for Split PDU Sessions over NG, Xn and F1 from CT4.
  Reply LS to CT4 in R3-243968.

## Slide 21: TEI Corrections
Progress in the last quarter
MBS:
  Support of restoration of N3mb Failure for MBS broadcast, coordination with CT4 (R3-243888).
  Stage 2 correction on support of RRC_INACTIVE multicast reception and network sharing efficiency.
  Correction of MBS F1-U failure Recovery and Correction of MBS NG-U Setup and non-shared gNB-DU.
  Stage 2 correction on support RedCap UE MBS Broadcast reception.
  SL relay:
  Stage 3 corrections on support of indirect-to-indirect path switch, direct path release/addition.
  Stage 3 corrections on support of U2U relay, i.e. add Peer UE ID in PC5 RLC channel to be setup Item IEs IE.
  Other stage 2 and stage 3 corrections.
  SDT Release:
  Align with RAN2 solution in stage2 specs.
  Capture RRCRelease message with resume indication in the stage 2 procedure for SDT without anchor relocation.
  Send LS R3-243963 to RAN2 on network-based solution.

## Slide 22: TEI Corrections
Progress in the last quarter
Progress in the last quarter
Mobility Enhancements:
  Stage 2 and Stage 3 corrections on support of LTM, S-CPAC, CHO with SCG.
XR:
  Stage 2 and stage 3 corrections.
SOM/MDT:
  Stage 2 corrections for NR-U, fast MCG recovery, CPAC detection and inter-system MRO.
NR NTN:
  Stage 2 correction on OAM requirement for UE location.
IAB
  Stage 2 corrections on IAB-node authorization and mobile IAB procedures.
  Stage 2 and stage 3 corrections on IAB-node de-registration handling, i.e. add new cause value in X2/Xn/S1/NG to indicate that the operation at (m)IAB-DU’s donor has completed, or the unauthorized (m)IAB-MT can be de-registered.
  Stage 2 corrections on support of no PDU session for (m)IAB-MT.

## Slide 23: TEI Corrections
Progress in the last quarter
Progress in the last quarter
Improved KPIs:
  Inform SA5 via LS that there is a misalignment between TS 28.558 and TS 28.552 with respect to the entity that performs the measurements, and observations concerning the S-TMSI identifier from RAN3 side.
  MDT for NPN:
  Keep 256 in RAN3 spec and provide PLMN range limiation for Logged MDT.
  MDT in MR-DC:
  Signalling based immediate MDT is triggered for both MN and SN as default. If the MN only indication is provided by OAM, the MDT configuration applies to MN only.
  User consent:
  Update the TS 38.401 and TS 37.320 to reflect the latest agreed CR from SA5.

## Slide 24: My Heartfelt Thanks To:
Angelo Centonza, Gen Cao (RAN WG3 Vice-Chairs)
  For chairing the corresponding sessions and organizing social events during the meetings!
  Thanks Tianyang and Chenghock for helping to organize the big RAN3 dinner in Fukuoka!
Seonggu (RAN WG3 Secretary)
  For impressive hard work and continous support!
Philippe G, Yan, Liwei, Georg, Yingjun...
  For their positive and hard work and moderating some tough email discussions and good support!
All Rapporteurs and moderators
  For their efforts to rapporteur updates and TEI corrections!
All RAN3 delegates
  For their positive, constructive and cooperative spirit and hard work!

## Slide 25: RAN3 Social Events in Changsha and Fukuoka
3GPP RAN3 New Tie and Scarf Launch in RAN3#123bis
Farewell party to Gerd in RAN3#124
Compared to other groups RAN3 is a smaller one giving
regular participants a feeling of a familiar atmosphere,
although sometimes family members were fighting heavily
against each other, but in most cases could reach a consensus
on best technical solutions.
- Gerd (DT)
Notes: w

## Slide 26: RAN3 Social Events in Changsha and Fukuoka
Notes: w