## Slide 1: REL-independent spec handling
Issues of TS 38.307
ETSI MCC

## Slide 2: Outline
how the REL-independent approach changed over time
concrete TS 38.307 problems taken from 2024-03 versions
Summary and proposal

## Slide 3: Classic REL-independent approach
Release | REL-indep. spec (like XX.307) | Core spec (like XX.101)
active REL-N (feature xy introduced in REL-N) | Nothing for feature xy | For feature xy the UE has to fulfill the following requirements: - requirementA: blablaA - requirementB: blablaB - requirementC: blablaC
frozen REL-N-1 | For feature xy the UE has to fulfill the following requirements: - requirementA: blablaA - requirementB: blablaB - requirementC: blablaC | Nothing for feature xy
... | ... | ...
frozen REL-M (REL-indep. from REL-M) | For feature xy the UE has to fulfill the following requirements: - requirementA: blablaA - requirementB: blablaB - requirementC: blablaC | Nothing for feature xy
+: REL-indep. spec of each REL is self-contained, no pointers; -: A lot of requirement details to be repeated

## Slide 4: Explicit pointers to the Core spec
Release | REL-indep. spec (like 25.307) | Core spec (like 25.101)
active REL-N (feature introduced in REL-N) | Nothing for feature xy | For feature xy the UE has to fulfill the following requirements: - clause a.: requirementA: blablaA - clause b.: requirementB: blablaB - clause c.: requirementC: blablaC
frozen REL-N-1 | For feature xy the UE has to fulfill the following requirements: - requirementA: see REL-N core spec clause a. - requirementB: see REL-N core spec clause b. - requirementC: see REL-N core spec clause c. | Nothing for feature xy
... | ... | ...
frozen REL-M (REL-indep. from REL-M) | For feature xy the UE has to fulfill the following requirements: - requirementA: see REL-N core spec clause a. - requirementB: see REL-N core spec clause b. - requirementC: see REL-N core spec clause c. | Nothing for feature xy
+: no repetition of requirement details -: still listings of all requirements in REL-M to REL-N-1

## Slide 5: Pointers to the REL-independent spec of REL-N and from there to Core spec
Release | REL-indep. spec (like 36.307) | Core spec (like 36.101)
active REL-N (feature introduced in REL-N) | No requirements for feature xy but an Annex B with - requirementA: see REL-N core spec clause a. - requirementB: see REL-N core spec clause b. - requirementC: see REL-N core spec clause c. | For feature xy the UE has to fulfill the following requirements: - clause a.: requirementA: blablaA - clause b.: requirementB: blablaB - clause c.: requirementC: blablaC
frozen REL-N-1 | For feature xy the UE has to fulfill the requirements given in Tables of Annex B of the REL-indep. spec of the REL in which the feature was introduced (=REL-N for feature xy) | Nothing for feature xy
... | ... | ...
frozen REL-M (REL-indep. from REL-M) | For feature xy the UE has to fulfill the requirements given in Tables of Annex B of the REL-indep. spec of the REL in which the feature was introduced (=REL-N for feature xy) | Nothing for feature xy
+: listings of all requirements only in Annex of REL-N
-: too many features, need to remember when a feature was introduced
important: requirements are still made in REL-M to REL-N-1 referring to the Core spec

## Slide 6: Class of features
Release | REL-indep. spec (like XX.307) | Core spec (like XX.101) | 
active REL-N (feature xy introduced in REL-N) | No requirements for feature xy but an Annex B with - requirementA: see REL-N core spec clause a. - requirementB: see REL-N core spec clause b. - requirementC: see REL-N core spec clause c. | For feature xy the UE has to fulfill the following req. - requirementA: blablaA - requirementB: blablaB - requirementC: blablaC | 
frozen REL-N-1 | For feature class AB (incl. feature xy) the UE has to fulfill the requirements given in Tables of Annex B of the REL-indep. spec of the REL in which the feature was introduced (=REL-N for feature xy, REL-N-1 for feature yz) No requirements for feature yz in REL-N-1 but an Annex B with - requirementA: see REL-N-1 core spec clause a. - requirementB: see REL-N-1 core spec clause b. - requirementC: see REL-N-1 core spec clause c. | Nothing for feature xy | For feature yz the UE has to fulfill the following req. - requirementA: blobloA - requirementB: blobloB - requirementC: blobloC
... | ... | ... | ...
frozen REL-M (REL-indep. from REL-M) | For feature class AB (incl. feature xy and yz) the UE has to fulfill the requirements given in Tables of Annex B of the REL-indep. spec of the REL in which the feature was introduced (=REL-N for feature xy, REL-N-1 for feature yz) | Nothing for feature xy | Nothing for feature yz
e.g. feature class: operating bands; feature xy = band xy introduced in REL-N; feature yz = band yz introd. in REL-N-1

## Slide 7: prerequisites for class of features
different features are REL-independent starting from the same REL-M
the requirements are in the same tables of the Core spec for all features of a feature class
do not forget that the REL in which a feature is introduced may vary e.g. if feature class = operating bands, there may be new bands introduced in multiple releases (like REL-16/17/18...) although they would all be REL-independent from REL-M (M=15)

## Slide 8: consequences for class of features
Assuming some features under a feature class are introduced in REL-N and in a REL-independent way from REL-M, then Annex B in the REL-indep. spec of REL-N is needed so that REL-M to REL-N-1 can point to it but the feature class is only needed in REL-M to REL-N-1 and not in REL-N because requirements of REL-N are covered by the core spec
it is not the "REL-independent from REL-M" from which all features of a feature class are REL-independent that sets requirements
Annex B with the requirement details is needed and the rule "REL-K spec sets requirements for only REL-K UEs" shall not be broken
a feature class may already be there from a previous REL-K (K<N) if you introduce additional features in REL-N i.e. this may mean no CR to the REL-indep. spec of REL-N but the WID of REL-N must document the REL-independence

## Slide 9: Problem 1:
Question: If you read in a spec "feature xy is REL-independent from REL-15", which requirements does a UE have to fulfill?
Examples from TS 38.307 REL-15:
"Unless stated otherwise, the release independent for the band combinations are from Rel-15."
Feature | Duplex-mode | Release independent from | Requirements to be fulfilled (see TS 38.307 of the release in which the band was introduced)
Operating bands | TDD | Rel-15 | 

## Slide 10: Problem 1: "REL-independent" is no requirement
Question: If you read in a spec "feature xy is REL-independent from REL-15", which requirements does a UE have to fulfill?
Examples from TS 38.307 REL-15:
"Unless stated otherwise, the release independent for the band combinations are from Rel-15."
Answer: This is undefined unless corresponding requirements linked to this feature are really provided.
So a lot of features REL-indep. from REL-15 have no REL-15 requirements
Feature | Duplex-mode | Release independent from | Requirements to be fulfilled (see TS 38.307 of the release in which the band was introduced)
Operating bands | TDD | Rel-15 | 

## Slide 11: Problem 2:
Question: Building a REL-N UE, you will find the corresponding requirements in which release of the 3GPP specs?

## Slide 12: Problem 2: Requirements for different releases
Question: Building a REL-N UE, you will find the corresponding requirements in which release of the 3GPP specs?
Answer: Only REL-N specifications can introduce requirements for a REL-N UE.
TR 21.900: "A mobile system can be constructed based on the set of all specifications which comprise a given Release. A Release differs from the previous Release by having added functionality introduced as a result of ongoing standardization work within the Groups."
if it would be "whatever REL", you will search for a long time and it will also make it very complex to implement/test or close a REL
we avoid to explicitly state the REL for each requirement because the REL is clear from the REL of the spec (as REL-N+1 is based on REL-N it would require a lot of updates); also our cat.A CR mechanism is based on this principle

## Slide 13: Problem 2: Requirements for different releases
Example: TS 38.307 REL-18: "When a new feature is introduced only the latest release of release independent spec needs to be updated."
What is the purpose of the existing REL-15 to REL-17 versions of TS 38.307 in this case? These are still valid specs. Note 1: The statements "Requirements to be fulfilled (see TS 38.307 of the release in which the ... was introduced)" still refer to these older releases! Note 2: As indicated in problem 1 "REL-independent from REL-M" is no requirement.
What happens when REL-18 is upgraded to REL-19?

## Slide 14: Problem 3:
Question: Is it possible that a feature introduced in REL-N can be REL-independent from REL-N?
Example: TS 38.307 REL-17: "If an RF feature introduced in the same release as the release which the feature is independent from, (i.e. M=N), the common UE RF requirements table in annex B.4 is specified from release N+1, otherwise the common UE RF requirements table is specified from release N."

## Slide 15: Problem 3:
Question: Is it possible that a feature introduced in REL-N can be REL-independent from REL-N?
Answer: No, of course not otherwise every feature would be REL-independent. A feature introduced in REL-N specifies requirements in the Core spec of REL-N and if it is REL-independent from REL-M (M<N), then the REL-independent spec covers the requirements of REL-M to REL-N-1.

## Slide 16: Problem 3: duplicated requirements
Another example: TS 38.307 REL-18: Requirements for additional NR operating bands and power classes of TS 38.101-1 in Rel-P [2] are introduced via this clause. (REL-P = present release of this specification = REL-18)
For REL-15 to REL-17 UEs the blue text and green text irrelevant as this is a REL-18 spec. For REL-18 UEs the blue text makes no sense since REL-18 requirements are specified in the REL-18 core spec and not in the REL-18 REL-independent spec.
conclusion: A lot of features have duplicated REL-18 requirements.
Feature | Duplex-mode | Release independent from | Requirements to be fulfilled (see TS 38.307 of the release in which the band was introduced)
Operating bands | FDD, TDD, SDL, SUL | Rel-15 | Table B.4.1-1, Table B.4.3-1

## Slide 17: Problem 4:
Question: A non-specific reference for specfication xy.abc in a REL-17 spec is referring to which release of xy.abc?
TR/TS template: "a non-specific reference implicitly refers to the latest version of that document in the same Release as the present document"

## Slide 18: Problem 4: mistakes in non-specific references
Question: A non-specific reference for specfication xy.abc in a REL-17 spec is referring to which release of xy.abc?
Answer: REL-17
Example: TS 38.307 REL-17
[6] 3GPP TS 38.133: NR; Requirements for support of radio resource management This means for each feature: - it is "introduced" in a release N, i.e. TS 38.101 [2-5] and TS 38.133 [6] of release N define certain UE requirements for this feature; the feature is indicated in the tables of the following clauses;
So [6] is referring to TS 38.133 REL-17 and not an arbitrary TS 38.133 REL-N.
conclusion: The concept of non-specific references is misunderstood in several places

## Slide 19: Summary
The provided examples show that the new approach of handling TS 38.307
  breaks the REL-consistency (basic 3GPP principle)
  misses statements of requirements e.g. for REL-15 UEs
  duplicates core requirements in the REL-independent spec in REL-18
  violating non-specific references in some places
  creates confusion how the different releases of the spec interwork
It is therefore recommended that TSG RAN tasks a cleanup of the TS 38.307 specifications