## Slide 1
On 3TX for Rel-19 MIMO
Agenda Item: 9.3.1.1
Source: Google
Document for: Discussion for decision
RP-24xxxx

## Slide 2: Current objective about 3TX for Rel-19 MIMO
Specify non-coherent UL codebook to facilitate 3-antenna-port codebook-based transmissions, without enhancement on UL full power transmission and without enhancement on SRS resource
Note: UL full power transmission mode 1 and 2 are not supported.

## Slide 3: RAN1 conclusion for 3TX SRS for antenna switching
Since there are different understandings on whether 3TX SRS for antenna switching is included in 3TX MIMO WID or not, RAN1 failed to reach consensus for enhancement of 3TX SRS for antenna switching
RAN1 made the following conclusion
  There is no consensus in RAN1 to support antenna switching for 3TX UE in Rel-19

## Slide 4: RAN4 WID on 6Rx
Specify the core requirements to enable 6Rx for higher frequency bands (>2.5GHz) targeting at support of handheld UE for NR FR1 single carrier scenario
  Example bands: n41, n77/n78, n79, n104
  Support 4 MIMO layers at least, and study the gain and feasibility and if feasible, support 6 MIMO layers
  Specify the Rx requirements including reference sensitivity requirements for support 6Rx
  Note: the specified requirements can be applicable to both handheld UE and FWA devices
  Specify the requirements to support SRS antenna switching including t1r6, t2r6, t3r6, t4r6 depending on UE capability
Study the issue of insertion loss imbalance across SRS ports, and if justified, specify the corresponding solution

## Slide 5: Proposal
Observation
  3T6R and 4T6R are included in RAN4’s scope on 6Rx, however currently 3T6R and 4T6R are not supported in RAN1 spec
  Since 3TX configuration is based on 4Tx SRS with 1 port muting, it is possible to have a common solution for both 3T6R and 4T6R
Proposal 1: Clarify that 3T6R is included in Rel-19 MIMO scope
  Clarify that 4T6R is also included in Rel-19 MIMO scope
  Specify a common solution for 3T6R and 4T6R