## Slide 1: Motivation for R19 3Tx basket WI Agenda Item: 9.1.5 Source: OPPO, Samsung, MediaTek Document for: Approval
3GPP TSG RAN#104
Shanghai, China, June 17-20, 2024
RP-241086

## Slide 2: Background
In Rel-18, RAN4 has introduced 3Tx feature in [1], and also introduced a basket WI [2] for urgent band combinations.
The 3Tx feature in Rel-18 was focused on:
Inter-band UL CA/ENDC with one CC in each band in both UL and DL
The two bands support 1Tx in one band and 2Tx in the other band
It was only for FWA devices
In Rel-19, 3Tx feature is extended to handheld UE in RF enhancement WI [3].
In RAN4#111, several new demands for Rel-19 have been proposed in [4,5] which are:
To support intra-band contiguous UL CA in TDD band for PC2 and PC1.5 3Tx UE
To support FDD 2Tx + TDD 1Tx for PC2 and PC1.5 3Tx UE
Consider Tx switching between FDD 1Tx + TDD 2Tx and FDD 2Tx + TDD 1Tx.
Meanwhile, it has been requested to support more than 2bands in DL cases.
All these features can be considered in Rel-19 with a new basket WI for 3Tx.

## Slide 3: Objective proposal
The objective of this basket work item is for inter-band UL CA/EN-DC band combinations with 3Tx.
  The 3Tx inter-band UL CA/EN-DC band combination includes >=2 bands in downlink and two bands in uplink. Each UL band includes 1CC or contiguous CA. And the concurrent Tx capability is 1Tx in one band, and 2Tx in the other band.
    For the band with 2Tx, both UL MIMO and TxD will be considered
  The targeted UE types are handheld UE and FWA devices.
  The targeted total power class of band combination includes PC3, PC2 and PC1.5.
    The following power capabilities of each band in the band combination can be considered, and the maximum transmission power of each band shall be limited by the total power class
    For the band with 1Tx: PC3, PC2
    For the band with 2Tx: PC3, PC2, PC1.5
  Note 1: FDD PC1.5 in single band is not considered, and FDD + FDD with total power class PC1.5 is not considered either.
  Note 2: FDD 2T + TDD 1T for total power class PC2 and PC1.5 are included.
  Specify band combination specific requirements for 3Tx band combinations
    Introduce band combinations to the CA/ED-DC configuration tables, and inter-band CA/EN-DC MOP tables
    Specify corresponding MSD requirements
  Frequency band combinations considered in this WI are in attached excel file “Status of 3Tx band combinations of this basket WI” with the contact information, configurations, and completion status inside.
  Note 3: The 3Tx band combinations included in this basket WI are introduced in a release independent way starting from REL-17 with no changes to the TS38.307 specification.

## Slide 4: Annex:
[1] RP-223517, WID: Low NR band 4Rx for handheld UE and 3Tx for inter-band UL CA
and EN-DC, OPPO, RAN#98e 2022-12
[2] RP-232674, New WID: Rel-18 new basket WI for 3Tx inter-band UL CA and EN-DC, OPPO, RAN#101 2023-09
[3] RP-240828, New WID: UE RF enhancements for NR FR1/FR2 and EN-DC, Phase 4, Huawei, AT&T, RAN#103 2024-03
[4] R4-2407701, Evolution path of 3Tx Ues, MediaTek, China Telecom, China Unicom, OPPO, Softbank, T-Mobile USA, Verizon, RAN4#111 2024-05
[5] R4-2407889, Motivation for NR 3Tx HPUE inter-band ULCA with FDD UL MIMO, SoftBank, OPPO, RAN4#111 2024-05