## Slide 1
Introduction of BDS B2b
in A-GNSS in Rel-19
CAICT, CATT, CMCC, China Telecom, China Unicom, CBN, Huawei, Honor, OPPO, Xiaomi, Spreadtrum, ZTE, ASR, H3C, Intel, MediaTek Inc., Qualcomm, China broadnet, Hisilicon, vivo, Ericsson, Swifts, Apple, Nokia, Nokia Shanghai Bell.
RP-24xxxx
3GPP TSG RAN Meeting #104
Electronic Meeting, June 17 - 20, 2024

## Slide 2
B1I signal(V3.0), B1C signal(V1.0), B2a signal(V1.0) and B3I signal(V1.0) of BeiDou Navigation Satellite System (BDS) have been supported in 3GPP in Rel-17.
BeiDou Navigation Satellite System
Signal In Space Interface Control Document
Open Service Signal B2b (Version 1.0) has been
published by China Satellite Navigation Office,
in August, 2020.
Introduction
Reference : China Satellite Navigation Office, http://www.beidou.gov.cn/xt/gfxz/202008/P020230516558683155109.pdf

## Slide 3
The main reasons that B2b signal will be supported in A-GNSS in Rel-19 are:
B2b signal offers the open global navigation service on B2 frequency and also broadcasts PPP-B2b signals, which can enhance the spectrum compatibility of UE and would reduce UE complexity;
B2b signal can provide A-GNSS four-frequency compatible interoperation capability;
Higher accuracy of A-BDS with dual/multi frequencies on B1, B2 or B3.
Higher processing efficiency with triple frequencies on B1, B2 and B3, by reducing the initial time for ambiguity fixed.
Motivation
Proposal 1: B2b signal should be introduced in A-GNSS in 4G and 5G as well as B1C, B2a etc.

## Slide 4
How to handle?
How to support B2b signal in both 4G and 5G in Rel-19:
  A small WI for supporting BDS B2b signal can be led by RAN2.
    The work load is small, can be finished in no more than 9 months;
    Multiple working groups involved：
      RAN2 (core part), RAN4 (performance part).

## Slide 5
Proposals
Proposal 1: B2b signal should be introduced in A-GNSS in 4G and 5G in Rel-19.
Proposal 2: RAN is kindly requested to discuss and decide how to support BDS B2b signal in both 4G and 5G in Rel-19. The following WF is preferred:
  A small WI for supporting BDS B2b signal can be led by RAN2 .

## Slide 6: Objectives and specifications impacted
Objectives：
  Specify A-BDS enhancements in Rel-19, including :
    Supporting new signal of BDS B2b in A-GNSS for both 4G and 5G [RAN2, RAN4];
    Specify corresponding assistant information in dedicated signaling [RAN2].
Specifications:
Impacted existing TS/TR {One line per specification. Create/delete lines as needed} |  |  | 
TS/TR No. | Description of change | Target completion plenary# | Remarks
TS37.355 | Support BDS B2b signal in A-GNSS, define corresponding assistant data for B2b, and add reference of B2b. | Main CR. RAN#108 | No more than 0.5 TU for each RAN2 meeting. Total 2 TUs for RAN2 are needed. Total 0.5 TU for RAN4 is needed.
TS36.305 | Add corresponding references of B2b. | Small CR. RAN#108 | 
TS38.305 | Add corresponding references of B2b. | Small CR. RAN#108 | 
TS36.171 | Add corresponding references of B2b and define corresponding requirements if needed. | Small CR. RAN#109 | 
TS38.171 | Add corresponding references of B2b and define corresponding requirements if needed. | Small CR. RAN#109 | 
Note: Currently no new posSibType is identified to be defined for B2b. So there is no impact on 36.331/38.331/36.455 and 38.455. |  |  | 

## Slide 7
THANK YOU