## Slide 1
Considerations on R19 UAV
3GPP TSG RAN #104 RP-241202
Shanghai, China, June 17-20, 2024
Agenda Item: 9.11
Source: CMCC
Type: Discussion

## Slide 2
Identification of UE
Fewer obstruction
More handovers and more HO failure
unordered handover due to fragmented cell
ordered handover
UAV-specific Identification
Interference Level
Propagation Model
Handover Complexity
generic identification
simple interference
Motivation: The Challenges of 5G-A Low-Altitude Network
Terrestrial Network
NLOS path dominated
Low-Altitude Network
LoS path dominated
complex interference
Reqiurement of trusted access and terminal authentication between NW and UTM
New interference: air-to-air, air-to-ground, and ground-to-air
Fig.1 China Mobile guarantees takeout deliveries in Shenzhen based on UAV
Fig.2 HELI-EASTERN 5G + aeromedical emergency rescue
CMCC has conducted testing and verification of low-altitude networking architecture, interference control, handover enhancement, trusted access, and service assurance in Shenzhen, Wuxi, Changzhou and other cities in China.
Flight Path Information Reporting
for Aerial UE Communication
Altitude-based Reporting/Configurations
for Aerial UE Communication
Subscription-based Identification
of Aerial UE
BRID and DAA Support via A2X Communication
R18 NR support for UAV

## Slide 3
Mobility Enhancement for UAV
Field Test Result: High HO Failure Ratio
CHO Enhancements for UAV
Beam Type | DL |  |  |  |  | UL |  | Mobility | 
 | RSRP | SINR | THP | RI | BLER | THP | Txpower | HO Number | HO Failure
4.9G Main Lobe | -77 | 6 | 440 | 3 | 8 | 116 | 19.3 | 100 | 50%
2.6G Side lobe | -70 | 0 | 300 | 2.1 | 13.5 | 80 | 21 | 200 | 75%
In Rel-18, signalling of flight path information from UE to NG-RAN is supported;
Considering related fixed UAV flight path across large network areas, the CHO mechanism can help to minimize the required signalling and increase the robustness of the Handover of the UAV；
This scenario is very similar to the terrestrial use cases such as high speed train scenario where the UE’s movement is predictable to some extent；
The NR Rel-16 CHO can be baseline for UAVs mobility solution, with the enhanced conditions, e.g., if the associated Height-, distance- or time-based condition is met respectively for one of the waypoints (location, time stamp)；
To specify the enhancement for UAV in Rel-19
    Mobility enhancement for UAV [RAN2, RAN3, RAN1]
      CHO triggerred upon height-, distance- or time-based condition is met respectively for one of the waypoints (height, location, time stamp) height and flight path;
      CHO LTM enhancement for UAV

## Slide 4
Control on UE flying state for UAV Supervision
Motivation
In RAN#103, SA2 sent an LS RP-240031 on NTZ (No-Transmit Zone). RAN has discussed the LS and replied that the operation on NTZ was not in scope Rel-18 UAV work:
  LS from SA2 indicates that RAN input is required as necessary guideline to complete their work for UE regulation on NTZ depending on SA2 progress
  If RAN will be asked to enforce/apply these restrictions, the feasibility and complexity of solution will need to be further discussed in RAN WGs
    How to restrict UAV UE’s initial cell connection if a cell is operating in the NTZ area
    What and if any kind of information may be needed from 5GC to enable any such control
    How to implement any reporting of spurious UAV UE (those who do not follow restrictions)
Additionnally, aerial vehicle devices are reqiured to be supervised by the UAV operator and regulatory department:
  For operator, the legacy device (i.e. a Rel-15/16/17 device and a non-UAV Rel-18 device) riding an aerial vehicle has to be considered under the control of USS/UTM as well.
  For this scenario, the flying state information for the UEs could not be achieved since gNB cannot obtain actual measurement report of height and location from the legacy devices.
    However, the flying state information can be derived by gNB in implementation e.g. flying state detection through height-dependent serving cell distribution or RSRP/RSRQ as shown in the below figure.
Consequently, the flying state information with the UE ID can be delivered to CN through Ng-interface from gNB.
  Serving Cell distribution and Handover rate simulation data for drone UEs[R2-1713897, TR36.777]

## Slide 5
Control on UE flying state for UAV Supervision
Objectives
Specify the Control on UE flying state for UAV Supervision, the following enhancements can be considered: [RAN2,RAN3]
  Specify Access control, scheduling restriction, cell (re)selection mechanisms specific to NTZ area. [RAN2]
  Specify network signaling to support NTZ related information transfer
    e.g., enhancement of SIB [RAN2,RAN3]
  Specify the provisioning method of flying state information delivered to 5GC from gNB, which information is [RAN3]
    report of spurious R19 UAV UEs which violate the NTZ restriction
    report of flying state information with the UE ID for the both legacy devices (Rel-15/16/17 device and a non-UAV device in Rel-18) as riding in aerial vehicle and Rel-18 UAV UE in flying state
UAV trajectory tracking

## Slide 6
Thanks!