## Slide 1: SL Multi-hop Relay in Rel-19
RP-241217
3GPP TSG RAN Meeting #104
Shanghai, China, June 17-20 2024
Agenda Item: 9.1.2
Source: Lenovo
Document for: Discussion

## Slide 2: SL Relay evolution in 3GPP
R17 5G
R18 5G
  Single-hop L2 and L3 based U2N relaying
  Common for both L2 and L3 relaying
  Relay discovery and (re)selection for L3 and L2 relaying;
  Relay and Remote UE authorization for L3 and L2 relaying
  Specific to L2 relaying
  Intra-gNB service continuity
  Adaptation layer design
  CP procedures
  Single-hop L2 and L3 U2U relay
  Relay discovery and (re)selection
  Relay and remote UE authorization
  U2U relay adaptation layer design
  CP procedures
  QoS handling
  Service continuity for single-hop L2 U2N relay
  Inter-gNB path switching
  Intra-gNB indirect-to-indirect path switching
  To support multi-path scenarios
  To support Multi-hop L2 N2U Relay work
    Specifying one additional hop relay or two additional hop relay
  Is each L2 U2N relay In-coverage (IC) or Out-of-coverage(OOC)?
  L2 U2N relays in a Multi-hop relay are Intra-cell, Intra-gNB&Inter-cell, or Inter-gNB?
R19 5G

## Slide 3: In-coverage (IC) or Out-of-coverage(OOC)
  Rel-17 L2 U2N relay:
  In Rel-17 feature for L2 U2N relay, the relay UE should be in the coverage of a cell. In addition, a criteria of being a L2 U2N relay UE is specified in Rel-17. The serving cell may configure a maximum threshold and/or a minimum threshold for Uu RSRP to a UE. Only the UE meeting the criteria can act as a L2 U2N relay UE. In general, the UE located at the centre of a cell can act as a L2 U2N relay to ensure the quality.
Observation 1: In Rel-17, L2 U2N relay UE should be In-coverage.
Observation 2: In general, cell-edge UE is not configured to act as a L2 U2N relay UE in Rel-17.

## Slide 4: In-coverage (IC) or Out-of-coverage(OOC)
  Rel-19 Multi-hop U2N Relay:
  First-hop relay UE: A relay UE is closest to gNB in a Multi-hop link, which has a direct connection with gNB e.g Relay UE1 in figure.
  Second-hop relay UE/Third-hop relay UE: a relay UE accesses gNB via another relay UE e.g first-hop relay UE.
  It is obvious that the first-hop relay UE should be In-coverage. According to the criteria for being a relay UE defined in Rel-17, it is unsuitable for a cell-edge relay UE to act as a first-hop relay UE. Therefore, cell-edge UE can act as a Second-hop relay UE or Third-hop relay UE.
Observation 3: First-hop relay UE should be In-Coverage(IC), which has a direct connection with gNB.
Proposal 1: A L2 U2N relay UE in a Multi-hop Relay except for first-hop relay UE e.g Second-hop relay UE or Third-hop relay UE can be OOC or IC in Rel-19.

## Slide 5: Intra-gNB or Inter-gNB
  Rel-19 Multi-hop Relay:
  In Multi-hop relay, there are more than one L2 U2N relay UE e.g First-hop relay UE and Second-hop relay UE. If second-hop relay UE can be IC, the associations between first-hop relay UE and second-hop relay UE are listed below. We need to discuss which following case can be supported in Rel-19.
  Case#1: Intra-cell
  Case#2: Inter-cell&Intra-gNB (see Fig.)
  Case#3: Inter-gNB
  It is natural that Case#1(Intra-cell) can be supported if both first-hop relay UE and second-hop relay UE can be IC. Regarding Case#3, it will lead to high complexity. Regrading case#2, after second-hop relay UE2 accesses cell#1 via relay UE1, the relay UE2 can follow the configuration from Cell#1.
Proposal 2: The Multi-hop relay case in which L2 U2N relay UEs belong to different gNBs is not supported in Rel-19.
Proposal 3: The Multi-hop relay case in which L2 U2N relay UEs belong to a single gNB (Intra-cell or Inter-cell) is supported in Rel-19.
Case#2: Inter-Cell&Intra-gNB

## Slide 6: Thanks
thanks