## Slide 1
3GPP TSG RAN Meeting #104 RP-24xxxx
Shanghai, China, June 17 - 20, 2024
Source: ZTE Corporation, Sanechips
Agenda Item: 9.1.5
Motivation on R19 basket WID on nRx(n=4, 8) for NR bands (<2.6GHz) for FWA (Fixed Wireless Access) UEs and handheld UEs

## Slide 2: Backgroud
In Rel18, there were two WIDs includes FR1 band supports 4Rx operation, which are:
  WID of 4Rx_low_NR_band_handheld_3Tx_NR_CA_ENDC [1]:
    4Rx for low frequency NR bands (<1GHz) for handheld UE
      Several <1GHz bands were included: n5, n8, n20, n28, n20, n26, n71
      Related RF requirements have already been completed and included in the TS38.101-1 specification.
    It is not a basket WID.
  WID of 4Rx_NR_bands_R18 [2]:
    4Rx for NR bands (<2.6GHz) for FWA UE, and 4Rx for NR bands (1GHz to 2.6GHz) for handheld UE
      Several <1GHz bands were included but for FWA UE: n5, n13, n26, n85
    It is a basket WID.
In Rel18, there was one WID to introduce 8Rx for CPE/FWA/vehicle/industrial devices
  Example bands: n7, n41, n77/n78/n79
  Related RF requirements have already been completed and included in the TS38.101-1 specification.

## Slide 3: Motivation
4Rx:
  The impacted RF requirements for are the ΔRIB,4R requirements.
    Basket WID 4Rx_NR_bands_R18 only incudes NR bands (<2.6GHz) for FWA UE, and (1GHz to 2.6GHz) for handheld UE
    Supporting 4Rx in low bands (i.e. <1GHz) for handheld UE is an optional feature.
    For a certain <1GHz band, the ΔRIB,4R requirements are different when 4Rx operation is supported by FWA form factor UE and handheld UE.
    Low frequency bands(especially <1GHz) are valuable for their large coverage but with the drawback of lower throughput due to smaller BW (typically not larger than 30MHz) and less antennas in handheld UE (now only 2Rx).
      Increasing antennas number (from 2Rx to 4Rx) can provide higher throughput and better coverage
8Rx:
  The impacted RF requirements for 8Rx are the ΔRIB,8R requirements
    8Rx is still for CPE/FWA/vehicle/industrial devices
    All of the general RF requirements related to 8Rx have already been completed.
    Comparing with 4Rx, many more benefits can be achieved for 8Rx. For example, it can further enhance the coverage for the users located at the cell edge. Also, it can significantly improve the downlink throughput for a single user.
    8Rx can be release independent from Rel-17.

## Slide 4: Motivation (Cont’d)
4Rx: Some new demands for 4Rx NR band can be found in the follow:
8Rx: Some new demands for 8Rx NR band can be found in the follow:
As a follow-up work of R18 basket WID of 4Rx_NR_bands_R18, it is proposed to generate R19 basket WID on nRx(n=4, 8) for NR bands (<2.6GHz) for FWA (Fixed Wireless Access) UEs and handheld UEs
Band | Contact name, company | Contact email | Other supporting companies | Additional information
n85 | Bill Shvodian, T-Mobile USA | Bill.shvodian@t-mobile.com | Ericsson, Nokia, Deutsche Telekom | 4Rx operation is primarily for FWA form factor, and can be supported by handheld UE.
n13 | Yuanyuan Zhang, Samsung | tina55.zhang@samsung.com | Bell Mobility, TELUS, Nokia, Ericsson | 4Rx operation is primarily for FWA form factor, and can be supported by handheld UE.
Band | Contact name, company | Contact email | Other supporting companies | Additional information
n1 | Bo-Han Hsieh, CHTTL | pohanhsieh@cht.com.tw | Samsung, ZTE, Sanechips | 8 Rx operation is targeted for FWA/CPE/Vehicle/Industrial devices form factor.
n3 | Lei Gao, China Telecom | gaol8@chinatelecom.cn | Samsung, ZTE, Sanechips, CHTTL | 8 Rx operation is targeted for FWA/CPE/Vehicle/Industrial devices form factor.
n34 | Xiaoran zhang, CMCC | zhangxiaoran@chinamobile.com | CATT, ZTE, Sanechips | 8 Rx operation is targeted for FWA/CPE/Vehicle/Industrial devices form factor.
n39 | Xiaoran zhang, CMCC | zhangxiaoran@chinamobile.com | CATT, ZTE, Sanechips | 8 Rx operation is targeted for FWA/CPE/Vehicle/Industrial devices form factor.

## Slide 5: Proposals
Proposal 1: As a follow-up work of R18 basket WID of 4Rx_NR_bands_R18, it is proposed to generate R19 basket WID on nRx(n=4, 8) for NR bands (<2.6GHz) for FWA (Fixed Wireless Access) UEs and handheld UEs
Proposal 2: The objection is proposed as follow:
  Specify the nRx(n=4, 8) REFSENS requirement for NR FR1 bands
    Support of nRx(n=4, 8) for the bands <2.6GHz added in this WI is optional


## Slide 6: Reference
  1. RP-231013, Revised WID for Low NR band 4Rx and 3Tx, OPPO
  2. RP-240251, Revised WID: Rel-18 4Rx for NR bands for FWA (Fixed Wireless Access) UEs (<2.6GHz) and handheld UEs (1GHz to 2.6GHz), ZTE, China Telecom
  3. RP-233186, Further RF requirements enhancement for NR and EN-DC in frequency range 1 (FR1) , Huawei

## Slide 7: Thank you