## Slide 1: Rel-19 Work Scope of Enhancements for UAV/UAM

## Slide 2: Need for R19 WI on UAV/UAM enhancements
Status of work on support for No-Transmit-Zone requirements in 3GPP
  SA2 has progressed study on solutions related to NTZ support. SA2 has reached an interim conclusion on principles and a solution to NTZ in S2-2407322, which however includes the following Editor’s Note: Editor's note: Feedback from and/or coordination with RAN/RAN WGs is needed to finalize the conclusion for Key Issue #3.
  SA2 has sent LS in S2-2407355, where SA2 see it beneficial for RAN, RAN2 and RAN3 to provide feedback on RAN impact of the interim conclusion in S2-2407322 for completing their study. Other solutions not captured in S2-2407322 are not completely precluded as mentioned in the SA2 LS.
  Currently RAN WG has no (or sufficient) TU time to discuss the RAN impact of the SA2-considered solution(s) until 3Q. As a result, SA2 study on NTZ may close in 3Q with many open doors and details to be further discussed in RAN WGs.
In our view,
  A separate WI for UAV/UAM including at least support of NTZ should be created at Sep. 2024 for RAN WGs (at least RAN2 and RAN3) to be able to discuss the SA2-considered solutions and remaining details sufficiently and provide feedback to SA2.
    Then, SA2 can start and progress normative work for NTZ in Q4 as pointed out in SA2 Chair report to TSG SA#104 (SP-240579, see Annex for the relevant part) in conjunction with RAN WGs’ discussions.
  Other enhancements than NTZ are also considered timely and beneficial for Rel-19, considering pending roll-out of drone-based delivery and pilot-test of UAM services.

## Slide 3: Potential Scope for Rel-19 UAV/UAM enhancements
Both UAV and UAM need to be considered for Rel-19
  Rel-19 and Rel-20 are step-stones for developing 6G 3D mobility
Potential enhancement scope
  Support of No-Transmit-Zone (NTZ), in order to minimize service interruption caused by NTZ or generic communication-restricted zone, applicable to UAV/UAM.
  Aerial Mobility Enhancements for aerial UE, in order to achieve enhanced mobility performance (avoidance of unnecessary mobility), targeting UAM
Unmanned Aerial Vehicle
Urban Air Mobility
Rel-17
Rel-18
Rel-19
Rel-20
Rel-21
The presence of passengers UEs inside AAM aerial UE imposes more stringent requirements on connectivity robustness and link performance over radio interface, compared to UAM aerial UEs.
6G 3D mobility

## Slide 4: Potential Scope for No-Transmit Zone
Motivation
  CEPT Decision 22(07) requires UAV UEs to fulfill NTZ requirements. In order to fulfill the NTZ requirements, 3GPP SA2 is carrying out study and reached interim conclusion on a solution in S2-2407322 for supporting NTZ.
  To follow ECC NTZ requirement, UE in NTZ-affected area should be barred from accessing NTZ-affected cell. Existing cell-based barring mechanism is not sufficient, e.g., when NTZ maps to a fraction of a cell.
  If UE happens to enter a NTZ-affected area in a NTZ-affected cell, it encounters communication interruption/failure. Mechanisms to avoid such failure or to enable fast recovery is strongly desirable to minimize service interruption due to NTZ.
Proposed scope
  Access barring enhancement to prevent UAV UE in NTZ-affected area from accessing a NTZ-affected cell
    NOTE that according to S2-2407322, an NTZ may map to one or more cells or a fraction of a cell, or overlap different cells in a mobile operator network.
  Mobility triggering for NTZ avoidance
  Fast recovery from service interruption due to NTZ
Bold items are our priorities

## Slide 5: Potential Scope for Aerial Mobility Enhancement
Motivation
  Mobility performance of aerial UEs
    Suitable or intended mobility candidates can be different for different UE heights and locations. Mobility candidate down-selection mechanism based on UE height/location is beneficial.
    Frequent mobility events or ping-pong may happen due to highly dynamic channel environments experienced by flying UEs.
  Measurement and measurement reporting
    In R18, height-dependent RS sets are introduced to cope with vertically changing radio environments in RRC_CONNECTED. The similar needs to be done for measurements and cell reselection in RRC_IDLE/INACTIVE.
    The Rel-18 enhancement of measurement report was intended to reduce too frequent measurement report triggering under a large number of LOS neighbor cells. However, such enhancement could suppress some important reporting about interference status change.
Proposed scope
  Candidate down-selection mechanism based on UE’s 3D location
    Applicable to measurement report triggering, CHO triggering, cell reselection
  Prevention of frequent mobility events for aerial UEs
  Down-selection of measurement RSs in RRC_IDLE/INACTIVE based on UE 3D location
  Enhancement of measurement reporting procedure to enable best trade-off between timely reporting of radio measurements (including interference) and reasonable RRC signaling overhead
Bold items are our priorities

## Slide 6: Summary
Need for R19 WI on UAV/UAM enhancements
  A separate WI for UAV/UAM including at least support of NTZ should be created at Sep. 2024 for RAN WGs (at least RAN2 and RAN3) to be able to discuss the SA2-considered solutions and remaining details sufficiently.
  Other enhancements than NTZ are also considered timely and beneficial for Rel-19, considering pending roll-out of drone-based delivery and pilot-test of UAM services
Potential Work Scope of Rel-19 WI for UAV/UAM enhancements
  Support of NTZ
    Access barring enhancement for NTZ
      Note: An NTZ may map to one or more cells or a fraction of a cell, or overlap different cells in a mobile operator network.
    CHO enhancement upon entering/leaving NTZ.
    Fast recovery from service interruption in NTZ.
  Enhancements for mobility of aerial UEs
    Candidate down-selection mechanism based on UE’s 3D location, applicable to measurement report triggering, CHO triggering, cell reselection.
    Prevention of frequent mobility events for aerial UEs.
    Down-selection of measurement RSs in RRC_IDLE/INACTIVE based on UE 3D-location.
    Enhancement of measurement reporting procedure for best trade-off between timely reporting and reasonable RRC signaling overhead.

## Slide 7: Annex: SA2 progress
SP-240579 to appear in SA meeting