## Slide 1
Views on b/n28 full-band duplex for PC3
Agenda: 9.1.5
Source: Samsung, KDDI
Document for : Discussion
RRP-2412755

## Slide 2
Background
  In RAN4#110-bis meeting, the WF [1] on the recommendation of a Rel-19 new spectrum WI for b/n28 full-band duplexer with PC3/PC2 was discussed but not approved.
  In RAN4#111 meeting, the discussion continued and the agreements were captured in [2] as following.
  There is no agreement or recommendation in RAN4 on how to proceed PC3 work for b/n28 full-band duplex implementation.
  It is expected that discussion on the specification work for b/n28 full band duplex with PC3/PC2 would be continued in RAN#104.
    2/4
[1] R4-2406708, WF on band n28 full band duplexer, Apple, R4#110-bis
[2] R4-2410558, WF on A-MPR for n28, Apple, RAN4#111

## Slide 3
Way forward
Observation and Proposals
    4/4
  Observation 1: From real UE implementation perspective, there are already commercial UEs implemented full-band b/n28 duplex in Japan several years ago, while with PC3 regulatory requirements compliant (i.e., A-MPR=0) for DTV protection (NS_17) in Japan.
  Observation 2: From NW implementation perspective, introducing a new set of PC3 A-MPR requirements (i.e., A-MPR≠0) for b/n28 full-band duplex bring NBC issue to legacy NW.
  Observation 3: It has adverse impact to popularize full-band b/n28 duplex if A-MPR relaxation (i.e., A-MPR≠0) is introduced for PC3 for full-band b/n28 duplex.
Proposal：Existing PC3 A-MPR requirements (i.e., A-MPR=0) on band 28/n28 shall be maintained regardless of UE implementation on duplex design.