## Slide 1: Discussion on Rel-19 NR NTN progress and scope
Huawei, HiSilicon
3GPP TSG RAN Meeting #104
Shanghai, China, June 17-20, 2024
Agenda Item: 9.3.2.2
Document for: Discussion/Decision
RP-241289

## Slide 2: DL Coverage Enhancements
Background
  According to RAN#102 discussions, the constraint for no SSB channel enhancements comes ONLY from link-level improvement:
    Multi-company contribution to RAN#102 (RP-232860) provides sentence below, which was captured in moderator summary (RP-233107):
      A link margin improvement for physical channels (e.g. PDSCH and PDCCH) should be considered without impact on SSB design
    Then justification in the agreed WID (RP-234078) includes:
      A link margin improvement for physical channels (e.g. PDSCH and PDCCH) may be considered without impact on SSB design.
  In RAN1#117, clarification were raised on whether “SSB channel enhancement is not considered” applies for link-level enhancement only or for system-level enhancement as well, and it was noted that:
    Any needed clarification “SSB channel enhancement is not considered” in the WID is up to RAN plenary
Proposal
  to revise Rel-19 NR NTN WID to align the objective part to the corresponding justification part:
    SSB channel enhancement for improved link level performance is not considered in this scope.

## Slide 3: Uplink Capacity/Throughput Enhancements
Background
  As per WID, RAN target to study OCC for DFT-s-OFDM PUSCH by RAN#104
    Study then specify, if beneficial, DFT-s-OFDM PUSCH enhancements via Orthogonal Cover Codes (OCC)
    Note: the study phase is targeted to be completed by RAN#104
RAN1 Progress till RAN1#117
  Conclusion: OCC with PUSCH can support at least multiplexing of 2 or 4 UEs and achieve up to 2 or 4 times capacity gains respectively, when repetitions are used.
    Note: the actual gain may be less due to e.g. intra/inter cell interference.
  Potential techniques: Three OCC techniques were identified:
    Inter-slot time-domain OCC with PUSCH repetition Type A with OCC length 2 or 4
    Inter-symbol(s) time domain OCC with OCC length 2 or 4
    Intra-symbol pre-DFT-s OCC (comb-like structure as in PUCCH format 4) with OCC length 2 or 4
Considering the observed performance gain and specification impact of different OCC techniques, we propose to:
    Specify Inter-slot time-domain OCC with PUSCH repetition Type A with OCC length 2 or 4 [RAN1]

## Slide 4: HD-FDD RedCap/eRedCap
Progress:
  It was observed in RAN1#116bis that when there is TA mismatch between UE and gNB:
    There are less resources available for a scheduled HD-FDD RedCap/eRedCap UE in NTN compared to TN for collision case 3 and 4;
    There might be less resources available for the scheduled HD-FDD RedCap/eRedCap UE in NTN compared to TN for collision case 1,2,5 and 6;
    There may be a BLER performance degradation when UL coverage enhancement features(e.g. available slot counting, DMRS bundling for PUSCH and PUCCH) are used by HD-FDD (e)RedCap UEs in NTN scenario, if gNB does not attempt to avoid the collision.
  It was further concluded in RAN1#117 that:
    For Rel-19 HD-FDD RedCap/eRedCap UE in NTN, the issues caused by TA mismatch between actual TA used by the UE and assumed TA for the UE at the gNB should be mitigated for collision cases 3 and 4.
      Note: further discussion on other cases is not precluded.
  A number of enhancement schemes were discussed, including defining new priority rules, clarifying the TA assumption at gNB when determining DL/UL collision and enhancing existing TA report.
Proposal:
  Specify enhancements to mitigate issues caused by TA mismatch between actual TA used by the UE and assumed TA for the UE at the gNB, at least for collision cases 3 and 4 below [RAN1]:
    Semi-statically configured DL reception collides with semi-statically configured UL transmission
    Dynamically scheduled DL reception collides with dynamic scheduled UL transmission