## Slide 1: Study on BS-based Integrated Sensing and Communication for Rel-19
China Telecom, CATT, H3C, BUPT
June 2024
3GPP TSG RAN Meeting #104
Shanghai, China, June 17 - 20, 2024
Agenda: 9.11
RP-241308

## Slide 2: Justification
The object detection and tracking for UAV from TS 22.137 can leverage the advantages of 5G networks and generate potential new revenue for operators.
The basic performance of sensing based on the 5G communication system has been proved through both simulations and field trials.
The market on "low altitude economy" is accelerating, and 3GPP should develop solutions to meet market requirement in a timely manner.
ISAC has been applied to monitor the packet delivery routes of MeiTuan UAVs in ShenZhen.
The field test for monitoring multiple objectives in ISAC networking environment in NanJing.

## Slide 3: Consideration on Timeline for ISAC
It is envisioned that the 5G-A and 6G systems will coexist for a long time, ISAC should be supported in 5G-A also, not only for 6G;
To expedite ISAC application, we can conduct the study on procedure and signaling design for ISAC concurrently with channel modeling. The study work could focus on the functions and signaling design without conflicting with the current work of ISAC channel modeling.
2024
2025
2026
2027
2028
Rel-19
Rel-20
Rel-21
5G-A
6G
ISAC SI for BS-based Sensing
Channel modeling for 5G-A/6G ISAC
5G-A ISAC WI
6G SI (incl. ISAC)
6G WI (incl. ISAC)
5G-A ISAC Enhancement
2023

## Slide 4: Potential ISAC study objectives in Rel-19
Potential scope for study on BS-based ISAC :
  Identify use cases that BS-based ISAC could well applies for, with selecting suitable sensing mode (Mono-static or Bi-static);
  Study standardization impacts on the interfaces and procedures towards sensing establishment, control and data reporting, the message design for sensing data reporting should be common and easy extension for future extension to support more sensing modes and algorithms;
  Study standardization impacts on the support for Multi-BS collaborative sensing functions;
  Study the necessity to introduce local sensing function within NG-RAN node from e.g. latency point.
The studies should be focused on the existing NG-RAN architecture and interfaces to enable sensing functions, reducing the impact on 5G current system as much as possible.

## Slide 5: Proposals
Based on the business model consideration and the timeline of industrial development, the followings are proposed:
Observation: There is urgent commercial need for UAV detection and tracking;
Proposal: Conduct the study on procedure and signaling design in RAN3 for ISAC in Rel-19.

## Slide 6: Thanks！