## Slide 1: Consideration on the Scope of Further Enhancement for NR QoE in Rel-19
Source: China Unicom
3GPP TSG-RAN Meeting #104 RP-241320
Shanghai, China Jun 17-20, 2024
Agenda Item: 9.11
Document for: Discussion

## Slide 2: Potential objective of Further Enhancement on QoE (1)
  Motivation 1
  5G system is designed for providing various types of new services, while 5G QoE management aims to specify the unified mechanism to collect and optimize the experience parameters for the eMBB service, some other new emerging 5G services, such as XR (i.e., AR and MR), IIOT.
  The IIoT scenarios and many XR scenarios (such as gaming or factory automation) are inherently real-time, implying that dynamic RAN optimization is of high interest. Hence, it seems beneficial to specify RVQoE measurements for the XR and IIoT service types in Rel-19.
  The QoE/RVQoE collection mechanism may rely on the progress of other WGs, e.g. SA4.
Proposal 1: Agree to support for new services (XR, IIoT) (in coordination with SA4).

## Slide 3: Potential objective of Further Enhancement on QoE (2)
  Motivation 2
  QoE enhancement can be further enhanced to support new functions/features, such as NTN, NPN, etc.
  The NTN scenario as one of the important scenarios, it can coexist with the TN network, and the QoE collection to improve network performance for the NTN network. It is necessary to discuss how to support in Rel-19.
    e.g. mobility scenario, ensuring QoE reporting continuity during TN and NTN network need to be studied.
  For the NPN scenario, as there are commercial deployments in 5G network, there is also a need to discuss supporting SNPN and PNI-NPN, e.g. how to enable the QoE measurement in NPN scenarios.
  For Sidelink and, MBS, there are still ongoing discussions on the motivation for QoE collection, whether to support sidelink and MBS rely on the discussion.
  Proposal 2: Agree with QoE support for NPN, NTN align with the existing metrics, and supporting for the enhancement, e.g. support assistance information from OAM to support the QoE collection, support QoE reporting continuity for mobility between TN and NTN.

## Slide 4: Potential objective of Further Enhancement on QoE (3)
  Motivation 3
  As the MBS multicast service is not supportive in R18, the QoE collection of MBS multicast service in RRC_INACTIVE state has not been discussed. If the MBS multicast service is confirmed to be supportive in R19, how to support the corresponding QoE collection mechanism can be discussed to include in the R19 scope.
  Proposal 3: It is proposed to support QoE measurement for MBS multicast service in RRC INACTIVE state, if MBS multicast service is confirmed to be supportive in R19.
  Motivation 4
  The QoE measurements are already supported for both RRC_IDLE and RRC_INACTIVE states, but the alignment of QoE measurements with radio-related measurements in RRC_IDLE and RRC_INACTIVE states has not been discussed. The alignment of QoE measurements with radio-related measurements in RRC_CONNECTED state had been specified in R18. Therefore, this part can be considered as part of the objective of Rel-19 NR QoE enhancement. This functionality can be extended to supporting NR-DC scenarios, e.g. the impacts on MN and SN need to be further studied.
  Proposal 4: Agree with the enhancement on the alignment of QoE measurements with radio-related measurements (e.g. RRC_IDLE / INACTIVE, NR-DC).

## Slide 5: Potential objective of Further Enhancement on QoE (4)
  Motivation 5
  For RVQoE topic, there are initial discussions in R18, and RVQoE can be applied for the purpose of network resource optimization. There are also some discussions on trigger event RVQoE. The trigger events for RVQoE reporting can be utilized to optimize user experience, e.g. handover, RAN overload, or NR-DC configuration.
  In R18, the RVQoE reports can be transferred to gNB-DU for data analysis and optimization. It could be further studied whether additional configuration information could be sent to gNB-DU.
  Another motivation of specifying the RVQoE is used for near-real-time QoE collection at RAN side. There will be conflicts in transferring the RVQoE reporting and uplink data when the traffic load is high, which will lead to an increase in the RVQoE reporting delay. Therefore, there is a need to study how to reduce the RVQoE reporting latency in R19.
  Proposal 5: RVQoE enhancements need to be further decided in the following objectives.
  Support event triggers for RVQoE reporting, e.g. handover, RAN overload, etc.
  Support the DU generation RVQoE configurations over F1 interface.
  Reduce RVQoE reporting latency, e.g. RVQoE reporting via lower layer signaling.

## Slide 6: R19 Further Enhancement on QoE
  The potential objective as summarized as following.
  Objective 1: Support for new services (XR, IIoT, AR/MR) (in coordination with SA4).
  Objective 2: QoE support for NPN and NTN, aligning with the existing metrics, and supporting the enhancement, e.g. defining specific assistance information.
  Objective 3: Support QoE measurement for MBS multicast service in RRC INACTIVE state, if MBS multicast service is supported.
  Objective 4: Further enhancement for the alignment of QoE measurements with radio-related measurements (e.g. RRC_IDLE / INACTIVE, NR-DC).
  Objective 5: RVQoE enhancements, which need to be further discussed.
  Support event triggers for RVQoE reporting, e.g. handover, RAN overload, etc.
  Support the DU generation RVQoE configurations over F1 interface.
  Reduce RVQoE reporting latency, e.g. RVQoE reporting via lower layer signaling.
Proposal 6: It is proposed to agree on the above objectives of further enhancements on NR QoE for further discussion.

## Slide 7
Thanks

## Slide 8: Reference
  RP-231579 QoE enhancements in Rel-19 Nokia, Nokia Shanghai Bell
  RP-232035 Scople of QoE Enhancements in Rel-19 Samsung
  RP-232126 QoE enhancements in Rel-19 Huawei, HiSilicon
  RP-232144 RAN Visible QoE in Rel-19 Xiaomi
  RP-232167 Views on NR QoE in Rel-19 ZTE, Sanechips
  RP-232422 QoE and RVQoE Measurement and Reporting Enhancements in Rel-19 Ericsson
  RP-232628 Moderator's summary for REL-19 RAN3 additional topics Ericsson (moderator)