## Slide 1: Consideration on R19 UAV in RAN
Agenda Item: 9.11
Source：CATT, China Telecom, China Unicom, Kyocera, Lenovo, vivo, LG Electronics Inc.
3GPP TSG RAN #104 RP-241338
Shanghai, China, June 17-20, 2024

## Slide 2
Use cases, requirements and R18 preliminaries
Backgrounds on R19 UAV in RAN and SA2
R19 UAV potential objectives

## Slide 3: Justification 1: UAV USE CASES
Top UAV use cases:
Construction
Agriculture
Insurance Claims
Offshore Refining
Police, Fire, Coast
Guard, Border Control
Journalism, News
Utilities
Filmography
Logistics

## Slide 4: Justification 2: Agreed Requirements For UAV
Requirement | Agreed value
Data Type | 1. Command and Control (C&C) 2. Application Data: includes video (streaming), images, other sensor data, etc.
Heights | Target up to 300m above ground level
Speeds | Target horizontal speeds up to 160 km/h (~100 mph) for all scenarios
Latency | 1. C&C: RAN2 understanding is 50ms (one way from eNB to UAV). 2. Application Data: latency value similar to LTE ground based users
Data Rates | 1. C&C: [60-100] kbps for uplink and downlink 2. Application Data: up to 50 Mbps for UL
C&C Reliability | As low as 𝟏𝟎−𝟑 Packet Error Rate
Requirements for aerial vehicles captured in TR 36.777
The above requirements are also applicable to NR.

## Slide 5: Justification 3: R18 NR UAV Background
Enhancements to measurement reporting
Height-based Reporting for Aerial UE Communication Height-dependent Configurations for Aerial UE Communication Flight Path Information Reporting for Aerial UE Communication Measurement reporting based on a configured number of cells (i.e. larger than one) fulfilling the triggering criteria simultaneously
Management/regulation related
Subscription-based aerial-UE identification The support for UAV identification broadcast (BRID) in NR PC5. The support of DAA using the same framework as BRID without DAA specific enhancements Based on the technical conditions defined for aerial UE usage in ECC Decision (22)07, specify the necessary UE types and additional OOBE requirements for aerial UEs in 1710-1785 MHz, 2500-2570 MHz and 2570-2620 MHz.
      RAN enhancements in R18 UAV include:
      Measurement reporting enhancements.
      Enhancements to fulfill management/regulatory requirements.

## Slide 6
Use cases, requirements and R18 preliminaries
Backgrounds on R19 UAV in RAN and SA2
R19 UAV potential objectives

## Slide 7: Background of R19 UAV discussion in RAN
      The current discussion status for R19 UAV is as follows according to the summary (RP-232627) in RAN#101, which should be considered as the baseline for further discussion.
Conclusions
Large operator support for UAV as one of the most important Rel-19 topics (within the items in this offline) from a commercial and mission critical perspective.
Architectural changes will not be part of the UAV work (i.e. any architectural enhancements can be considered under NTN)
Starting point of an acceptable objective:
  Mobility enhancements
    Specifying new CHO triggering events
    Studying/specifying LTM enhancements for UAV
  No transmit zone (if SA2 will also do work on this)
  Enhancements for RRC_IDLE/RRC_INACTIVE

## Slide 8: Background of R19 UAV progress from SA2
      On No-transmit Zone (NTZ)
As indicated in LS RP-240810, “RAN WGs will further study any RAN specific solution to enable NTZ if asked to enforce/apply these restrictions (e.g. by SA2)”
As further indicated in LS S2-2407355:
  SA2 UAV SI is considering to support NTZ mechanism with RAN impacts
     “solutions #7, #9, #16, #17, etc. may rely on or identify potential RAN impacts. ”,
  SA2 keep asking RAN WGs’ input as necessary guideline, in order for them to finalize the end-to-end NTZ design in Rel-19 UAV:
     “RAN input may provide additional/different solution guidance regarding RAN impacts related to NTZ that can assist SA2 in evaluating and selecting final end to end solution for normative work.”
      Observation: SA2 is asking for RAN input as necessary guideline, in order to finish the end-to-end NTZ design for Release 19 UAV.

## Slide 9
Use cases, requirements and R18 preliminaries
Backgrounds on R19 UAV in RAN and SA2
R19 UAV potential objectives

## Slide 10: CHO enhancements
High accuracy positioning in variable scenarios and use cases indoor/outdoor
-- Continue enhancements
Improving mobility performance of aerial UEs
Motivation:
According to TR 36.777, the number of detectable cells and the range of the detected cells increases as UAV altitude increases. And the distribution of reachable distance to serving cell demonstrated that aerial UE can be served by a geographically far-away cell compared to ground UE.
For CHO, it means in different altitude ranges there could be different candidate cells. So CHO needs to take UE altitude/flight path into account for candidate cell preparation and CHO triggering.
Objective:
Specify CHO enhancement considering flight path plan/height related events: [RAN2]
Specify CHO triggering events associated with flight path/height event.
NOTE: No impact is expected to other WGs.
Field Trial results captured in TR 36.777

## Slide 11: No-Transmit Zones
No-transmit zones
Motivation:
ECC decision (22)07 on harmonized framework on aerial UE usage in MFCN harmonized bands states “a mechanism is necessary to ensure that aerial UE respect no-transmit zones”. LS from SA2 indicates that they are working on this in Rel-19 and need RAN input as necessary guideline to complete their work.
Objective:
[TBD] Specify enhancements to support No-transmit zone in RAN (e.g. impacts to CONNECTED/IDLE mobility, NW signaling aspects for NTZ config., etc.). [RAN2,RAN3]
  NOTE: This work depends on SA2 UAS Ph-3 SI progress.

## Slide 12: UAV Detection and Notification
UAV Detection and Notification
Motivation:
In practice, there is the need for the network to know the real-time status of UAV, so as to carry out effective supervision to the UAVs in the network (e.g. detection/control on malicious UAVs). For example, the network may need to be aware of whether a UAV is in the flying status, and thus start supervision on its communication (e.g. release of connectivity and de-registration, if needed) w.r.t. its dynamics in a timely and on-demand manner, based on the interaction with supervision platform. Such demand may apply to both pre-R18 and R18 UAVs. It is possible for NG-RAN to identify a UAV with related dynamics via implementation-specific manners (e.g. via measurements, interference detection, etc.). However, due to the lack of specification support, NG-RAN currently cannot send such information to 5GC, which thus cannot contact the supervisory platform to provide necessary control to the UAVs in the field as intended.
Objective:
Specify UAV motion status detection and notification from NG-RAN to 5GC [RAN3]
  Specify the NW signaling procedure and information exchange over NG interface (e.g. UAV identification request/response, related motion status, etc.).

## Slide 13
Notes: 万物互联，无限沟通
Universal Connectivity, Infinite Communication.