## Slide 1: On Rel-19 Multi-carrier enhancements
3GPP TSG RAN Meeting #104
Shanghai, China, June 17-20, 2024
RP-241380
Agenda Item: 9.11
Source: Lenovo, China Telecom, China Unicom, Huawei, HiSilicon, Apple, CATT, OPPO, vivo, Spreadtrum, xiaomi, HONOR, Cybercore, TCL, Transsion, New H3C
Document for: Discussion and decision

## Slide 2: RP-232626: Moderator's summary on Rel-19 Multi-carrier enhancements in RAN#101
Companies who are supportive of multi-carrier enhancement in Rel-19: Futurewei, Lenovo/Motorola, Huawei/HiSi, DCM, TELUS, Bell Mobility, ZTE, MTK, Telstra, Nokia (if it’s a new proposal with sufficient operator demand), vivo, Xiaomi, Samsung (if scope is small)
  Some of the companies indicated that it depends on the scope
Companies who disagree (i.e., multi-carrier enhancement should not be part of Rel-19):
  Some of the companies indicated that it depends on the scope
From moderator point of view, the following topics seem to be a good starting point for further discussion on potential multi-carrier enhancement in Rel-19:
  Enhancements on multi-cell/user scheduling via single DCI
      Spec impact could depend on scope (ZTE), need to separate different proposals under this area (MTK/Apple)
  Single cell with multiple carriers:
      Concern on large spec impact (Ericsson/ZTE/Qualcomm/LGE/Lenovo/Motorola), need to involve RAN1/2/4 and should start with a study (Nokia)
  Note: Other companies indicated their preference on other proposals not included above

## Slide 3: Background: Rel-18 Standardization outcome
Main standardization outcome
DCI format design:
  At most one PDSCH or PUSCH per scheduled cell
  New DCI formats, DCI 0_3 & DCI 1_3, introduced
  Up to 4 cells can be co-scheduled by one DCI 0_3/1_3
  DCI 0_3/1_3 can be used for single cell scheduling
  DCI 0_3/1_3 and DCI 0_0/1_0/0_1/1_1/0_2/1_2 can be monitored simultaneously from a same scheduling cell.
Basic framework
Supported cases:
  Only same SCS among co-scheduled cells is supported
  Only same carrier types (licensed/unlicensed, FR1/FR2/FR2-2) among co-scheduled cells is supported
  Only a single scheduling cell for each scheduled cell
  Only single PDSCH or PUSCH scheduled per scheduled cell
  Only TB-based transmission supported per scheduled cell
Up to 4 cells scheduled by one DCI format 1_3
Up to 4 cells scheduled by one DCI format 0_3

## Slide 4: Motivation for Rel-19 Multi-carrier enhancements
Multi-carrier operation is very important for 5G commercial networks by aggregating various spectrum resources for providing high data rate and low latency communication.
Due to quite limited TU for Rel-18 Multi-carrier enhancements, some important use cases have been excluded from Rel-18, e.g., different SCS among co-scheduled cells, different carrier types among co-scheduled cells, more than one scheduling cell for a scheduled cell. Co-scheduling carriers with different SCS is of high commercial needs for operators, e.g., 3.5GHz TDD + Sub-3GHz FDD, FR1 + FR2. For a scheduled cell, supporting one scheduling cell for multi-cell scheduling and another scheduling cell for single-cell scheduling can offload PDCCH from the sole scheduling cell.
Furthermore, two new DCI formats are introduced in Rel-18, DCI format 0_3 and 1_3. Each DCI format 0_3 or 1_3 can schedule up to 4 cells with limitation of a single PUSCH or PDSCH per scheduled cell. In Rel-17, for FR2 with high SCS, multi-PDSCH/PUSCH scheduling is introduced, i.e., up to 8 PUSCHs or PDSCHs on a single serving cell can be scheduled by a single DCI format 0_1 or 1_1, in order to save UE power consumption and reduce PDCCH overhead.
Hence, it is straightforward to combine multi-cell scheduling and multi-slot scheduling in Rel-19 to fully exploit the gain of power saving and PDCCH overhead reduction so that one DCI format 0_3 or 1_3 can schedule multiple cells with one or multiple PUSCHs/PDSCHs per scheduled cell. This is especially useful when scheduling cell in FR1 with a lower SCS schedules multiple cells in FR2 with higher SCS.

## Slide 5: Objectives for Rel-19 Multi-carrier enhancements
Enhancements on multi-cell PUSCH/PDSCH scheduling by a single DCI [RAN1]
  Different SCS/carrier type among co-scheduled cells by DCI format 0_3/1_3 is supported
  Up to two scheduling cells for a scheduled cell is supported
      Self-scheduling for single-cell scheduling (e.g., using DCI format 0_0/1_0/0_1/1_1/0_2/1_2) and multi-cell scheduling using DCI format 0_3/1_3 from another cell if configured
  One or multiple PUSCHs/PDSCHs per scheduled cell is supported
      It is up to RAN1 to determine the maximum number of PUSCHs/PDSCHs per scheduled cell
  Note: No new DCI format is introduced.