## Slide 1
RP-241519
Agenda Item: 10.1.5
Type: WID NEW
Document for: Information
3GPP TSG RAN Meeting #104
Shanghai, China,
June 17th – 20th, 2024
Motivation for introduction of LTE FDD band in 1800 – 1830 MHz for Canada
Source: Novamint, Sequans, Semtech, Telit, Ubiik, EDF, EUTC

## Slide 2
The 1800-1830 MHz spectrum has been exclusively designated at a national level for the use of electricity utilities in Canada for fixed communication (point to point and point to multipoint).
The current regulation is available at the following link: https://ised-isde.canada.ca/site/spectrum-management-telecommunications/en/devices-and-equipment/standard-radio-system-plans-srsp/srsp-3017-technical-requirements-fixed-radio-systems-operating-bands-1700-1710-mhz-and-1780-1850-mhz
The Canadian regulator (ISED) clarified that no specific technology or duplex mode is mandated in this band and therefore LTE and FDD technologies can be deployed already now if fulfilling the regulation (see ISED letter in attachment)
Pilots are ongoing or are planned to be conducted both in the lab and in the field later this year by several Electricity utilities.
Background

## Slide 3
Electricity utilities in the region have relied on WiMax operating in the 1800-1830 MHz range as the communication backbone only
Electricity utilities in Canada are eager to transition to LTE technology within the 1800-1830 MHz spectrum.
The telecom regulator in Canada, ISED, is already engaged in making the regulatory changes (like channel spacing) to make deploying LTE more optimal (moving from 125kHz to 100kHz channelization) on this band
This Work Item is proposing the definition of a new FDD band to transition from WiMax to LTE technology and allow new use cases, such LPWA (NB-IoT and eMTC) and cat 1-4 UEs
The following assumptions are to be considered:
  Fixed communications only are allowed (point to point and point to multipoint)
  The band is specified to support Full Duplex operation for cat 1-4 UEs, assuming their form factor is CPE-like and therefore removing constraints on size and some implementation aspects
  NB-IoT and eMTC devices are expected to operate in Half Duplex mode.
Based on the above assumptions the following channel arrangement is proposed
Justification

## Slide 4
Proposals
Proposal 1 (Core)
Specify in a Release independent manner the characteristics of the new band :
  UL 1800 – 1810 MHz and DL 1820 – 1830 MHz
  Band numbering and RF characteristics
  Support the following channelization: 10, 5, 3 and 1.4 MHz
  Support of Full Duplex operation
Define maximum transmit power for both eNB and UE in compliance with the regulations
Update the related 3GPP E-UTRA technical specifications to include support for the new band
Proposal 2 (Core)
Specify and modify core requirements (e.g. UE power class, Additional Maximum Power Reduction (A-MPR), Reference sensitivity, blocking performance) and specifications to support UE categories 1-4, M1&M2 and NB1&NB2 in a release-independent way
Proposal 3 (Performance)
Update the related 3GPP E-UTRA technical specifications to include support for the new band, if necessary
Specify performance requirements and specifications for the new LTE band to support UE categories 1-4, category NB1&NB2 and category M1&M2 in a release-independent way

## Slide 5
Next Steps
Agree the WID on introduction of LTE FDD band in 1800 – 1830 MHz for Canada at RAN#104 (see RP-241518)
Attachment: ISED letter