## Slide 1: Motivation for new L-band definitions and possible Carrier Aggregation (CA) combinations for NR NTN
Source: Inmarsat, Viasat, Thuraya/Yahsat, Terrestar Solutions, Omnispace
3GPP TSG RAN #104
June 16 - 20, 2024, Shanghai, China
Agenda: 9.1.5 - Proposals led by RAN4 (spectrum related)
TDOC: RP-241531
For: discussion

## Slide 2: MSS Spectrum Priorities
Summary:
New NR NTN band [n253] to support the MSS Extended L-band (UL 1668-1675, DL 1518-1525), mirroring the current band 253 for IoT NTN covering the same range
New NR NTN band encompassing the combined L-band and Extended L-band (e.g. n255 + [n253])
  DL block 1518-1559 MHz
  UL block #1 1626.5-1660.5 MHz
  UL block #2 1668-1675 MHz
DL and UL Intra-SAN Carrier Aggregation (CA) for FR1 NR NTN bands.
  Intra-band (e.g. n255 + n255, n253 + n253, n256 + n256)
  Inter-band (e.g. n256 + n255, n255 + n253, etc)
New DL + UL cross-band pairings, to allow combining 1xDL and 1xUL from different NTN bands, e.g:
  n255 UL + n256 DL (and vice-versa)
  n255 DL + n253 UL (and vice-versa)
  etc

## Slide 3: Missing MSS L-band spectrum band specifications
Background and Motivation:
Extended L-band frequency range (UL 1668-1675, DL 1518-1525) has been addressed in Release-18 for IoT NTN (LTE band) only, i.e. band 253 (IoT_NTN_extLband).
The need for a corresponding NR NTN band covering the Extended L-band range has been expressed since early phases of Release 17 (initial proposals were to address the full L-band range from the beginning), and later on from RAN#99, but has been postponed reportedly due to high RAN4 workload
The L-band and Extended L-band DL ranges are contiguous and are both available in the majority of global regions (Region 1, 3 and parts of Region 2), but separate band specifications leads to lack of flexibility, making carrier allocations across the 1525 MHz DL boundary unusable, and does not allow to leverage the larger DL spectrum for higher data rates
The L-band and Extended L-band UL ranges are non-contiguous, so there is a need to identify how to best specify them:
  The simplest and most future-proof option would be to specify unpaired band segments (1x DL and 2x UL).
  However, other options, such as: (a) specification of 2 operating bands – each per UL segment – or (b) of a single operating band with two ULs with explicit signalling, or (c) as a single band with PRB restrictions and in-band emission limits could also be considered.
There is an urgent need to complete the FR1 NR NTN band plan to allow sufficient time for UE implementation in preparation for network roll-out

## Slide 4: Separate DL bands lead to inefficient and inflexible use of spectrum
5 MHz channels can only be allocated at the edges of the two bands.
  The ~5 MHz range of channel position (NR ARFCN) crossing the two bands cannot be used
>=10 MHz channels cannot be supported at all in the Extended L-band [n253] allocation (limited to 7 MHz)
>=10 MHz channels can only be allocated entirely in n255, preventing to make effective use of the spectrum in Extended L-band
Results in severe limitations:
  Prevents access to extra 7 MHz of Extended L-band spectrum granting total of 41 MHz of spectrum
  Prevents allocation of channels across the 1525 MHz edge, including 10 MHz channels anchored in the lower part of the band
5
1525 MHz
1518 MHz
1559 MHz
5 MHz
[n253]
n255
5 MHz
1525 MHz
1518 MHz
1559 MHz
[n253]
n255
10 MHz
5 MHz
10 MHz
~5 MHz of unusable NR ARFCNs
~5 MHz of unusable NR ARFCNs
10 MHz channel cannot be deployed in [n253]

## Slide 5: New NR NTN Band and CA combos Candidate Proposals
Band(s) | Candidate Band Number | Downlink | Uplink | Channel Raster | Mode | TX-RX Separation
Extended L-band | [n253] | 1518-1525 MHz | 1668-1675 MHz | Enhanced (10 kHz) - Mandatory | Flexible FDD or Unpaired | Flexible or unspecified
Potential Combined L-band and Extended L-band | TBD | 1518-1559 MHz | Block #1 1626.5-1660.5 MHz Block #2 1668-1675 MHz | Enhanced (10 kHz) - Mandatory | Flexible FDD or Unpaired DL and UL | Flexible or unspecified
New or Modified Combination | Band combination configuration | UpLink configuration | Subclass | Power class of band X | Tx number of band X | Power class of band Y | Tx number of band Y | Total Power class
New | CA_n255(2A) | CA_n255(2A) | NR only | PC3 | 2Tx | - | - | PC3
New | CA_n256(2A) | CA_n256(2A) | NR only | PC3 | 2Tx | - | - | PC3
New | CA_n253(2A) | CA_n253(2A) | NR only | PC3 | 2Tx | - | - | PC3
New | CA_n255A-n256A | CA_n255A-n256A | NR only | PC3 | 1Tx | PC3 | 1Tx | PC3
New | CA_n255A-n253A | CA_n255A-n253A | NR only | PC3 | 1Tx | PC3 | 1Tx | PC3
New | CA_n256A-n253A | CA_n256A-n253A | NR only | PC3 | 1Tx | PC3 | 1Tx | PC3