## Slide 1: Intra-SAN Carrier Aggregation (CA) and fragmented carrier aspects for NR NTN
Source: Inmarsat, Viasat, Thuraya/Yahsat, Terrestar Solutions, Omnispace
3GPP TSG RAN #104
June 16 - 20, 2024, Shanghai, China
Agenda: 9.1.4 - Proposals led by RAN4 (non-spectrum related)
TDOC: RP-241533
For: discussion
Public

## Slide 2: Rationale - DL Carrier Aggregation
Initial channel allocations may in certain regions be constrained by existing/legacy services, whereby channels may become available in non-contiguous areas of spectrum
With dual band satellites, in some cases the capacity and DL throughput could be significantly increased by aggregating carriers from different bands (e.g. n255 + n256) – in the same satellite (SAN)
Intra-band non-contiguous CA and inter-band CA would thus unlock increasing the channel BW (and thus cell throughput) to provide higher data rates
[n253]
n255
NR
NR
legacy services
n255
NR
legacy services
n256
NR
NR

## Slide 3: Rationale - UL Carrier Aggregation
NR NTN smartphone is UL link-budget limited, thus limiting how many PRBs can realistically be allocated
Higher PRB allocations are practically limited by PA Max Out Power (MOP) which reduces the UL Power Spectral Density (PSD) as more PRB are allocated
By making use of multiple mid-band PAs available on the device, allocating PRB groups to different PAs (intra-band, inter-band), we could increase the effective UL BW without compromising UL PSD. PA chain could be reused across TN-NTN bands, increasing number of available PAs.
2TX configurations with 4 PRBs could also be considered in addition
CA approach should be agnostic of the Power Class - even stronger applicability to higher-class devices with higher power and higher-gain, such as non-smartphone devices (e.g. CPE/FWA, automotive/vehicular, UAV/UAS, directional/high-gain UE
PA1
PA2
L-band UL
CC1
L-band UL
CC2
Intermods/
suppression/
leakages?
PA1
PA2
L-band UL
CC1
S-band UL
CC2
Intra-band
Inter-band 1
PA1
PA2
L-band UL
CC1
Ext L-band UL
CC2
Inter-band 2
e.g. 2PRB
e.g. 2PRB
e.g. 2PRB
e.g. 2PRB
e.g. 2PRB
e.g. 2PRB

## Slide 4: Objectives and General Principles
Identify and, if necessary, specify any missing requirements in order to support NTN-NTN intra-SAN Carrier Aggergation (CA), both intra-band and inter-band, with an initial focus on bands n255 and n256
Both DL and UL CA must be supported  UL leveraging 2 TX PAs independently on the UE
The Carrier Aggregation (CA) framework for NR NTN should be understood as generic at least for FR1 – applicable to any FR1-NTN band (current or upcoming), similar to TN
The existing R16 Terrestrial CA framework should be the baseline (R17 NR NTN was understood to be baselined on R16)
Work should focus only on the delta to support NTN, the majority of the framework from TN should be reused to maximize feature parity/commonality.
The framework could be later re-used as a baseline for FR2-NTN (e.g. Ka, Ku, etc)

## Slide 5: Initial NR NTN CA combination Proposals
Initial propose combinations focus on L-band and S-band (n255, [n253], n256)
Actual combinations to be further discussed.
New or Modified Combination | Band combination configuration | UpLink configuration | Subclass | Power class of band X | Tx number of band X | Power class of band Y | Tx number of band Y | Total Power class
New | CA_n255(2A) | CA_n255(2A) | NR only | PC3 | 2Tx | - | - | PC3
New | CA_n256(2A) | CA_n256(2A) | NR only | PC3 | 2Tx | - | - | PC3
New | CA_n253(2A) | CA_n253(2A) | NR only | PC3 | 2Tx | - | - | PC3
New | CA_n255A-n256A | CA_n255A-n256A | NR only | PC3 | 1Tx | PC3 | 1Tx | PC3
New | CA_n255A-n253A | CA_n255A-n253A | NR only | PC3 | 1Tx | PC3 | 1Tx | PC3
New | CA_n256A-n253A | CA_n256A-n253A | NR only | PC3 | 1Tx | PC3 | 1Tx | PC3

## Slide 6: Fragmented Spectrum support
Background:
Current NTN spectrum often hosts some legacy services
The total potential available spectrum for NTN is quite significant, but in some areas it may be interrupted by some narrowband legacy services – re-farming will likely take place, but will take time
Some chunks may be available that are just slightly smaller than a full NR channel BW, and would work best aggregated with a parent channel
An NTN operator may specify a wider NR CHBW and schedule signalling and user data around existing legacy services, but currently this is mostly left to implementation, and there are no explicit mechanisms to facilitate this mode of operation
Total allocation is not expected to exceed 50 MHz
5-10 MHz CH
2-3 MHz block
SSB
1CC UE BW
1CC – Max 50 MHz
2-3 MHz block
Objectives/Scope:
Identify minimum specification needed (if any) to facilitate aggregation of small fragmented spectrum blocks (smaller than the minimum NR Channel BW) through single wider Component Carrier of 50 MHz or less
Include this minimum objective as part of overall Fragmented Carriers SI/WI for Terrestrial Networks, to maximize commonality with TN design and avoid dedicated effort