## Slide 1: Rx switched nX-n29 low-low carrier aggregation
RP-241537
3GPP TSG RAN Meeting #104
Shanghai, China, 17th – 20st June, 2024
Agenda Item 9.1.5
Source: TELUS, Bell Mobility

## Slide 2: Motivation
Low-bands carry significant traffic volumes in Bell and TELUS urban and rural markets.
Considering n29 is DL only band, n29 capacity is completely lost in low-bands only coverage areas
Today’s low band challenge:
We are rich in mid-band spectrum (~300 MHz) which is effective closer to sites, however we have limited low-band spectrum (15 MHz) which propagates farther
As our customers move between sites (urban and rural), they’re spending more time in low-band coverage.
Low-band carries significant traffic volumes in urban and rural
  Our customers spend 15% of their day on average in urban low-bands, and 50% in rural low-bands
Low-band capacity challenge has a huge impact on customer experience. Users will experience poor data speeds due to low-band congestion.
Low-Low band CA is one way of solving this problem, however OEM’s have challenges to support low-low band CA and this ecosystem does not exist
B29 is widely deployed in our network and is underutilized
  Bell and TELUS together has nationwide access to 10 MHz of MBS – DL only (n29) in 700MHz spectrum.
  Band 29 reaches 83% of Canada’s pop.
We would like to propose a solution that enables low-low CA solution with minimal impact to the devices (next slide)
85% of traffic in urban
50% of traffic in rural
15% of traffic in urban
50% of traffic in rural
Mid-bands
Low-bands

## Slide 3: Potential low-low CA solution
Device needs to support inter-carrier scheduling: UE monitors n12 DL PDCCH DCI, which has both n29 and n12 scheduling
Device needs to support TTI level SOI switching; when n29 is scheduled, UE needs to switch to n29 filter, and during that slot there is no simultaneous n12 UL transmission / DL reception
Device switches back to n12 duplexer after n29 scheduled slot is finished
TTI :
TTI :
n12
Tx
Rx
n29
Rx
Transceiver
TTI :
n12
Tx
Rx
n29
Rx
Transceiver
n12
Tx
Rx
n29
Rx
Transceiver
This solution calls out specifically n29, but could apply to any DL only low band (e.g., n67)