## Slide 1: Discussion on introduction of PC2 and new Channel Bandwidth for n28
3GPP TSG RAN Meeting #104
Shanghai, China, Jun. 17-21, 2024
RP-241599 (Revision of RP-240931)
KDDI, Rakuten, NTT DOCOMO, Samsung, Nokia, Ericsson, Murata Manufacturing Co Ltd., Qualcomm,

## Slide 2: Background
PC2 n28 ) R4-2410558 , Apple
  For PC2 n28 discussion in RAN4, some companies assume only a full-band (single) duplexer, while the others assume dual duplexer. Proponents of dual duplexer insist that if single duplexer is assumed for PC2 requirements, then the current PC3 requirements should be relaxed, e.g. adding A-MPR>0, since the current PC3 n28 requirements are based on the dual duplexer assumption.
New NR CBWs ) R4-2407945 , CMCC/CBN
  Full-band single duplexer also brings another benefit, introducing new wider NR CBWs for n28, e.g. 40MHz for UE, 35MHz and 45MHz for both UE and gNB, which is not achievable with the current n28 UE RF requirements.

## Slide 3: Requirement Type and Candidate Solution
Requirement Type | PC3 | PC2 | New CBW | Legacy NW impacts | RF architecture | Candidate Solution | Solution
Type 1 (Legacy) | No A-MPR | No requirements | Not support | N/A | Dual duplexer | N/A | 
Type 2 | No A-MPR | A-MPR>0 | Support | No | Full-band duplexer with maintained performance | Maintained simulation assumptions | Solution 2-1
 |  |  |  |  |  | Modified simulation assumptions | Solution 2-2
 |  |  |  |  | New UE RF architecture (Full-band duplex+α, i.e. multi duplexers) |  | Solution 2-3
Type 3 | A-MPR>0 | A-MPR>0 | Support | Yes | Full-band duplexer with reduced/relaxed performance | Modified n28 A-MPR | Solution 3-1
 |  |  |  |  |  | RB restriction to avoid A-MPR impacts | Solution 3-2
 |  |  |  |  |  | New band | Solution 3-3
 |  |  |  |  |  | New NS for the existing CBW | Solution 3-4

## Slide 4: Observations
Observation 1 )
  Existing Japanese operators have already deployed their n28 NW based on their link-budget with no A-MPR for PC3.
Observation 2 )
  From legacy NW deployment perspective on coverage/performance, introducing a new set of PC3 A-MPR>0 requirements for n28 full-band duplexer (Type 3) brings critical issues to legacy NW.
Observation 3 )
  Introducing a new set of PC3 A-MPR>0 requirements for B28/n28 (Type 3) in later stage is an unprecedent change for 3GPP and not acceptable to n28 operators, non-backward compatible change in terms of deployment impacts (Relaxation is not acceptable).
Observation 4 )
  Having two sets of requirements (Type 2 and Type 3) causes market fragmentation, thus not acceptable either.
Observation 5 )
  Type 4 requirements (no A-MPR impacts but still requires RB restriction) are not acceptable either, since it brings loss of valuable RBs and capacity and huge impacts on legacy NW. (Relaxation is not acceptable).
Observation 6 )
  There was a discussion on NS_17 (PC3 no A-MPR) in RAN4 May meeting but no discussion for NS_18.

## Slide 5: Proposals
Proposal 1 )
  RAN agree to specify RAN4 requirements which enables PC2 in n28.
Proposal 2 )
  RAN agree to specify RAN4 requirements which enables wider CBW in n28.
Proposal 3 )
  RAN agree not to allow any relaxations for PC3 in n28. RAN4 will only consider solutions/requirements without any relaxations. (i.e. RAN agrees to allow only Type2 requirements)
Proposal 4 )
  RAN agree the text proposal for a new WID in the next slide.

## Slide 6: Text Proposal for Rel-19 new WID (modification from RP-241205/CMCC and CBN)
4.1 Objective of SI or Core part WI or Testing part WI
The objectives of this WI are to introduce requirements for UE Power Class 2 and 40MHz Channel Bandwidth for NR band n28, including the following aspects:
Introduce requirements for PC2 and those associated with following bullets
  Both 1Tx and 2Tx PC2 are supported
  UL-MIMO is supported.
  Specify A-MPR requirements for PC2
Introduce 40MHz Channel bandwidth located in UL: 703 - 743MHz and DL: 758 - 798MHz for band n28 supporting PC3 and PC2.
  Allow flexible channel allocations within the frequency range (UL: 703 - 743MHz and DL: 758 - 798MHz) for BW<40MHz.
Release independence of UE 40MHz Channel bandwidth to Rel-15 is anticipated unless new UE capability is introduced.
Maintain the current A-MPR requirements for NS_17 and any other applicable NS or emissions limits (i.e. no A-MPR for PC3) and avoid any impacts of legacy network (e.g. RB restriction)
NOTE: No new NS_17 A-MPR and RB restriction for PC3 to avoid the impacts on existing network operating with PC3.

## Slide 7
Appendix

## Slide 8: Cost impacts form KDDI’s business perspective
Still under internal estimation of KDDI’s cost impacts, but also, totally the worst case will cost + $1 billion (US).
The number of already deployed BSs for B28/n28 (as of 2023/Mar.).
  + 40,000 antenna sites
If PC3 A-MPR is added, our coverage area will be ↓14.9% based on our link-budget.
To avoid coverage shrink, the half of legacy antenna sites will be needed to replace from legacy BSs to new BSs for supporting PC3 A-MPR/RB restrictions. The other half of them will also be needed to develop those new features.
We’ve paid frequency migration cost to domestic broadcast companies depending on Tx power. Among domestic MNOs, our payment is highest due to the number of our antenna sites.
Note: The above cost estimation is only done by KDDI and not verified by co-sourcing companies.

## Slide 9
EOF