## Slide 1: R19 AI/ML for NR air interface study objective checkpoint discussion
Futurewei Technologies, Inc.
3GPP TSG RAN Meeting #105
Melbourne, AU, September 9 – 12, 2024
Agenda Item: 9.3.1.3
RP-241759

## Slide 2
Contents
Checkpoint for Rel-19 AI/ML for Air Interface
    Study Objectives
    Key Factors to Consider
Continued work of Rel-19: focused areas
Proposal of AI/ML for Air-Interface for Rel-19
Appendix
    Major remaining issues
    Summary of Rel-19 observations related to further study topics

## Slide 3: NR_AIML_Air Study objectives for September Checkpoint
Study objectives with corresponding checkpoints in RAN#105 (Sept ’24):
CSI feedback enhancement [RAN1]:
  For CSI compression (two-sided model), further study ways to:
    Improve trade-off between performance and complexity/overhead
      e.g., considering extending the spatial/frequency compression to spatial/temporal/frequency compression, cell/site specific models, CSI compression plus prediction (compared to Rel-18 non-AI/ML based approach), etc.
    Alleviate/resolve issues related to inter-vendor training collaboration.
while addressing other aspects requiring further study/conclusion as captured in the conclusions section of the TR 38.843.
  For CSI prediction (one-sided model), further study performance gain over Rel-18 non-AI/ML based approach and associated complexity, while addressing other aspects requiring further study/conclusion as captured in the conclusions section of the TR 38.843 (e.g., cell/site specific model could be considered to improve performance gain).
Necessity and details of model Identification concept and procedure in the context of LCM [RAN2/RAN1]
CN/OAM/OTT collection of UE-sided model training data [RAN2/RAN1]:
  For the FS_NR_AIML_Air study use cases, identify the corresponding contents of UE data collection
  Analyse the UE data collection mechanisms identified during the FS_NR_AIML_Air (TR 38.843 section 7.2.1.3.2) study along with the implications and limitations of each of the methods
Model transfer/delivery [RAN2/RAN1]:
  Determine whether there is a need to consider standardised solutions for transferring/delivering AI/ML model(s) considering at least the solutions identified during the FS_NR_AIML_Air study
Testability and interoperability [RAN4]:
  Finalize the testing framework and procedure for one-sided models and further analyse the various testing options for two-sided models, in collaboration with RAN1, and including at least:
    Relation to legacy requirements
    Performance monitoring and LCM aspects considering use-case specifics
    Generalization aspects
    Static/non-static scenarios/conditions and propagation conditions for testing (e.g., CDL, field data, etc.)
    UE processing capability and limitations
    Post-deployment validation due to model change/drift
  RAN5 aspects related to testability and interoperability to be addressed on a request basis
NOTE: offline training is assumed for the purpose of this project.
NOTE: the outcome of the study objectives should be captured in TR 38.843 for future reference.
NOTE: Coordination with SA/SA WGs of the ongoing study/work as it may relate to their required work.

## Slide 4: NR_AIML_Air Study Objectives for September Checkpoint and Status
RAN WG | Area | Objective | Status | Remarks
RAN1 | CSI compression | Improve trade-off between performance and complexity/ overhead | Partially completed | Studied spatial/temporal/frequency CSI compression cases with and without CSI prediction and agree to focus on Case 2/3 which show further gain but may have higher complexity.
 |  | Alleviate/resolve issues related to inter-vendor training collaboration | Partially completed | 5 options and 3 direction with 10 issues were identified. No conclusion on recommendation and no time in discussing the identified directions/issues.
 | CSI prediction (1-sided model) | Study performance gain over Rel-18 non-AI/ML based approach and associated complexity | Completed | Performance improvement (small to medium) is observed with increased complexity.
RAN2/1 | Other aspects | Necessity and details of model Identification concept and procedure | Partially completed | No conclusion on necessity (only applicable use case is determined). Not all options have procedures studied. RAN 1 concluded to further study Model identification.
 |  | Collection of UE-sided model training data | Partially completed | No consensus on the feasibility of UP solution for Option 2&3; No consensus on the level of MNO controllability and visibility possible via solution 1b).
 |  | Model transfer/delivery | Partially completed | Still 3 options on the table: Case y, z1 and z4; “Known model structure” needs further study. RAN 1 concluded to further study Model transfer/Model delivery.
RAN4 | Testing apsects | Testability and interoperability | Partially completed | 

## Slide 5: Key factors to consider for the checkpoint
Key factors to consider at solution level
  Balance robust performance + air-interface overhead reduction and complexity
  Minimize inter-vendor collaboration effort
  Note: Considering above, identifying a smaller scope with limited set of options/cases is more important for 5G Advance than supporting more functions and/or full flexibility.
Readiness for normative work
  Many identified issues remain to be addressed.
  Some of the options identified in WID do not have sufficient results or show significant gain.
  Supporting the normative work for 2-sided model in the remainder part of Rel-19 would not be feasible.
    RAN1 agenda item 9.1.3.2 for CSI compression and 9.1.3.3 for AI/ML model and data have both concluded that extending the study is recommended.
Preparing AI/ML framework for longer term
  Thorough study on 2-sided model and the associated mechanism(s) to reduce the inter-vendor collaboration effort is beneficial for longer term support of AI/ML use cases in Rel-19 and 6G.
  Extend the study phase to the remainder of Rel-19 and only focus on the identified down-selected options/cases.

## Slide 6: Continued work of R19: focused areas
Extend the study for CSI Compression and AI/ML Model and Data for the remainder duration of Rel-19.
Among the identified options for inter-vendor training collaboration:
  Further study to determine few practical solutions for real deployment scenario.
  Focus on balancing device optimization flexibility and collaboration and specification effort/impact needed.
Identify few among focused CSI compression cases (and associated options in each) that can balance performance, air-interface overhead and complexity.
  Conduct thorough evaluation on prioritized options/cases in the following aspects and consider further down-selection:
    Model generalization
    Performance monitoring accuracy of CSI compression cases for identified/prioritized inter-vendor training collaboration options.
  Based on the outcome of study for focused CSI compression case(s) involving CSI prediction, RAN1 to determine supporting either joint CSI prediction and CSI compression OR separate CSI prediction and CSI compression for normative work.
For each prioritized inter-vendor training collaboration option and TSF case:
  Identify potential specification impacts, including
    Data collection mechanism(s) for training, inference and accurate monitoring, including cause identification when performance degradation occurs.
    Signaling and protocol enhancement(s) if needed and associated procedures.
    LCM and incurred enhancements for supporting 2-sided model(s)
For other aspects and RAN2:
  Decide whether model identification is necessary and its applicable use cases/scenarios, including clarification regarding concepts such as associated ID and the relationship between model ID and associated ID.
  Identify/down-select the option for model transfer/delivery, including the definition of known model structure, if Case 4z is selected.
  Resolve remaining issues associated with data collection for UE-side model training, such as feasibility of UP solution for data collection Option 2 & 3, as well as issues related to MNO’s controllability and visibility of collected data for Option 1b).

## Slide 7: Proposal of AI/ML for Air Interface for Release 19
From the study aspects of NR_AIML_Air:
  Further extend the study of CSI compression and AI/ML model.
  Extend the study to the entire duration of Rel-19.
  For RAN1, consider at least the following in the scope:
    Prioritize one or few practical solution option(s), i.e., Option 3 and/or 4 to alleviate inter-vendor training collaboration for real deployment scenario.
    Prioritize among identified CSI compression cases to balance performance, air-interface overhead, complexity and specification effort.
    Thorough evaluation on prioritized options/cases, focusing on model generalization and accuracy of performance monitoring, including root cause identification.
    Identify potential specification impacts for each prioritized inter-vendor training collaboration option and TSF case.
  For RAN2, consider data collection management, model delivery/transfer, model/functionality Identifications and corresponding LCMs, and UE capability enhancements for dynamic capabilities.
Standards impacts considerations
  Identify potential specification impact for prioritized option(s)/case(s) with essential LCM operations while considering longer-term benefits and support for AI/ML framework.

## Slide 8: Appendix

## Slide 9: Major Remaining RAN1 Issues (as of RAN1 #118) on AI/ML model and data
General framework to support online training, over-the-air training, and model update.
Handling of NW-side and/or UE-side additional conditions
  For inference for UE-side models, many options were proposed by companies to ensure consistency between training and inference regarding NW-side additional conditions if identified, however, no consensus reached on many aspects due to lack of time.
  No time to discuss the options regarding UE-side additional conditions to ensure consistency between training and inference.
Further details of over-the-air (i.e., online) model identification and two-sided model pairing
For model identification of UE-side or UE-part of two-sided models, example use cases of online identification (Type B1 and Type B2) and offline identification (Type A), limited examples were discussed/agreed due to lack of time.
Functionality and Model-ID based LCMs:
  Unified approach/procedure or not
  The applicability and necessity of Model-ID based LCM
    Based on functionality-based LCM or independent?
Model transfer/delivery: some pros and cons were discussed but further study/discussion is needed for the necessity and its applicability to the studied sub use cases.
Performance monitoring of inactive model(s) and the associated complexity.
To be updated based on SR from Rapporteur

## Slide 10: Major Remaining RAN2 Issues (as of RAN2 #125)
Data collection management for model training and performance monitoring:
  enhancements to existing data collection framework
  signaling for data collection
Model delivery/transfer:
  inter-vendor solutions,
  security issues (especially via third-party servers)
Model/Functionality Identifications and LCM:
  online model identification procedure
  model-pairing for 2-sided models
  meta information
  signaling for LCM
UE capability enhancements:
  ways to report dynamic capabilities for data collection, model storage and model inference (postponed to WI phase)
  definition of AI/ML related Features/FGs (postponed to WI phase)
To be updated based on SR from Rapporteur

## Slide 11: Major Remaining RAN4 Issues (as of RAN4 #112)
Options of testing goals were set with many items that require further study.
  Option 1: The testing goal is to verify whether a specific AI/ML model (if model identification is possible)/functionality can be conducted in a proper way.
    FFS how to define the specific AI/ML model (e.g., a model captured in RAN4 spec as baseline)
    FFS how to define that the model is properly conducted (e.g., by defining AI/ML dedicated performance/core requirements associated with model outputs)
  Option 2: The testing goal is to verify whether the minimum performance gain of AI/ML model (if model identification is possible) /functionality/feature can be achieved for a static scenario/configuration.
    FFS how to define a static scenario/configuration (e.g., by defining a related testing dataset based on channel models in TR 38.901)
    FFS whether and how to define non-static specific scenarios/configurations
Other important RAN4 issues that have not been resolved.
  Requirements for data collection (what will be the requirements? are they testable? and how to test them?)
  Requirements for model delivery/update/transfer
  Performance monitoring/evaluation for LCM (definition of requirements for dynamically changing scenarios, accuracy of monitoring, setting the ground truth, performance degradation)
  Test encoder/decoder for 2-sided models: the feasibility of any of the testing options has not concluded and more study is required.
  Testing of interoperability for different collaboration levels.
To be updated based on SR from Rapporteur

## Slide 12: Summary of Observations for RAN1 progress (1/4)
Observation #1:
For alleviating/resolving issues related to inter-vendor training collaboration:
Companies agree to support 2 directions for inter-vendor training collaboration options 3, 4 and the associated sub-options in each:
  Direction A: Sharing parameters/reference model/dataset that enables UE-side offline engineering (Inter vendor collaboration option 3a/5a/4)
  Direction B: Sharing NW side encoder parameter to UE side for UE side inference directly with on-device operation (Inter vendor collaboration option 3b)
  Direction C: Fully standardized reference model(s) and parameters with specified CSI generation part and/or CSI reconstruction part
A set of study points were also identified for each direction in RAN1#118 with at least a total of 10 issues [5].
As identified/agreed in the RAN1 meeting prior to September checkpoint, there is no study or discussion of the details for each issue with potential down-selection possibility.
RAN1 is recommending extending
  the study of the AI/ML CSI compression
  the study of the Model identification, and Model transfer/Model delivery

## Slide 13: Summary of Observations for RAN1 progress (2/4)
Observation #2:
For extending the spatial/frequency compression to spatial/temporal/frequency compression:
5 temporal-domain (TSF) CSI compression cases were identified while Case 0 covers only spatial-frequency domain CSI compression [2].
Companies agree to focus on Case 2 and Case 3.
As of RAN1#118:
  No results were submitted for model generalization evaluation and multi-vendor joint training.
  Only 2 sources submitted results for separate training.
  No evaluation for the performance on model performance monitoring for any of the TSF cases (model performance monitoring evaluation for Case 0 was performed in Rel-18)
Case | Target CSI slot(s) | Whether the UE uses past CSI information | Whether the network uses past CSI information
0 | Present slot | No | No
1 | Present slot | Yes | No
2 | Present slot | Yes | Yes
3 | Future slot(s) | Yes | No
4 | Future slot(s) | Yes | Yes
5 | Present slot | No | Yes

## Slide 14: Summary of Observations for RAN1 progress (3/4)
Observation #3:
For cell/site specific models:
2 options were identified for the evaluation of AI/ML-based CSI compression using localized models in Release 19 [2]:
As of RAN1#118:
  No conclusive observations
    Only 2 sources in total submitted results for system level performance (mean and 5% UPT) comparison with either the benchmark or comparison with global model(s) spread across various options.
  All submitted results based on result templates (except from 1 source) are for spatial-frequency CSI compression (no past CSI information).
  No conclusion whether localized model can improve trade-off between performance and complexity/overhead.
  .
  Option 1: The dataset is derived from UEs dropped within the local region, with spatial consistency modelling as per TR 38.901.
    E.g., Dropped in a specific cell or within a specific boundary.
  Option 2: By using a scenario/configuration specific to the local region.
    E.g., Indoor-outdoor ratio, LOS-NLOS ratio, TXRU mapping, etc.

## Slide 15: Summary of Observations for RAN1 progress (4/4)
Observation #4:
The study objectives identified in the NR_AIML_AIR WID [1] for CSI compression (two-sided model) include 2 main items.
Up till RAN1#118, of the identified study objectives for CSI compression:
Evaluations/observations for improving the trade-off between performance and complexity/overhead are either not being conducted, e.g., model generalization, or non-conclusive with results from only few sources.
Options identified for alleviating/resolving issues related to inter-vendor training collaboration have been discussed and at least 10 issues across these option have been identified, BUT no study/discussion has been performed for these issues.
  For CSI compression (two-sided model), further study ways to:
    Improve trade-off between performance and complexity/overhead
      e.g., considering extending the spatial/frequency compression to spatial/temporal/frequency compression, cell/site specific models, CSI compression plus prediction (compared to Rel-18 non-AI/ML based approach), etc.
    Alleviate/resolve issues related to inter-vendor training collaboration.

## Slide 16: Summary of Observations for RAN1 progress (4/4)
Observation #5:
On the general/other aspects, RAN1/2 were tasked, in the study phase, to determine
  Necessity and details of model Identification concept and procedure in the context of LCM [RAN2/RAN1]
  Collection of UE-sided model training data [RAN2/RAN1]
  Model transfer/delivery [RAN2/RAN1]
From RAN1 aspects
  The necessity of model identification has not been concluded. Instead, RAN1 concluded that it is at least applicable to some of inter-vendor training collaboration option(s) of CSI compression using two-sided model.
  While example procedures for MI-Option 1 and MI-Option 2 are provided, procedures for MI-Option 3 (via model transfer) and MI-Option 4 (via reference model) have not been determined.
    Even for MI-Option 1 and MI-Option 2, there are many issues to be resolved, such as the working range of associated ID, the relationship between associated ID and model IDs, the entity that assigns the model ID and so on.
  Model transfer/delivery was identified necessary at least for some of inter-vendor training collaboration option(s) of CSI compression using two-sided model (if supported). However, there are still three options left on the table after deprioritizing other three options.
  On data collection for UE-sided model training, RAN1 believed it has determined the data content to be collected in R18, so the work was left to RAN2.
RAN1’s conclusion of this study: RAN1 is recommending extending the study of the Model identification, and Model transfer/Model delivery based on RAN1 understanding the study is not completed.

## Slide 17: Summary of Observations for RAN2 progress
Observation #6:
RAN2, as the leading WG for the study objectives, were tasked to determine
  Necessity and details of model Identification concept and procedure in the context of LCM [RAN2/RAN1]
  Collection of UE-sided model training data [RAN2/RAN1]
  Model transfer/delivery [RAN2/RAN1]
In the development, major effort has been put on the following core part of the WI (not the SI).
  LCM for both NW-side and UE-side models, for both Beam Management and Positioning use cases.
  Data collection for both NW-side and UE-side model trainings.
The main objective that has been studied was on the collection of UE-sided model training data. However, there are still many issues with the study. The following is a partial list.
  RAN2 couldn’t reach consensus on the feasibility of UP solution for data collection Option 2 & 3.
  RAN2 cannot reach consensus on the level of MNO controllability and visibility possible via solution 1b without input from SA groups.
  RAN2 has not concluded on the need for partial and no visibility option.
In addition, RAN2 was confused by some RAN1 concepts, such as associated ID etc.
  RAN2 will be working on a list of questions to be sent to RAN1 for clarification after the August meeting. Before that, it is hard to conclude that the study has been completed.

## Slide 18: Related Agreements for Other Aspects of AI/ML Model and Data: RAN1#118
Agreement
RAN1 is recommending extending the study of the Model identification, and Model transfer/Model delivery based on RAN1 understanding the study is not completed.

## Slide 19: Related Agreements for CSI Compression: RAN1#118
  For CSI compression (two-sided model), further study ways to:
    Improve trade-off between performance and complexity/overhead
      e.g., considering extending the spatial/frequency compression to spatial/temporal/frequency compression, cell/site specific models, CSI compression plus prediction (compared to Rel-18 non-AI/ML based approach), etc.
    Alleviate/resolve issues related to inter-vendor training collaboration.
while addressing other aspects requiring further study/conclusion as captured in the conclusions section of the TR 38.843.
Agreement
According to the Rel-19 study objective,
RAN1 is recommending extending the study of the AI/ML CSI compression based on RAN1 understanding the study on CSI compression is not completed.

## Slide 20: Related Agreements for CSI Compression: RAN1#118
Agreement
Continue the study of following directions - on-device operation and UE side offline engineering
Direction A: Sharing parameters/reference model/dataset that enables UE-side offline engineering (Inter vendor collaboration option 3a/5a/4)
  Potential down-selection into one or more among sub-options 3a/5a-1, 3a/5a-2, 3a/5a-3, 4-1, 4-2, and 4-3 considering their feasibility and performance, including at least the following issues
    [Issue 1] What additional information should be shared from NW-side to UE-side to enable UE-side encoder training, validation, and testing?
    [Issue 2] Is there concern for NW’s proprietary information disclosure, and if so, how to address it?
    [Issue 3] Is there an overhead concern, and if so, how to address it?
    [Issue 4] Is there performance impact due to mismatch between NW side data distribution and UE side data distribution, and if so, how to address it?
Direction B: Sharing NW side encoder parameter to UE side for UE side inference directly with on-device operation (Inter vendor collaboration option 3b), including at least the following issues
  [Issue 3] Is there an overhead concern, and if so, how to address it?
  [Issue 5] Whether it is feasible to use a common encoder across UEs, and whether it is feasible for NW-side to train multiple encoders for different UEs?
  [Issue 6] Is there performance impact due to mismatch between NW side data distribution and UE side inference data distribution, and if so, how to address it?
  [Issue 7] Is there concern for NW’s and UE’s proprietary information disclosure, and if so, how to address it?
Direction C: Fully standardized reference model(s) and parameters with specified CSI generation part and/or CSI reconstruction part (Inter vendor collaboration option 1), including at least the following issues
  [Issue 8] Whether to consider 3GPP’s statistical channel model or field data for reference model(s) training. In case of the latter, how does RAN1 collect field data and agree on them?
  [Issue 9] Is there performance impact due to mismatch between the distribution of the dataset used for reference model(s) training, UE-side data distribution, and NW-side data distribution, and if so, how to address it?
  [Issue 10] What additional information should be specified to enable UE-side encoder training, validation, and testing, and UW-side decoder training, validation, and testing?
  Note:
    1-1: Only reference encoder is specified, and NW-side and/or UE-side may train their actual CSI generation part and NW-reconstruction part separately compatible to the reference encoder.
    1-2: Only reference decoder is specified, and NW-side and/or UE-side may train their actual CSI generation part and NW-reconstruction part separately compatible to the reference decoder.
    1-3: Both reference encoder and reference decoder are specified, and NW-side and/or UE-side may train their actual CSI generation part and NW-reconstruction part separately that are compatible to the reference decoder/encoder.
Note: UE-side data and NW-side data in “UE-side data distribution” and “NW-side data distribution” are field data.
Note: Some issues identified in one direction may/may not be applicable for other Direction.
Note: potential down selection among the 3 directions is not precluded
Study of data distribution mismatch to consider the use of synthetic data and/or field data.

## Slide 21: Related Agreements for CSI Compression: RAN1#116
Agreement
To alleviate / resolve the issues related to inter-vendor training collaboration of AI/ML-based CSI compression using two-sided model, study the following options:
Option 1: Fully standardized reference model (structure + parameters)
Option 2: Standardized dataset
Option 3: Standardized reference model structure + Parameter exchange between NW-side and UE-side
Option 4: Standardized data / dataset format + Dataset exchange between NW-side and UE-side
Option 5: Standardized model format + Reference model exchange between NW-side and UE-side
Note 1: The above options may not be mutually exclusive and may be used together.
Note 2: Other options are not precluded.
Note 3: The study should consider how different methods of exchanging the parameters / dataset / reference model would affect the feasibility and collaboration complexity of options 3 / 4 / 5 respectively, e.g., over the air-interface, offline delivery, etc.
Note 4: “Dataset” refers to a set of data samples of CSI feedback and associated target CSI.

## Slide 22: Related Agreements for CSI Compression: RAN1#116
Agreement
For Option 3, further define the two sub-options:
  3a: Parameters received at the UE or UE-side goes through offline engineering at the UE-side (e.g., UE-side OTT server), e.g., potential re-training, re-development of a different model, and/or offline testing.
  3b: Parameters received at the UE are directly used for inference at the UE without offline engineering, potentially with on-device operations.
For Option 5, further define the two sub-options:
  5a: Model received at the UE or UE-side goes through offline engineering at the UE-side (e.g., UE-side OTT server), e.g., potential re-training, re-development of a different model, and/or offline testing.
  5b: Model received at the UE are directly used for inference at the UE without offline engineering, potentially with on-device operations.
For Option 4, it is clarified that:
  Dataset received at the UE or UE-side goes through offline engineering at the UE- side (e.g., UE-side OTT server), e.g., model training or offline testing.
Note: The descriptions under each option are only for the purpose of simplified discussion and do not mean deprioritizing any other flavors (such as an exchange originating from the UE-side and ending at the NW-side) from potential specification.

## Slide 23: Related Agreements for CSI Compression: RAN1#116
Agreement
For Option 3/4/5, focus further discussion on the following assumptions:
  Option 3a/5a
    The model(5a)/parameter(3a) exchange originates from the NW-side and ends at the UE-side.
    Model(5a)/parameters(3a) exchanged from the NW-side to UE-side is either CSI generation or reconstruction part or both.
      Option 3a-1/5a-1: Model/Parameters exchanged from the NW-side to UE-side is CSI generation part.
      Option 3a-2/5a-2: Model/Parameters exchanged from the NW-side to UE-side is CSI reconstruction part.
      Option 3a-3/5a-3: Model/Parameters exchanged from the NW-side to UE-side are both CSI generation part and CSI reconstruction part.
      Some additional information, if necessary, may be shared from the NW-side to help UE-side offline engineering and provide performance guidance.
        Performance target
        Dataset or information related to collecting dataset
    Study different methods of exchanging, e.g., over the air-interface, offline delivery, etc.
  Option 3b
    The method of exchanging is over the air-interface via model transfer/delivery Case z4.
    The parameter exchange is from NW to UE.
    Parameters exchanged from the NW-side to UE-side is CSI generation part.
  Option 5b
    The method of exchanging is over the air-interface via model transfer/delivery Case z4, assuming that the model structure is aligned based on offline inter-vendor collaboration.
    The model exchange is from NW to UE.
    Model exchanged from the NW-side to UE-side is CSI generation part.
  Option 4:
    The dataset exchange originates from the NW-side and ends at the UE-side.
    Option 4-1: Dataset exchanged from the NW-side to UE-side consists of (target CSI, CSI feedback).
    Option 4-2: Dataset exchanged from the NW-side to UE-side consists of (CSI feedback, reconstructed target CSI).
    Option 4-3: Dataset exchanged from the NW-side to UE-side consists of (target CSI, CSI feedback, reconstructed target CSI).
    Some additional information, if necessary, may be shared from the NW-side to help UE-side offline engineering and provide performance guidance.
      Performance target
    Study different methods of exchanging, e.g., over the air-interface, offline delivery, etc.
  Note: For each option/sub-option of interest, companies to bring discussion on how inter-vendor collaboration complexity, interoperability, and feasibility may be addressed. Companies to strive to provide solution(s) that can address all the following aspects: inter-vendor collaboration complexity, performance, interoperability, and feasibility.
  Note: The descriptions under each option are only for the purpose of simplified discussion and do not mean deprioritizing any other flavors (such as an exchange originating from the UE-side and ending at the NW-side) from potential specification.

## Slide 24: Table 7.2.1.3.2-1. Analysis of different data collection options for UE-side model training.
Option Aspect | Option 1a) | Option 1b) | Option 2 | Option 3
First termination entity | OTT Server Training entity (e.g., Over-The-Top (OTT) server) | Server for data collection for UE-side model training | Inside the CN (e.g., LMF) | Inside OAM domain
AI/ML-specific Data Transfer Path | UE to OTT server via either 3GPP or non-3GPP network | UE ->CN->Server for data collection for UE-side model training/OTT server (Note 4) | UE-> CN -> Server for data collection for UE-side model training/OTT server (Note 4) | UE-> gNB->OAM -> Server for data collection for UE-side model training/OTT server (Note 4)
UP/CP tunnel | UP tunnel (for the case of data transfer from UE to OTT server via 3GPP network) | UP tunnel | CP tunnel (provided that the data volume remains within the NAS signalling capacity) FFS: UP tunnel (Note 7) | CP tunnel (provided that the data volume remains within the RRC signalling capacity) FFS: UP tunnel (Note 7)
Protocol layer for data transfer | Application layer | Application layer | NAS layer for CP tunnel FFS: the protocol layer for UP tunnel | RRC layer for CP tunnel FFS: the protocol layer for UP tunnel
Controllability of MNO on data transfer (Note 1) | No AI/ML specific controllability | Has controllability FFS: level of controllability (Note 5) | Full controllability | Full controllability
Solution for network controllability | N/A (the OTT server can directly request data from the UE) | Example: per PDU sessions | NAS procedure, FFS impact to other layers Via NAS procedure or FFS other procedures | Via RRC procedure
Possible Options for Visibility of data content in MNO and Data format (Note 2, Note 3) | No standardized visibility | FFS on level of visibility (Note 5) | Opt A) Full visibility for standardized data content. Opt B) Partial visibility for partially standardized data content. (Note 6) Opt C) No standardized visibility (Note 6). FFS: meaning of ‘partial/partially’ SAME for OPTION 3 | Opt A) Full visibility for standardized data content. Opt B) Partial visibility for partially standardized data content. (Note 6) Opt C) No standardized visibility. (Note 6) FFS: meaning of ‘partial/partially’ and how to achieve different levels of visibility
Impacted WGs | N/A | SA2, SA3, RAN2, RAN3, CT1 | SA2, SA3, RAN3, RAN2, CT1 and CT3 | RAN2, RAN3, SA3, SA5, SA2
Note 1: Full controllability: The MNO can manage data transfer to the server for UE-side data collection, without the need of SLA. This includes initiating, terminating, and fully managing data transfer. Note 2: Visibility of data content signifies that the MNO can at least, be aware of, access, and comprehend the data without the need of SLA. Note 3: The following options are identified to realize the different levels of data content visibility to the MNO: Full visibility for standardized data content. Partial visibility for partially standardized data content (e.g. UE proprietary information can be included transparently together with the standardized data message). No standardized visibility (e.g. only UE proprietary information can be included tranperantly) Note 4: The potential involvement of NF or other higher layers entities/functionalities should be discussed in other WGs. Impact on the OTT server is not in the scope of RAN2 discussion. Note 5 RAN2 cannot reach consensus on the level of MNO controllability and visibility possible via solution 1b without input from SA groups Note 6: RAN2 has not concluded on the need for partial and no visibility option Note 7: RAN2 couldn’t reach consensus on the feasibility of UP solution |  |  |  | 

## Slide 25: References
[1] RP-234039, New WID on Artificial Intelligence (AI)/Machine Learning (ML) for NR Air Interface, Qualcomm (Moderator), RAN#102.
[2] R1-2401766, Session notes for 9.1 (Artificial Intelligence (AI)/Machine Learning (ML) for NR Air Interface), Ad-hoc Chair (CMCC), RAN1#116.
[3] R1-2403662, Session notes for 9.1 (Artificial Intelligence (AI)/Machine Learning (ML) for NR Air Interface), Ad-hoc Chair (CMCC), RAN1#116bis.
[4] R1-2405695, Session notes for 9.1 (Artificial Intelligence (AI)/Machine Learning (ML) for NR Air Interface), Ad-hoc Chair (CMCC), RAN1#117.
[5] R1-2407478, Session notes for 9.1 (Artificial Intelligence (AI)/Machine Learning (ML) for NR Air Interface), Ad-hoc Chair (CMCC), RAN1#118.