## Slide 1: Discussion on AI/ML for air interface WI

## Slide 2: Check points for RAN#105
In RAN#105, there is a checkpoints for following additional studies on AI/ML for air interface.
  CSI feedback enhancement [RAN1]
    CSI prediction
    CSI compression
  Model identification [RAN2/RAN1]
  Data collection for UE-sided model training [RAN2/RAN1]
  Model transfer/delivery [RAN2/RAN1]
  Testability and interoperability [RAN4]
The conclusion from RAN1 for above study is that,
  For CSI prediction,
    from RAN1 perspective, study of CSI prediction has been completed and performance improvement is observed with increased complexity.
  For CSI compression,
    RAN1 is recommending extending the study of the AI/ML CSI compression based on RAN1 understanding the study on CSI compression is not completed.
  For model identification and model transfer/delivery
    RAN1 is recommending extending the study of the Model identification, and Model transfer/Model delivery based on RAN1 understanding the study is not completed.

## Slide 3: CSI prediction
In RAN1#118 meeting, following observation and conclusion was achieved,
  As shown above, AI/ML based CSI prediction can be beneficial in terms for performance perspective. Therefore, it is proposed to recommend for normative work within Rel-19 timeframe.
  One consideration point is the scope of CSI prediction, since limited meetings are left in Rel-19. One way is to reuse Rel-18 CSI framework as much as possible. For example, Rel-18 codebook can be reused.
Proposal #1
  CSI prediction using UE-sided model is recommended for normative work within Rel-19 timeframe including at least following
    Necessary signaling/mechanism(s) to facilitate LCM operations specific to the CSI prediction use case, if any
    Note: Rel-18 CSI framework can be a starting point, and codebook enhancement is not considered.
Observation
Based on the evaluation for CSI prediction, the following high-level observations are provided:
From the perspective of basic performance gain over benchmark of non-AI/ML based CSI prediction, under the same UE speed for training and inference
  for AI/ML based CSI prediction over non-AI/ML based CSI prediction, 0%~7.8% gain depending on traffic model, in terms of mean UPT, is observed by 7 sources
  for AI/ML based CSI prediction over non-AI/ML based CSI prediction, 3.8%~20.7% gain depending on traffic model, in terms of 5% UE UPT, is observed by 7 sources.
From a perspective of AI/ML complexity, 19 sources adopt the model subject to the computational complexity in units of FLOPs from 0.05M to 3000M. For complexity of non-AI/ML benchmark, 16 sources adopt the algorithm (e.g., Kalman filter, Auto-regression, Wiener filter) subject to the computational complexity in units of FLOPs from 0.14M to 107M. The ratio of FLOPs (AI/ML over benchmark 2) ranges from 1 to 35, which is used by majority sources. For non-AI/ML benchmark, main computation complexity is dominated by filter updates, which may not be need to be updated per inference at the expense of performance loss.
From the perspective of performance impact on channel estimation error and phase discontinuity, compared to non-AI/ML CSI prediction, higher gain is observed by 10 sources for AI/ML based CSI prediction in the presence of channel estimation error or phase discontinuity.
From the perspective of generalization over various scenarios/configurations (e.g., various UE speed, deployment scenario, carrier frequency) that have been evaluated, compared to generalization Case 1 where the AI/ML model is trained with dataset subject to a certain scenario#B/configuration#B and applied for inference with a same scenario#B/configuration#B
  For generalization Case 2 where the AI/ML model is trained with dataset from a different scenario#A/configuration#A, generalized performance may be achieved for some certain combinations of scenario#A/configuration#A and scenario#B/configuration#B but not for others.
  For generalization Case 3 where the training dataset is constructed with data samples subject to multiple scenarios/configurations including scenario#B/configuration#B, generalized performance of the AI/ML model can be achieved.
Agreement
From RAN1 perspective, study of CSI prediction has been completed and performance improvement is observed with increased complexity.

## Slide 4: CSI Compression
In RAN1#118, followings are agreed
In our understanding,
  Although spatial/temporal/frequency compression provides higher gain compared to spatial/frequency compression (Rel-18), overhead/complexity perspective needs to be further studied.
  Further feasibility study is required for options/sub-options to handle inter-vendor training collaboration
Proposal #2
  AI/ML CSI compression using two-sided model is recommended to further study for whole Rel-19 timeframe, including at least
    Feasibility study for options/sub-options to handle inter-vendor training collaboration
    Trade-off between performance and complexity
.
Agreement
According to the Rel-19 study objective,
RAN1 is recommending extending the study of the AI/ML CSI compression based on RAN1 understanding the study on CSI compression is not completed.

## Slide 5: Model identification and model transfer/delivery
In RAN1#118, followings are agreed
In our view,
  Model identification and model transfer is mainly beneficial for two-sided model. Given the situation that the study CSI compression has not been completed, extension of study on CSI compression is expected.
  Therefore, the scope of study should be focus on two-sided model.
Proposal #3
  The study of the Model identification, and Model transfer/Model delivery is recommended to further study for whole Rel-19 timeframe
    Note: the scope of study should be focus on two-sided model
.
Conclusion
• From RAN1 perspective, model identification is at least applicable to some of inter-vendor training collaboration option(s) of CSI compression using two-sided model (if supported)
Conclusion
From RAN1 perspective, model transfer is needed at least for some (e.g., Option 3b) of inter-vendor training collaboration option(s) of CSI compression using two-sided model (if supported)
Agreement
RAN1 is recommending extending the study of the Model identification, and Model transfer/Model delivery based on RAN1 understanding the study is not completed.

## Slide 6: Summary
Proposal #1
  CSI prediction using UE-sided model is recommended for normative work within Rel-19 timeframe including at least following
    Necessary signaling/mechanism(s) to facilitate LCM operations specific to the CSI prediction use case, if any
    Note: Rel-18 CSI framework can be a starting point, and codebook enhancement is not considered.
Proposal #2
  AI/ML CSI compression using two-sided model is recommended to further study for whole Rel-19 timeframe, including at least
    Feasibility study for options/sub-options to handle inter-vendor training collaboration
    Trade-off between performance and complexity
Proposal #3
  The study of the Model identification, and Model transfer/Model delivery is recommended to further study for whole Rel-19 timeframe
    Note: the scope of study should be focus on two-sided model
.