## Slide 1: Background on “LTE D2D Proximity Services” Study Item proposal
Qualcomm
3GPP TSG RAN #58
December 4-7, 2012, Barcelona, Spain
RP-121699

## Slide 2: Background up to RAN/SA #57
SA1 Feasibility Study on Proximity Services opened in September 2011
  Focused on both device-to-device discovery and communication, for both in network and out of network coverage
Increased interest to migrate public safety services to LTE, e.g.
  US Dept of Commerce: RWS-120033 (input to 3GPP RAN Rel-12 workshop)
  TCCA: SP-120381 & SP-120456 (inputs to TSG SA on LTE interest from the TETRA industry)
  Vodafone: SP-120630 (input to SA Plenary)
  LTE Device-to-Device always identified as key / must-have requirement
RAN Study Item on LTE Device to Device Proximity Discovery submitted in RAN #57
  RP-121435
  Focused on discovery only
  27 supporting companies
  Postponed to RAN #58 with all other new Rel-12 proposals

## Slide 3: Events in the last quarter
LS from SA Plenary to SA1 (cc RAN) urging to progress on ProSe
  SP-120651 / RP-121485
    SA would like to inform SA1 of the need to agree a normative work item for ProSe. This will allow the urgent needs of the Public Safety and Critical Communications community to be addressed. To enable economy of scale advantages, the requirements should ensure that the resulting system can be used for both Public Safety and non-Public Safety services, where possible
SA1 Feasibility Study on Proximity Services concluded in November 2012
  TR 22.803 sent to SA Plenary for approval (S1-124203)
  95% completion level
  TR conclusions:
    The Feasibility Study for Proximity Services (ProSe) Technical Report analyses several use cases of ProSe for both general and public safety use. The use cases address two key aspects of ProSe:
    Discovery, and
    Communication via an optimized path.
    Taking into consideration the Use Cases and Scenarios defined in Clause 5, new potential requirements related to UE operations, network operations, charging and security for ProSe have been identified in Clause 5 with additional potential requirements in Clauses 6.1, 6.2, 6.3, and 6.4.
    It is recommended to proceed with normative work.

## Slide 4: Events in the last quarter (cont.)
SA1 & SA2 also agreed to a normative work item
    S1-124396 (SA1 version) & S2-124826 (addition of SA2 objectives)
    SA1 reports the above progress to SA & RAN in S1-124515 / RP-121481
Scope of the agreed SA1/SA2 work item
  ProSe Discovery over EUTRA
    Within network coverage
    Outside network coverage, only for Public Safety
  ProSe Communication over EUTRAN
    Within network coverage
    Outside network coverage, only for Public Safety
  EPC support of ProSe Communication over WLAN
    No impact to RAN

## Slide 5: Proposed RAN Study Item
A RAN study item is proposed on LTE Device to Device Proximity Services
  Includes both discovery & communication to meet all service requirements described & endorsed by SA1 & SA2, and those coming from Public Safety
Scope of proposed RAN study item
  LTE proximity discovery within network coverage => multiple use cases / requirements
  LTE direct communication within network coverage => focused on public safety
  LTE D2D (discovery & communication) outside network coverage => for public safety
  Note discovery & communication will share several aspects & objectives in each working group, e.g. channel models in RAN1, UE/RF assessment in RAN4
RP-12xxxx, supported by XX companies
  There is large support for this SID & there will be corresponding activity in multiple SA WGs
  It should be approved at RAN #58 to be able to start the work & meet its various requirements within Rel-12

## Slide 6: Proposed RAN Study Item (cont.)
D2D Discovery within network coverage SA: in scope of agreed SA1/SA2 WI RAN: in scope of proposed SI | D2D Communication within network coverage SA: in scope of agreed SA1/SA2 WI RAN: proposed that SI shall focus to public safety requirements at this stage
D2D Discovery outside network coverage for public safety only SA: in scope of agreed SA1/SA2 WI RAN: in scope of proposed SI | D2D Communication outside network coverage for public safety only SA: in scope of agreed SA1/SA2 WI RAN: in scope of proposed SI

## Slide 7: Thank you

## Slide 8: Annex: Objectives of SA1/SA2 agreed WI / SA1 part
The SA1 objective is to specify service requirements for:
ProSe Discovery over E-UTRA;
  within network coverage and
  outside network coverage, only for Public Safety
  Discovery within network coverage is limited to the cases under continuous operator network control. Continuous is intended to mean that any use of operator resources, including spectrum, from a specific UE needs to be authorized and fully controlled by the operator network at any time, based on operator choice.
ProSe Communication over E-UTRA;
  within network coverage and
  outside network coverage only for Public Safety
  Communication within network coverage is limited to the cases under continuous operator network control. Continuous is intended to mean that any use of operator resources, including spectrum, from a specific UE needs to be authorized and fully controlled by the operator network at any time, based on operator choice.
EPC support of ProSe Communication over WLAN.
  Direct control of the WLAN link is outside the scope of 3GPP. However, service requirements that enable the 3GPP EPC to provide network support for connection establishment, maintenance, and service continuity for WLAN direct communication are in scope. These shall have no impact on specifications under the responsibility of TSG RAN.

## Slide 9: Annex: Objectives of SA1/SA2 agreed WI / SA1 part (cont.)
Service requirements for ProSe Discovery and ProSe Communication will address:
  Continuous network operator control.
  Presence, group communication, broadcast services and relay
The requirements for Public Safety and non-Public Safety services shall be common whenever possible.
The service requirements generated by this work will not apply to GERAN or UTRAN.
  NOTES: For the purposes of this WID these two Proximity Services definitions are used:
  ProSe Discovery: a process that identifies that a UE is in proximity of another, using E-UTRA.
  ProSe Communication: a communication between two Ues in proximity by means of a communication path established between the Ues.
    The path for discovery and communication could for example be established
      directly between the UEs
      or network based, e.g.routed via local eNB(s).
It is required to include means for operator to apply regulatory requirements (including lawful intercept, as per regional regulation).

## Slide 10: Annex: Objectives of SA1/SA2 agreed WI / SA2 part
The SA2 objectives are as follows:
As part of the TR phase
  Define the architectural requirements (based on the Stage 1 normative requirements) in order to scope/guide the work in SA2;
  Develop solutions based on objective a); and
  Determine which solution(s) from the TR phase to document in normative specifications
Specify selected solutions in relevant specifications.