## Slide 1: Motivation for “Low cost & enhanced coverage MTC UE for LTE” Work Item
Vodafone Group
3GPP TSG RAN#60,
Oranjestad, Aruba, 11th – 14th June 2013
RP-130815

## Slide 2: High level view
Many MTC applications target low data rate, that can be handled sufficiently by GSM/GPRS networks with low modem development cost.
There is a need to make LTE the natural home for these applications, as otherwise:
  GSM/GPRS spectrum and network functions will need to be maintained longer
  Re-farming of spectrum to LTE will take longer
  Running more radio technologies leads to additional operational costs for the operator.
Due to the nature of MTC applications being autonomous (not necessarily located close to humans), ubiquitous geographical coverage is an important driver for wireless networks supporting MTC.
  New technologies are emerging that aim to offer a better service to MTC than GSM today.
Vodafone believes that it is important for LTE to maximise its ability to serve MTC applications, so that LTE operators can generate new revenue.
  Low cost LTE devices and enhanced LTE coverage will drive more MTC applications to use LTE.

## Slide 3: 3GPP status and proposed way forward
The study item on “Provision of low-cost MTC UEs based on LTE” showed that:
  Low cost device with Bill of Material Cost comparable to E-GPRS would be possible.
  Coverage improvement* of 20dB possible, but 15dB offers a good trade-off with other factors such as spectrum efficiency, UE power consumption (see proposed WID for more details).
PROPOSAL: Agree new work item to specify some or all of the techniques identified in outcome of the study item.
This will allow LTE to offer:
  A low cost LTE device type for MTC.
  15dB coverage improvement for low cost MTC and other MTC UEs for delay tolerant MTC applications.
    We believe that 15dB of improvement will significantly enhance the likelihood of LTE being selected instead of GSM and other technologies to provide MTC services.
We believe that the proposed Rel-12 work item will significantly enhance the ability of LTE as a technology to provide MTC services.
*Unlike for normal LTE MTC devices, for low cost MTC devices, the coverage is reduced by adding low cost techniques, so the improvement would be relative to that for those devices.

## Slide 4: Summary of core specification work in working groups
Impacts to RAN1:
  For low cost MTC UE aspects:
    Define new UE category and associated additional UE capabilities for cost reduction techniques.
    Possible design of new MIB with reduced system info to allow UE operation with reduced bandwidth for data and enhanced coverage.
  For fundamental coverage techniques:
    Define baseline techniques highlighted in WID.
    Define simplification of PHICH and PCFICH functionality or alternate mechanism for PHICH and PCFICH functionality such that coverage limited MTC UE is not constrained by PHICH and PCFICH physical channels.
    Define mechanism to identify delay-tolerant MTC UEs and their level of coverage, and possibly tune their configuration to trade-off coverage with spectrum efficiency impacts
  For complimentary coverage techniques to mitigate spectrum efficiency impacts:
    Consider the additional techniques in the WID.
Impacts to RAN2:
  Identify and specify any impact to RRC/PDCP/RLC/MAC procedures (ARQ procedures, retransmission timers, HARQ timing, scheduling request) caused by additional air interface delay due to repetitions on PUCCH/PUSCH/PDSCH in physical layer.
  Specification of signalling to configure the UE to use the new physical layer techniques.
  Input to SIB design and specification of related changes – if agreed in RAN1.
Impacts to RAN4 core requirements:
  EVM impacts of PSD and RS boosting on PDCCH/E-PDCCH.
  UE requirements will need to be defined for operation of Single Rx antenna. Impact on Rx sensitivity, and possible impact on other UE receiver requirements should be discussed – due to lower SNR at UE compared to 2 Rx). Also potential impact on RRM measurement requirements from single Rx antenna. Discussion on whether mobility requirements can be relaxed for low cost MTC UE.
  RRM measurement core requirements possibly impacted by modifications to System Info delivery (potential removal of some mobility-related info, or longer reception delays).

## Slide 5: Summary of performance specification work in working groups
Impacts to RAN4 performance requirements
  New UE demodulation requirements for UE configured with enhanced coverage features for:
    PDSCH reception
    P-BCH reception
    PDCCH/E-PDCCH reception
    Possibly DL ACK/NACK detection (depending on RAN1 agreements)
(Note that requirements for 1 Rx and 2 Rx UE would be needed for the above).
  New BS demodulation requirements (to handle UE configured with enhanced coverage features) for:
    PUSCH reception
    PRACH detection (Relaxed Pmissed detection requirement, possibly including reception of new RACH format).
    PUCCH detection.
  RRM performance requirements), which include RRM measurement accuracies and RRM test cases to verify any modifications to mobility requirements for MTC UEs with low cost and/or enhanced coverage.