## Slide 1: RP-130826 Motivation for Metropolitan Beacon System (MBS) for UTRA and LTE
High Precision Urban and Indoor Positioning across a Metropolitan Area

## Slide 2: Metropolitan Beacon System
The Metropolitan Beacon System is a Terrestrial based beacon system used to complement Global Navigation Satellite System (GNSS) for positioning in GNSS challenged environments of urban canyons and indoor locations

## Slide 3: Motivation for Metropolitan Beacon System
FCC issued the 2nd R&O in 2010 and the 3rd R&O in 2011. The R&O contained the following requirements:
  Required operators to comply with Phase 2 E911 dialing requirements from a national average to a county/PSAP level
  Tightened accuracy standards for network based technologies from 100m(67%)/300m(90%) to 50m(67%)/150m(90%)
It is estimated that 60%[1] of wireless calls in the US come from indoor locations, therefore the desire to find people in an emergency in indoor environments is only increasing.
  Annually over 150 million Emergency calls (E911)[2] are made in the US and over 70%[3] from Wireless devices
  FCC constituted a committee CSRIC III to study the problems of location in indoor environments during the emergency call (2011-2013)
  CSRIC III put together a national test bed with over 8 companies participating (Verizon, AT&T, T-Mobile, Sprint, Qualcomm, NextNav, Boeing and Polaris Wireless) to characterize the performance of various location technologies in indoor environments
  CSRIC III submitted a report to the FCC on the outcome of the test bed
  FCC is evaluating the report and is expected to base it’s policy on indoor location accuracy requirements on the basis of this report
The 2nd and 3rd R&O has created the need for higher accuracy systems in GNSS challenged areas immediately and the MBS solution is technically capable of meeting that need
[1]: JD Power and Associates 2012; [2]: National emergency Number Association (NENA); [3]: FCC

## Slide 4: Metropolitan Beacon System (MBS)
MBS Beacon
MBS Beacon
MBS Beacon
Cell phone
In urban canyon

GPS Satellite
Blocked!
Location Network Elements
Cell phone
Indoors
High Performance
GPS-like performance indoors and in urban environments
Accurate vertical position
Fast time to first fix
Wide Area Broadcast Network
Highly synchronized beacons, with deployment optimized for location
Broad coverage from minimal sites
Limited Receiver Impact
Reuse Digital baseband
On-device computation of location
Reduced power consumption
Limited Application and Core Network Impact
Designed to leverage existing elements with configuration to support NextNav information
MBS is a terrestrially-based positioning constellation, featuring significant technical commonality with GPS

## Slide 5: Features
MBS Network architecture effectively results in a terrestrial positioning constellation, featuring significant commonality with GNSS
  Timing-based system, using highly synchronized terrestrial transmitters for device-based trilateration
  Wide-area network architecture, providing consistent indoor service across coverage area
Carrier Grade, reliability and consistency across an entire metropolitan area in GNSS challenged environments
Air interface-agnostic system – allows for evolution of location technology independent of air interface
Unique height system results in 1 – 3m vertical precision
Operates in the 920MHz band in the United States
NextNav Air Interface ICD is available at: https://partner.nextnav.com/

## Slide 6: Features
System designed for minimal impact on mobile handsets and core network elements
  Re-use of GPS digital baseband
  Fits in with transport of existing location information derived from different positioning systems (e.g.:- GPS, Galileo, Glonass)
    For Instance:- Identical modes of operation as GNSS:
      Standalone  no assistance information provided to the UE
      Assisted Mode  with assistance information provided to the UE

## Slide 7: Communications Safety, Reliability and Interoperability Council Trials (“CSRIC”)
In 4Q12 the FCC’s CSRIC advisory group held a comprehensive, independent trial of location technologies for indoor E911 in the San Francisco / Silicon Valley area.
Joint effort by Public Safety, technology vendors and national wireless carriers. Results released March 2013
Urban
San Francisco
Financial District
Suburban
Santa Clara County
Rural
San Benito County

## Slide 8: CSRIC Test Protocol Review
CSRIC 3, Working Group 3 was chartered by the FCC with, among other things, creating an information base from which indoor location accuracy standards for E911 could be established
  WG3 consists of technology vendors, public safety representatives and the four major U.S. wireless carriers
Test program was performed by a 3rd party (TechnoCom), and was completely blind to participants
  Over 13,000 test calls for each participating vendor at 75 indoor test points per building (including deep building core)
  Test bias towards dense urban / urban (70% of test points)
Extremely rigorous test process, appropriate for mission-critical applications, resulted in some vendor attrition, with performance for all vendors impacted
  Warm start position fixes
  Consumer-grade receivers
Technologies tested in CSRIC Test Bed
  RF Fingerprinting
  Assisted GPS with Advanced Forward Link Trilateration (AGPS + AFLT)
  Metropolitan Beacon System (MBS)
Results published in March 2013: http://transition.fcc.gov/bureaus/pshs/advisory/csric3/WG3_Indoor_Test_Report_Bay_Area_Stage_1_Test_Bed_Jan_31%20_2013.pdf

## Slide 9: CSRIC Participants – WG 3
Organization
Bexar Metro 9-1-1 Network District
ATIS
Polaris Wireless, Inc.
Verizon Wireless
TeleCommunications Systems, Inc. (TSC)
Intrado, Inc.
Virginia Information Technologies Agency
US Cellular
CSR Technology Inc.
Qualcomm Inc.
APCO International
Nokia Siemens Networks
WG 3 Indoor Location Test Bed Subgroup consisted of the following members:
Organization
Motorola Mobility, Inc.
CommScope
Verizon Wireless
TechnoCom Corporation
Wiley Rein LLP
Sprint
NENA
T-Mobile
Time Warner Cable
CenturyLink
Applied Communication Sciences
Boeing
APCO International
Metro Emergency Services Board
NextNav LLC
True Position, Inc.
AT&T
Cassidian Communications
Over 30 technology companies, wireless operators and public safety entities participated in the process to evaluate location technologies over an 18 month process

## Slide 10: Comparison of MBS and AGPS System (with AFLT) in real world conditions – CSRIC Results
Chart: 
| Dense Urban | Urban | Suburban | Rural
MBS 67th percentile | 57.1 | 62.8 | 28.6 | 28.4
MBS 90th percentile | 102.4 | 141.1 | 52.9 | 44.9
A-GPS 67th percentile | 155.8 | 226.8 | 75.1 | 40.5
A-GPS 90th percentile | 267.5 | 449.3 | 204.8 | 210.1
Morphology
2D Accuracy (in m)
AGPS
MBS

## Slide 11: MBS Yield and TTF – CSRIC Results
 | Total Number of Test Calls Attempted | Total Number of Test Calls With Position Fix Returned | Percentage of Test Calls with Position Fix Returned (Yield)
All Dense Urban Buildings | 5174 | 4859 | 93.9%
All Urban Buildings | 4444 | 4238 | 95.4%
All Suburban Buildings | 3581 | 3581 | 100.0%
All Rural Buildings | 843 | 820 | 97.3%
 | Average Duration | Standard Deviation | 90th Percentile
All Dense Urban Buildings | 27.36 | 0.61 | 27.45
All Urban Buildings | 27.40 | 0.48 | 27.64
All Suburban Buildings | 27.39 | 0.52 | 27.52
All Rural Buildings | 27.56 | 0.35 | 27.86
Yield: Ratio of Number of Calls with Position Fix Returned/Total Number of Test Calls Attempted
Time to Fix: Time to Fix within the 30 sec timeout as specified by FCC Test Plan (OET-71)

## Slide 12: Public Safety Requirements from the CSRIC Report
Public safety expects that standardization, commercial availability and deployment of such [emerging] technologies are priorities for all stakeholder
Public Safety desires reliable and consistent caller location information to a specific dispatch-able building (and floor in multi-story environments)
Tighter performance [than 50 meter accuracy] is required, particularly in urban and dense urban environments to narrow the search ring to a single building or a more reasonable number of adjacent buildings
Lacking the specific building and floor, the desire would be for the smallest possible search ring

## Slide 13: Urban Search Ring Results
AGPS Based Solution
~200m
Location Solution Provider
~150m
MBS
~50m
“Horizontal position fixes that substantially exceed 50 meter accuracy provide only general location information…”
- from the conclusions of the CSRIC report
90% reduction in search
Area with MBS
Average Urban / Dense accuracy at 67% confidence level; source: CSRIC.

## Slide 14: MBS Specification Impacts LTE/LPP
MBS is defined as a GNSS positioning method
Changes required for MBS Standalone Mode
  The GNSS-ID IE is updated to add MBS.
  The GNSS-ID-Bitmap is updated to include MBS.
  The GNSS-SignalID and GNSS-SignalIDs IEs interpretation/explanation are updated to add MBS M1 signal.

## Slide 15: MBS Specification Impacts LTE/LPP
MBS is defined as a GNSS positioning method
Changes required for MBS Assisted Mode
  The GNSS-ID IE is updated to add MBS.
  The GNSS-ID-Bitmap is updated to include MBS.
  The GNSS-SignalID and GNSS-SignalIDs IEs interpretation/explanation are updated to add MBS M1 signal.
  The Generic-GNSSAssistanceDataSupportElement IE is updated to add a conditional MbsAssistanceSupport IE when the GNSS-ID indicates MBS in the LPP ProvideCapabilities message.
  The GNSS-GenericAssistDataReqElement IE is updated to add a conditional gnss-MbsAssistanceReq IE, when the GNSS-ID indicates MBS in the RequestAssistanceData message.
  The GNSS-GenericAssistanceDataElement IE is updated to add an optional gnss-MbsAssistance IE when the GNSS-ID indicates MBS in the ProvideAssistanceData message.
  The GNSS-SatMeasElement IE is updated to add an optional MbsMEasElement IE when the gnss-ID in the GNSS-MeasurementForOneGNSS indicates MBS in the ProvideLocationInformation message.

## Slide 16: MBS Specification Impact RRC
MBS is defined as a GANSS positioning method
Changed required for MBS Standalone Mode
  The GANSS ID is updated to include MBS and the coding of the GANSS Signal IDs is updated to include MBS in the UE positioning Capability IE in the UE Capability Information message.
  The GANSS Positioning Methods IE is updated to add MBS in the UE positioning reporting quantity IE in the UE positioning measurement IE in the Measurement Control message.

## Slide 17: MBS Specification Impact RRC
MBS is defined as a GANSS positioning method
Changes requires for MBS Assisted Mode
  The GANSS ID is updated to include MBS and the coding of the GANSS Signal IDs is updated to include MBS in the UE positioning Capability IE in the UE Capability Information message.
  The GANSS Positioning Methods IE is updated to add MBS in the UE positioning reporting quantity IE in the UE positioning measurement IE in the Measurement Control message.
  The UE positioning GANSS assistance data IE is updated to add a new optional UE positioning GANSS MBS assistance data IE when the GANSS ID in the GANSS Generic Assistance Data indicates MBS in the Measurement Control message.
  The coding of the GANSS ID is updated to add MBS in note 1 of the UE positioning GANSS assistance data IE.
  The GANSS measurement parameters is updated to add a new optional UE positioning GANSS MBS Measurements IE in the GANSS Signal Measurement Information when the GANSS ID indicates MBS in the UE positioning GANSS measured results IE in the UE positioning measured results IE in the Measurement Report message.
  The UE positioning GANSS additional assistance data request IE is updated to add a new optional GANSS MBS Assistance to the GANSS Requested Generic Assisted Data in the GANSS additional assistance data request IE in the UE positioning error IE in the UE positioning measured results IE in the Measurement Report message.
  The UE positioning GANSS assistance data IE updated to include the GANSS MBS assistance data IE may also be included in the Assistance Data Delivery message.
  The UE_POSITIONING_GANSS_DATA UE Variable is updated to add the UE positioning GANSS MBS assistance data IE.

## Slide 18: MBS Time Budget Requirements
RAN2
  R2#83 0.25J,
  R2#83bis 0.5L, 0.5U
  R2#84 0.5L, 0.5U
  R2#85 0.5L, 0.5U
RAN3
  R3#82 0.5U
  R3#83 0.5U
  R3#83bis 0.5U
RAN4
  R4#69 0.5U+L
  R4#70 0.5U+L
  R4#70bis 0.5U+L
  R4#71 0.5U+L

## Slide 19: Summary
The need for a complementary solution to GNSS systems is the highest now – especially for emergency calls and services, where a large percentage of calls originate in GNSS challenged environments. The Metropolitan Beacon System (MBS) solves that problem
MBS system designed to create minimal impact on existing GNSS based ecosystem and improves it’s performance
  Shares digital baseband with GPS and leverages existing AGNSS call flows
  Lower power consumption than GNSS
  Fast time to fix and Floor level information for indoor environments
  Metropolitan Beacon Systems brings “carrier grade” ubiquity, reliability and accuracy to GNSS challenged environments
MBS work item supported by many companies
  AT&T, Broadcom, Research in Motion, Telecommunication Systems, NextNav, CSR
The current MBS work item (Tdoc RP-130603) has Identical impact as Beidou (Tdoc RP-130416) approved at the last plenary
  Similar specification impact, similar work plan, and similar work group time unit allocation