## Slide 1: RP-130857 Motivation for Metropolitan Beacon System (MBS) for UTRA and LTE Study Item
High Precision Urban and Indoor Positioning across a Metropolitan Area

## Slide 2: Metropolitan Beacon System
The Metropolitan Beacon System is a Terrestrial based beacon system used to complement Global Navigation Satellite System (GNSS) for positioning in GNSS challenged environments of urban canyons and indoor locations

## Slide 3: Motivation for Metropolitan Beacon System
FCC issued the 2nd R&O in 2010 and the 3rd R&O in 2011. The R&O contained the following requirements:
  Required operators to comply with Phase 2 E911 dialing requirements from a national average to a county/PSAP level
  Tightened accuracy standards for network based technologies from 100m(67%)/300m(90%) to 50m(67%)/150m(90%)
It is estimated that 60%[1] of wireless calls in the US come from indoor locations, therefore the desire to find people in an emergency in indoor environments is only increasing.
  Annually over 150 million Emergency calls (E911)[2] are made in the US and over 70%[3] from Wireless devices
  FCC constituted a committee CSRIC III to study the problems of location in indoor environments during the emergency call (2011-2013)
  CSRIC III put together a national test bed with over 8 companies participating (Verizon, AT&T, T-Mobile, Sprint, Qualcomm, NextNav, Boeing and Polaris Wireless) to characterize the performance of various location technologies in indoor environments
  CSRIC III submitted a report to the FCC on the outcome of the test bed
  FCC is evaluating the report and is expected to base it’s policy on indoor location accuracy requirements on the basis of this report
The 2nd and 3rd R&O has created the need for higher accuracy systems in GNSS challenged areas immediately and the MBS solution is technically capable of meeting that need
[1]: JD Power and Associates 2012; [2]: National emergency Number Association (NENA); [3]: FCC

## Slide 4: Metropolitan Beacon System (MBS)
MBS Beacon
MBS Beacon
MBS Beacon
Cell phone
In urban canyon

GPS Satellite
Blocked!
Location Network Elements
Cell phone
Indoors
High Performance
GPS-like performance indoors and in urban environments
Accurate vertical position
Fast time to first fix
Wide Area Broadcast Network
Highly synchronized beacons, with deployment optimized for location
Broad coverage from minimal sites
Limited Receiver Impact
Reuse Digital baseband
On-device computation of location
Reduced power consumption
Limited Application and Core Network Impact
Designed to leverage existing elements with configuration to support NextNav information
MBS is a terrestrially-based positioning constellation, featuring significant technical commonality with GPS

## Slide 5: Study Item Objective
The objectives of this study item are to
  Evaluate the performance of MBS positioning in LTE
    Specifically: location accuracy, yield, and time to fix
    The LTE evaluation will utilize real world results and simulation data as applicable
    MBS performance will be evaluated against an internationally recognized standards for positioning, such as the E911 mandate of 50m – 67% and 150m – 90% of the time
  Evaluate the performance of MBS positioning in UTRA
    Specifically: location accuracy, yield, and time to fix
    The UTRA evaluation will utilize real world results and simulation data as applicable
    MBS performance will be evaluated against an internationally recognized standards for positioning, such as the E911 mandate of 50m – 67% and 150m – 90% of the time
  Asses Protocol and Interface impacts for LTE and UTRA
  Produce Technical Reports for MBS performance and Protocol impacts in UTRA and LTE
Technical Reports presented to RAN#63 for Information and RAN#64 for Approval

## Slide 6: MBS Study Item Time Budget Requirements
RAN4
  R4#68bis 0.25 RRM & Demod
  R4#69bis 0.5 RRM & Demod
  R4#70 0.5 RRM & Demod
  RAN#70bis 0.5 RRM & Demod