## Slide 1: NAICS Way Forward
RP-140058
ATT, Sprint, Verizon, Qualcomm Incorporated, Huawei, HiSilicon, MediaTek, Samsung
3GPP RAN #63
Fukuoka, Japan
March 3-6, 2014
Agenda: 14.1.4

## Slide 2
Extensive studies of intra-cell and inter-cell interference mitigation with advanced UE receivers have been conducted in the last 12 months in RAN1 and RAN4.
For inter-cell interference cancellation, the study item concluded the following (TR 36.866):
  Higher-layer signaling of parameters related to interference PDSCH could be beneficial to reduce the blind detection complexity or performance degradation.
    The list of candidate parameters for higher-layer signaling have been identified.
    The list of parameters that are desirable for UE blind detection (possibly from a reduced subset of all values) have been identified.
    Potential CSI enhancement should be investigated
  Blind detection for some parameters was found acceptable in terms of complexity and performance in some cases (based on SL-IC and R-ML receivers)
    Blind detection of PDSCH ON/OFF if other parameters are known
    Blind detection of modulation order if other parameters are known
    Blind detection of DM-RS port 7 and 8 and modulation order if other parameters are known
    Blind detection of RI for CRS-based TM if other parameters are known
    Blind detection of PMI rank 1 with 2Tx for CRS-based TM if other parameters are known
  Exact combination of parameters to be detected and subset restrictions are FFS
For inter-stream interference cancellation, advanced SU-MIMO receiver based on IC/ML without network assistance can provide significant gains compared to Rel-11 (36.866, section 8.2.4.2).
NAICS Study Item Findings

## Slide 3
In order to provide UE receiver enhancements to operators within Rel-12 time frame, two work items should be approved
  RAN1-led NAICS work item on SL-IC and R-ML receivers for inter-cell interference cancellation targeting low to medium SINR UEs
  RAN4-led SU-MIMO work item on advanced receivers for inter-stream interference cancellation targeting medium to high SINR UEs
Way Forward

## Slide 4
Way Forward
Realistic objectives should be defined such that
  All RAN1/2 tasks for the NAICS work item could be completed by RAN #65 (Sept 2014)
  The performance part of both work items could be completed by RAN #68 (June 2015)
Further enhancement to UE receivers could be considered in Rel-13 after the Rel-12 advanced receiver activities are completed in the same working group.

## Slide 5
Appendix
Latest TR is embedded below